DJ160.3 
     The fifth digit is REWRITTEN whenever the radio receives a proper group or
personal page code, and will display personal code number that was received.   It
is transmitted only when the radio is in GP DSQ mode.  It is NOT transmitted when
the radio is in DSQ or G DSQ modes.  See below.
 
     To set the DSQ number, push [f] [DSQ set], enter five numbers, then push
[V/M].
 
 
     NOTE:  In the examples that follow, I will assume you have programed the
code 123.4.5 into your DSQ using the DSQ set function.
 
 
          (a) DSQ Squelch Operation:
     Receive Mode:   DSQ squelch is used to cause the radio to be silent
(squelched) while in receive until it receives a three digit code.  IF it
receives the correct three digits during the first second or two of a
transmission, it will release the squelch and the receive the rest of that
transmission.
     Transmit Mode:  When used to transmit, the radio will automatically transmit
the three digit DSQ group code right after you press the [PTT] button, so
remember to pause a moment before talking if using the radio in DSQ mode.
 
     To set DSQ Squelch, push [f] [GP DSQ] until DSQ is displayed.   Be sure that
ONLY DSQ is displayed, not G DSQ or GP DSQ.  Normally, if you start with no DSQ
display, hitting [f] [GP DSQ] once will cause DSQ only to be displayed.
 
 
     Summary of DTMF Squelch function:
 
Receive:   Radio remains squelched unless it receives the tones 1,2,3
 
Transmit:  Radio transmits the tones 1,2,3  whenever [PTT] is pressed.
 
  (you must hold down the PTT button throughout your transmission.  If you let go
of the PTT button, you must re-transmit the three digit code if you want the
receiver to hear you!  This is not a problem when using one DJ160 with another,
but can be if you are using the DJ160 with a different radio where manual entry
of the DTMF tones is required)
 
     NOTE:  If using another radio to manually send DTMF squelch codes, the three
digits must be punched in within a space of 1.5 seconds total.
 
 
         (b) DTMF page function:
     This mode is set using the [f] [GP DSQ] buttons.  Hold down the [f] button
and press the [GP DSQ] button until G DSQ or GP DSQ is displayed.  G DSQ stands
for group page mode, and GP DSQ stands for personal page mode.  Normally if no
DSQ function is displayed, you hold down the [f] key and press the [GP DSQ] key
once to display DSQ, twice to display G DSQ, three times to display GP DSQ, and a
fourth time to clear the DSQ function from the display.
CONTINUED IN DJ16OT.4 
DJ160T.5 
         Personal Paging:
 
     This is a somewhat complicated variant of group paging, used to page a
particular person in a group.  Not only is it complicated, but the implementation
on the Alinco DJ 160T differs from that used on some other radios, for the Alinco
uses a single digit personal code where other radios sometimes use a three digit
personal code.  Generally I recommend users not bother with this overly
complicated feature, but I will attempt to at least partially document it here.
Its primary use where you have a party of several individuals all with the same
group but different personal paging codes.  In this situation one can either page
all members of the group using the group page function OR page a given individual
member of the group using the personal page function.
 
     Receive:  The radio may be set to display either "G DSQ" or "GP DSQ".  This
is done using the [f] [GP DSQ] buttons.  If the three digit group code followed
by a single digit personal code followed by a star is received (1,2,3,4,*), the
unit will make the "personal page type" tone (beep boop), the "GP" in the display
will flash, and "Err" will be displayed on the main display.  The "Err" is
displayed because a personal identifier digit was not sent.  If in addition to
the above codes a personal identifier code is received (1,2,3,4,*,7) the radio
will make the personal page type beeping and "GP" will flash.  In addition, the
last digit of the DSQ code will be re-written to 7, to reflect the fact that a
page FROM the person with code number 7 was sent.  Pushing [V/M] button will stop
the flashing of the "GP" in the display.
 
     Transmit:  (Pay CLOSE attention here!  The radio uses the numbers in its DSQ
SET significantly differently when transmitting in GP DSQ mode than it does when
in G DSQ mode!)   Radio MUST be in GP DSQ mode (NOT G DSQ mode) to properly
automatically transmit a personal DTMF page.  Let us assume that you have set
your DSQ code to 123.4.5.  When the [PTT] button is pressed, the radio will send
the following tones:  1,2,3,5,*,4.
CONTINUED IN DJ16OT.6 
DJ16OT.6 
     The first three tones sent are the group code.  This is followed by personal
code of the person you want to PAGE.  Then a star is sent, then YOUR personal
code is sent as an identifier.  Note carefully that it is the FIFTH (last) digit
of the five digit DSQ number that is sent as the FOURTH digit of the DTMF
transmission when you are in GP DSQ mode!  Note too that this last digit is
rewritten every time you RECEIVE a page, so if you want to send a personal page
to someone OTHER THAN the person who paged you last, you must use DSQ SET to
rewrite the last digit of your five digit code to specify the personal code digit
of the person you want to page.  Alternatively, note that when you enter GP DSQ
mode by pressing [f] [GP DSQ] three times, the five digit code is displayed.  At
this point, entering a SINGLE digit will usually cause the fifth digit to be
changed to whatever you want it to be.  Pressing [f] [GP DSQ] a fourth time will
put the radio in GP DSQ mode, removing the display of the five DSQ code digits.
If no code is entered when the GP DSQ display of the code is called up, after
about 5 seconds the display will automatically revert to the normal radio display
with GP DSQ set.  Alternatively, you can reset the entire DSQ display using the
[f] [DSQ set] button combination.  In any case, when using the GP DSQ (personal
page) function, you must each time check the code to make sure you have set the
personal and group code correctly.  Be especially careful that the outgoing
personal code (last digit of the display) is correct for the person you want to
page.
 
 
     Summary of DSQ Code digits:
 
  123.4.5    in display
   a  b c
 
    a  Three Digit Group Code.
         DTMF Squelch:
 (receive mode) These three digits must be received to break squelch when DTMF
squelch (DSQ only displayed) is used.
 (transmit mode) These three digits only are transmitted when in DSQ mode upon
pressing the [PTT] button.  example:  if you have set 123.4.5 as your DSQ code,
when you press [PTT] in DSQ mode 1,2,3 will be transmitted.
 
         Group and Personal Page functions:  These three digits are used as the
group code in both group and personal paging functions and are the first three
digits transmitted as part of a larger group or personal page code transmission.
They are the first three digits that MUST be received when trying to activate a
group or personal page.  See below for more details.
 
 
    b  This is YOUR personal page code.
         DTMF Squelch:  This digit IS NOT USED in DTMF squelch functions.
CONTINUED IN DJ16OT.7
DJ16OT.4 
     Receive Mode:  In this mode, the radio is silent until it receives the
proper page tone sequence.  At that point, it will beep in a fashion that is
characteristic of either receipt of a group page or of a personal page.  The tone
for a group page consists of several dual beeps, with all beeps being of the SAME
tone.  eg:  beep beep      beep beep     beep beep    etc.
The tone for a personal page consists of several dual beeps, but the two beeps
within each dual beep are of different frequencies.  eg:  beep boop     beep boop
beep boop   etc.
 
     NOTE:  The radio behaves EXACTLY the SAME when in either G DSQ or GP DSQ
modes when it is RECEIVING.  The two modes (G DSQ and GP DSQ) differ ONLY in
terms of what tones get transmitted when you push the [PTT] button!!  I recommend
you use only the G DSQ mode, for it is simpler to understand.  But I will attempt
to shed some light on the GP DSQ mode too.
 
      Group Paging:
 
      Receive:   (Radio may be set to either G DSQ or GP DSQ)  Radio must receive
group code (1,2,3) followed by a star (*) at a minimum in order to produce the
pager tone.  If the radio receives ONLY the three digit group code followed by a
star (1,2,3,*) it will give the group page beep, the "G" in the G DSQ of the
display will flash, but "Err" will be shown in the main display because the
personal code was not properly sent.  If the radio receives a group code followed
by a star followed by a personal code OR a group code followed by a star followed
by a personal code followed by two stars (1,2,3,*,4) or (1,2,3,*,4,*,*)  it will
give the beep for receipt of a group page, the "G" on the display in the G DSQ
will flash, AND, if you press [f] [DSQ set] the fifth digit displayed will be the
personal code that was just received (4 in this case).   If the unit was set for
123.4.5 in the DSQ SET mode, that display will be altered to 123.4.4 to reflect
the fact it received a "4" as a personal code digit.  After a page is received
and the "G" in the display is flashing, pushing [V/M] button once will cause the
G to stop flashing.
 
 
     Transmit:  The DJ 160T must be in G DSQ mode to properly transmit a group
page (not in GP DSQ mode).   Pressing the [PTT] key will automatically send out
the group code, followed by a star, followed by your personal code (fourth digit
in the DSQ set display), followed by two stars  (1,2,3,*,4,*,*).
CONTINUED IN DJ16OT.5
DJ16OT.8
         Group paging:
 (receive mode)  This digit is re-written any time a proper group page is
received to reflect the number of the other party who sent you the page.
example:  you have 123.4.5 in your DSQ setting and you now receive a group page
consisting of 123*8**  (or one simply consisting of 123*8).  Your pager will make
the group page type beep, "G" will flash in the display, AND, if you go to DSQ
set mode, you will see that the last digit of the code displayed is now NOT a 5,
but is instead an 8, informing you that "person number 8" was the originator of
that group page.  Thus, if your page code WAS set to 123.4.5 and you receive the
group page 123*8**, when you now press [f] [DSQ set] you will no longer see
123.4.5 but instead see 123.4.8.
 
 (transmit mode)  This digit is NOT USED in group page transmit mode.
 
        Personal paging:
 (receive mode) This digit is re-written any time you receive a valid personal
page, and will display the personal code of the person who sent that page.
example:  you have 123.4.5 as your DSQ code, and you receive the following
sequence:  1234*7   Your pager will now make the personal page type beep, "GP"
will flash on the display, and if you press [f] [DSQ set] you will no longer see
123.4.5 displayed, but instead will see 123.4.7.   The last digit reflects the
fact you received a personal page from a person whose own personal code is 7.
 
 (transmit mode) This is the digit that is sent out FOURTH when you push the
[PTT] button.  It specifies which person in the group will receive the personal
page.  You must be careful to set this digit correctly for the person you in the
group who you wish to page, keeping in mind that this digit gets re-written every
time you receive a page of any kind!  If you have 123.4.5 set as your DSQ code,
pressing [PTT] in GP DSQ mode will cause 1,2,3,5,*,4 to be transmitted.  Note
very carefully that this, the fifth digit in your DSQ setting display, is sent
out FOURTH when you are in GP DSQ mode and press the [PTT] button!
 
CONTINUED IN DJ16OT.9

DJ16OT.7 
         Group Paging:
 (receive mode)  this digit IS NOT USED in group paging receive mode.   ONLY the
first three digits and the last digit are used when receiving a group page.
 
 (transmit mode) When you press [PTT] in G DSQ mode, first the three digit group
code is sent, then a star, then this digit (your personal page code) is sent
followed by two stars (1,2,3,*,4,**).  Thus, this digit is the digit that is SENT
OUT TO OTHERS to identify to them who has sent the page.  It will be displayed in
the fifth digit of the DSQ code display on all radios that received your group
page, to identify you as the one who sent the page.
 
 
         Personal Paging:
 (receive mode) this digit specifies what "other party code" must be sent by
someone trying to page you personally.  In order to receive a PERSONAL page, your
radio must receive the group code followed by this digit followed by a star
(1,2,3,4,*).   Preferably you should receive all that PLUS an additional single
digit that identifies who was sending you the page (1,2,3,4,*,N  where N is a
single digit that identifies the person who sent the page).   If this last
identifier digit is not sent, you will hear a personal page type beep, and "GP"
will flash, but "Err" will be on the main display indicating that a personal
identifier code was not received.
 
 (transmit mode) This is the digit sent out LAST when you press the [PTT] button.
It identifies YOU as the person sending the page.  example:  with DSQ set to
123.4.5  if you press [PTT]  1,2,3,5,*,4  will be sent.   The 4 is received and
displayed as the last digit of the DSQ code on all radios that received your
page.
 
 
     c This is the single digit code for "the other party".
         DTMF Squelch:  This digit is NOT USED in DTMF squelch functions.
 
CONTINUED IN DJ16OT.8 
 
DJ16OT.9
 
     DTMF Wild Card function:
 
     If you forget a squelch or paging code, you can pick up and decode codes
sent by others.  Use [f] [DSQ set] to set DSQ first to 000.0.0 and then set it to
###.0.0.  (upside down A's will be displayed instead of #'s).
Now set your radio to G DSQ mode.  If you receive ANY valid page, the radio will
beep.  Press [f] [DSQ set] and the ###.0.0 display will be replaced by the page
code you just received.
 
 
 
     DTMF Decode function:
 
     At any time, any codes received will be decoded and kept in the M3 dialing
number.  Thus, any time you hear a bunch of DTMF codes on the air, you can press
the [Dial Ch] button, then rotate the top selector know so that M3 is displayed,
then use the up and down arrow buttons (* and #) to scroll the display right (up
arrow) or left (down arrow).  Up to 16 digits will be retained.  You can also set
the radio to DSQ mode while lying in wait to receive DTMF tones.  That way, the
radio will break squelch when it has received three or more DTMF tones, alerting
you to the fact it has captured a code.   Note: according to the manual, you must
have phone numbers stored in one or both dial memories (M1 and M2) for the decode
to work.  But in my experience that does not seem to be required by my unit.

END OF SERIES.