DR112.1 
STEP 10- REPLACE LITE UNDER POWER SWITCH, REMEMBER TO
         USE THE BLUE COVER OVER THE NEW LITE AS WELL
         AS THE YELLOWS SLEEVES ON WIRES. THIS LITE
         YOU SOLDER FROM THE FRONT.
 
STEP 11- REPLACE 3 LITES THAT ARE ABOVE THE MICRO SWITCHES
         ON THE FRONT OF THE PCBOARD. THIS WILL HAVE
         TO BE UN-SOLDER FROM THE BACK. ALSO REPLACE THE BLUE
         COVERS OVER THE 3 LITES.
 
STEP 12- REPLACE 2 LITES THAT STICK THROUGH HOLES THAT
         GO WHERE THE LCD DISPLAY IS, ALSO REPLACE THE
         YELLOW SLEEVES. THESE LITES SOLDER FROM THE BACK.
 
STEP 13- RE-INSTALL THE LCD DISPLAY AND BE SHURE THERE IS
         NO CONTAMINATION OF THE CONTACTS ON THE BOARD AND
         LCD DISPLAY. BE SHURE TO RE TWIST THE TABS ON THE
         DISPLAY THAT GOES THROUGH THE PC BOARD. THIS DISPLAY
         MUST BE TIGHT TO THE PC BOARD OR THE DISPLAY WILL
         NOT WORK EITHER WITH MISSING LCD SEGMENTS ON OR
         NO SEGMENTS ON. THIS LCD DISPLAY SHOWS THE FREQ.
         SIGNAL STRENGTH, CHANNEL NUMBER, AND OTHER FUNCTIONS.
 
STEP 14- TEST THE DISPLAY BY POWERING UP THE RADIO. IF YOU
         ARE GETTING MISSING NUMBERS, PULL THE LCD DISPLAY
         AND CLEAN THE CONTACTS ON THE PC-BOARD AND THE
         DISPLAY. I DID BY SCRAPPING THE PC BOARD WITH A
         SCREW DRIVER AS WELL AS THE LCD DISPLAY CONTACT
         RIBBON.
 
STEP 15- ASSEMBLE THE RADIO AND CHECK THE DISPLAY AT EACH
         MAJOR ASSEMBLY POINT.
 
STEP 16- RESET THE CPU AS SHOWN IN YOUR OWNERS MANUAL. THIS
         IS BECAUSE THAT THE CPU IS LOCATED ON THE BOARD
         YOU WERE WORKING ON AND MAY HAVE SOME BAD DATA AFTER
         WORKING ON THE RIG. YOU MAY HAVE TO RESET THE CPU
         WHEN YOU TEST THE RIG IN ORDER TO SHOW THE
         FULL LCD DISPLAY
 
   ANY QUESTIONS CAN BE SENT TO ME AT MY HOME BBS AND I WILL TRY
TO ANSWER THEM TO THE BEST OF MY ABILITY.
 
   THANKS AND 73'S
 
FRANK N2JYG @ WA0PTV.#WNY.NY.USA.NOAM
SYSOP OF THE "GLIDA NODES" IN SHERMAN NY
 
SYSOP OF HIGHLAND BBS IN SHERMAN NY 300-9600 BAUD USR-HST, V.32
V.42 AND NMP5/ AS WELL AS MY FAX NO. VIA A FAX SWITCH (716) 761-6460 
 
A SPECIAL NOTE: I HAVE HAD AN ALINCO DR-110 FOR THE LAST SEVERAL
YEARS ON THE SHERMN <N2JYG-3> NODE F LOACATED IN SHERMAN NY
AND IT KEEPS ON TICKING EVEN WHEN THE STORMS ROLL THROUGH. AS WELL AS
A DR-410 AND NO PROBLEM, EXCEPT FOR THE LED LITES....OH WELL !!!