# Text boxes

+

+

+

+

RF ATTEN

# TX TUNE

RX TUNE

AUDIO

KEY

ANT

13.8 VDC

+

+

+

+

+

+

+

39.2

39.0

38.8

38.6

38.5

39.3

38.9

38.6

39.2

39.3

39.7

39.5

38.2

35.2

37.0

The SMK-1was available from the NorCal QRP Club.  Although the kit is no longer available, information on the kit and mods can still be found on the NorCal QRP Club web site:  http://www.fix.net/~jparker/norcal.html

Once in a while, an unbuilt kit will show up for sale on QRP-L or at a hamfest.

I mounted my SMK-1in a Radio Shack enclosure (#RSU11907664). Standoffs were used to mount the circuit board to the top panel and  instead of mounting the control pots directly on the circuit board, they were mounted on the panel and wires run to the board.

The following hardware was mounted on the front panel:

ANT Jack: Radio Shack #274-346 panel-mount phono (RCA) jack.

KEY Jack: Radio Shack #274-346 panel-mount phono (RCA) jack.

Audio Jack: Radio Shack #274-246 – 1/8” panel-mount phone jack.

13.8 VDC: Radio Shack #274-1563 panel-mount coaxial DC input jack.

Control Knobs: Radio Shack #274-415 – ¾” hexagon control knob.

The frequency markings for the RX TUNE and TX TUNE controls may need to be adjusted for your rig.  Power it up and check it out before applying the final label to the panel.

NOTE:  Delete this text box before printing and you will have room to

print another label on the same sheet.