# Text boxes

## BATTERY

SOLAR

PANEL

I obtained the Micro M+ solar charger circuit board fully assembled and tested from SunLight Energy Systems:  http://www.seslogic.com/

I mounted the circuit board on a piece of plywood, which was then hot glued inside a Radio Shack enclosure (#RSU11907664). The plywood was necessary to shim the circuit board so the LED would be at the proper height to protrude through the top panel.  I located the circuit board so the LED would be centered in the “Sun” on the panel label.

The following were mounted on the front panel:

Solar Panel Jack: Radio Shack #274-1563 - panel-

mount coaxial DC input jack.

Battery Jack: Radio Shack #274-718 – chassis-mount

dual female binding post.

Use the panel hardware that suits your power supply needs and adjust the label accordingly.

NOTE:  Delete this text box before printing and you

will have room to print another label on the

same sheet.