## 2C39
High-Mu Power Triode

### Data Source and Substitute Data

Prefered Substitutes .......................... None

Substitutes ................................... None

### Mechanical Data

Bulb .......................................... Special
Base

.......................................... Metal & Ceramic
Maximum

Overall Length ...................... 2.750 Inches
Maximum Diameter

............................ 1.260 Inches
EIA Base

...................................... 2C39B

### Electrical Data

Heater Characteristics
Heater Voltage

................................ 6.3 Volts
Heater Current

................................ 1.1 Amperes

### Direct Interelectrode Capacitances (approx)

Triode
Input .........................................

6.5 pf
Output ........................................ 0.03 pf
Grid to

Plate ................................. 1.95 pf

### Maximum Ratings (Design Center Values)

Triode
Plate Voltage .................................

1000 Volts
Plate Dissipation ............................. 100 Watts

### Characteristics and Typical Operation

GIC
Plate Voltage ................................. 600

Volts
Grid No. 1 Voltage ............................ -35 Volts
Grid No. 1

Current ............................ 40 Ma.
Plate Current (Zero Signal)

................... 60 Ma.
Driving Power .................................

5.0 Watts
Power Output (approx) ......................... 20 Watts

Searched 19953 records on 3582 tubes, 1 match.

Haut du formulaire

Please enter the tube number:

This database contains data on thousands of tubes. Every effort has been made to insure the accuracy of this reference, however, I assume no liability for the results of using information contained herein. Other Tube Search Engines: 
Duncan Amps 
Frank's Electron Tube Pages 
KBApps partial 195X RCA Receiving Tube Manual 
OPCOMs 1959 Sylvania Tube Manual 
OPCOMs 1943 and 1949 Sylvania Tube Manual

Bas du formulaire

(c) 1995-2003 by NJ7P

NJ7P/Thu Aug 14 02:27:17 2003