Button 1 - Display

Cycles through display modes.

UTC Time

Shows Universal Coordinated Time in 24-hour format.

Rotating hand shows 1/8ths of second.

Local Time

Shows local zone time in 12-hour format.

Includes daylight savings time correction.

Rotating hand shows 1/8ths of second.

Latitude

Shows latitude in degrees, minutes, seconds.

Last character will show the site survey status:

‘ ‘: No survey

‘s’: Survey in progress

‘h’: Survey complete, position hold

Longitude

Shows longitude in degrees, minutes, seconds.

Last character will show the site survey status:

‘ ‘: No survey

‘s’: Survey in progress

‘h’: Survey complete, position hold

Master status

If an external device is communicating with Oncore via the RS-232 port, clock will switch to SLAVE status.

Reverts to MASTER status after 90 seconds of serial inactivity.

Button 2 - Menu

Cycles through available menus.

When Display (button 1) is pressed, returns to previously selected display mode.

Time zone change

Use Select (button 3) to select time zone.

To make selection permanent, commit with 2+3 combo.

Message will confirm commitment to EEPROM.

Error log

Errors accumulated in EEPROM and are not erased on startup.

On entry, will display the number of errors logged.

Errors can be cycled through with Select (button 3).

For each error, 20 decimal digits will be displayed.

First 10 digits are the internal clock time the error was logged

Format: MMDDhhmmss

If this is a time mismatch error, the second 10 digits will be the Oncore time.

Format: MMDDhhmmss

There must be 5 mismatches in a row before the error is logged, after which the internal clock will be re-synchronized.

Timer mismatch errors are suppressed for the first minute after startup.

If this is any other error, the second 10 characters will be repeating and indicate the error code:

4444444444

Timer 1 (1PPS) timer overflow

5555555555

Serial receive framing error

6666666666

Serial receive overflow error

7777777777

T1 (1PPS) edge out of phase with internal scheduler

Reset the entire error log with 2+3 combo.

Satellite status

Use Select (button 3) to cycle between lines

First line shows number of satellites tracked and DOP (Dilution of Precision) from 0 to 99.9

DOP will be 000 when site position is fixed

Subsequent lines will show status of receiver channels

Channel number (1 through N)

GPS satellite ID number (eg: Sat7)

Channel tracking mode (eg: m8)

0: code search

1: code acquire

2: AGC set

3: preq acquire

4: bit sync detect

5: message sync detect

6: satellite time available

7: ephemeris acquire

8: available for position

Satellite carrier to noise density ratio (s0-255 dB-Hz)

Channel status flags (‘d’ followed by two hex digits)

Bit 7: using satellite for position fix

Bit 6: satellite momentum alert flag

Bit 5: satellite anti-spoof flag set

Bit 4: satellite reported unhealthy

Bit 3: satellite reported inaccurate

Bit 1: using satellite for time solution

Bit 0: parity error

CPU clock frequency

Accuracy +/-64Hz

Oncore Identity

Use Select to cycle between lines of Oncore ID message.

Lines longer than display will scroll back and forth automatically.

Not available in SLAVE mode.

Site location survey

Asks if you want to start site survey.

Use 2+3 combo to initiate survey.

Survey takes several hours to complete.

Not available in SLAVE mode.

Oncore Self-test

Use 2+3 combo to start self-test.

Will usually result in errors being logged.

Not available in SLAVE mode.

Button 3 - Select

Used to select between options in Menu.

See individual Menu states for details.

Combo 1+2 - Audible Tick Toggle

Turn simulated WWV sounds on/off.

Combo 2+3 - Commit

Used to commit menu options.

See individual Menu states for details.

Combo 1+3 - Dial Sync

Activate when dial second hand is straight up.

Dial will freeze until the start of the next minute.