Alternate FT1000Mark_ V_Field  disassembly procedure.

Written and illustrated by  Bill W2PKY

Remove 10 screws from the rear panel.

Remove screws from the CAT socket.

Remove 2 screws holding the RF Amp in place. Use a magnetic tool to help with the recessed screws.

RF Amp heat sink side view.

Remove 2 more screws on the outside of the chassis holding the RF Amp assembly in place.

Remove the RF Amp module and rest on the edge of the back panel. Notice the fan on the right side of the chassis.

There is a screw at the top of the board out of the picture.

After the RF Amp is out of the chassis and the left side of the rear panel is pulled away from the chassis; Notice the clearance of the RCA jacks. Disconnect the ribbon cable circled in red. Remove 4 screws and the tin shield around the RF circuit board. The RF circuit board can now be flipped over for modification.

When reassembling be careful to avoid pinched wires in this area.