## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: General Licensing Class Chapter 11
Your Receiver
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 6
Your Receiver
The simplest combination of stages that implement a superheterodyne receiver is HF oscillator, mixer, detector. (G7C07)
Simple Generic Superheterodyne Receiver
6

## Slide 7: Your Receiver
Simplest combination
HF oscillator
mixer
detector

## Slide 8
Mixer
(In AM Broadcast
Receiver)
Signal B
At 1255 kHz
(or at 1655 kHz)
Signal C
At 455 kHz
Intermediate Frequency
Local
Oscillator
Signal A
At 800 kHz
(or at 1200 kHz)
Station Signal
7
Your Receiver

## Slide 9: Your Receiver
A mixer is the circuit used to process signals from the RF amplifier and local oscillator and send the result to the IF filter in a superheterodyne receiver. (G7C03)
IF Amplifier Stages
Single conversion receiver
Dual conversion receiver
8

## Slide 10
Your Receiver
Intermodulation is a process that combines two signals in a non-linear circuit or connection to produce unwanted spurious outputs. (G8B12)
  In a receiver, intermodulation is necessary and desirable; it makes frequency conversion work.
  Undesirable when a strong station mixes with a weaker one in the receivers front end.
The circuits used to combine signals from the IF amplifier and BFO is a Product Detector and sends the result to the AF amplifier in a single-sideband receiver (G7C04)
9
Your Receiver

## Slide 11
In a receiver the Mixer stage combines a 14.250 MHz input signal with a 13.795 MHz local oscillator signal to produce a 455 kHz intermediate frequency (IF) signal. (G8B01)
  A Mixer circuit is used to process signals from the RF amplifier and local oscillator and send the result to the IF filter in a super heterodyne receiver.
In this mixer the output is the sum and the difference of the two applied signals:
The sum would be 14.250 + 13.795 or 28.045 MHz
The difference would be 14.250 - 13.795 or 0.455 MHz
Filtering removes the undesired frequency
Mixer
First IF amp.
Local oscillator 13.795 MHz
14.250 MHz
455 kHz
11
Your Receiver
Heterodyning is another term for the mixing of two RF signals. (G8B03)
Very simple mixer
Your Receiver

## Slide 12
Your Receiver
Recap of block diagram of dual conversion receiver.
Pass band functions.
Amplifies signals.
Process signals.
Pass band and amplification
Receiver can more finely tune in the desired frequency.
Pass band and amplification
Recovers info as in modulation
Amplifies audio recovered from demodulator.
With mixer changes frequency of signal.
11

## Slide 13
Your Receiver
A high-stability variable frequency oscillator in a transceiver is a typical application for Direct Digital Synthesizer. (G7C16)
  Without these highly stable oscillators, your frequency would waltz across the band or jump randomly around the band.
Variable frequency with the stability of a crystal oscillator is a major advantage of direct digital synthesizer (DDS). (G7C05)
  Digital work on the air with tolerance down to 1 Hz keeps your signal stable on a frequency making reception of the digital signal more reliable.
The term “software-defined radio” (SDR) means a radio in which most major signal processing functions are performed by software. (G7C11)
  Software-defined radio (SDR) is a radio communication system where components that have been traditionally implemented in hardware (e.g. mixers, filters, amplifiers, modulators/demodulators, detectors, etc.) are instead implemented by means of software on a personal computer or embedded system.
13
Your Receiver

## Slide 14
Your Receiver
An advantage of using I and Q signals in software-defined radios (SDRs) is that all types of modulation can be created with appropriate processing. (G7C10)
14
A software defined radio is one that can be configured to any radio or frequency standard through the use of software. ...
An SDR is a radio communication system where components that have typically been implemented in hardware such as mixers, filters, amplifiers, modulators, detectors, are instead implemented in software.
Software Defined Radio (SDR)
Your Receiver

## Slide 15
Your Receiver
There is a 90 degree phase difference between the I and Q signals that software-defined radio equipment uses for modulation and demodulation. (G7C09)
The combination of a mixer’s Local Oscillator (LO) and RF input frequencies produce the sum and difference in the output. (G8B11)
If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, a 13.345 MHz signal will produce an image response in the receiver. (G8B02)
  13.800 MHz minus 455 kHz is 13.345 MHz, the lower image response frequency.
  To prevent this many receivers use a tuned preamplifier before the mixer input (sometimes called a pre-selector).
An advantage of a receiver Digital Signal Processor IF filter as compared to an analog filter is that a wide range of filter bandwidths and shapes can be created. (G4C12)
As the noise reduction control level in a receiver is increased the received signals may become distorted. (G4A17)
15
Your Receiver

## Slide 16
Your Receiver
One reason to use the attenuator function that is present on many HF transceivers is to reduce signal overload due to strong incoming signals. (G4A13)
Dual function switch: Pre-amp & Attenuator.
Icom 7000
16
Your Receiver

## Slide 17
Your Receiver
A noise blanker is a device that detects pulses and blocks the signal during the time of each pulse. A noise blanker becomes more effective (very much) at large bandwidths as long as there are no strong signals present in the pass band. (G4A16)
The purpose of the "notch filter" found on many HF transceivers is to reduce interference from carriers in the receiver passband. (G4A01)
17
Your Receiver

## Slide 18
Your Receiver
A discriminator circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio. (G7C08)
    FM receivers have different types of circuits than the superheterodyne receivers designed for AM, CW and SSB.
Discriminator circuit
Frequency to voltage conversion
17
Your Receiver

## Slide 19
Your Receiver
The S meter on your new HF transceiver ties directly in to the receiver section of the radio and is tied in to the receiver’s automatic gain control (AGC). (G4D06)
The S-meter is an instrument present on the majority of radio receivers that measure the strength of the signal that is being received. (G4D04)
    Most all receivers have an S-meter showing received signal strength.
18
Your Receiver

## Slide 20
Element 3 General Class Question Pool
Your Receiver
20
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 21: G7C08 Which parameter affects receiver sensitivity?
Input amplifier gain
Demodulator stage bandwidth
Input amplifier noise figure
All these choices are correct

## Slide 22
G8B12
What process combines two signals in a non-linear circuit or connection to produce unwanted spurious outputs ?
Intermodulation.
Heterodyning.
Detection.
Rolloff.
22

## Slide 23: G8B05 Which intermodulation products are closest to the original signal frequencies?
Second harmonics
Even-order
Odd-order
Intercept point

## Slide 24: G8B13 Which of the following is an odd-order intermodulation product of frequencies F1 and F2?
5F1-3F2
3F1-F2
2F1-F2
All these choices are correct

## Slide 25
G7C04
How is a product detector used?
Used in test gear to detect spurious mixing products
Used in transmitter to perform frequency multiplication
Used in an FM receiver to filter out unwanted sidebands
Used in a single sideband receiver to extract the modulated signal
23

## Slide 26
G8B03
What is another term for the mixing of two RF signals?
Heterodyning.
Synthesizing.
Cancellation.
Multiplying.
24

## Slide 27
G8B01
Which mixer input is varied or tuned to convert signals of different frequencies to an intermediate frequency (IF)?
Image frequency
Local oscillator
RF input
Beat frequency oscillator
24

## Slide 28
G7C05
Which of the following is an advantage of a direct digital synthesizer (DDS)?
Extremely narrow tuning range
Relatively high-power output
Pure sine wave output
Variable output frequency with the stability of a crystal oscillator
27

## Slide 29: G7C11 Which of these functions is performed by software in a software-defined radio (SDR)?
Filtering
Detection
Modulation
All these choices are correct

## Slide 30: G7C09 What is the phase difference between the I and Q RF signals that software-defined radio (SDR) equipment uses for modulation and demodulation?
Zero
90 degrees
180 degrees
45 degrees

## Slide 31
G8B11
What combination of a mixer’s Local Oscillator (LO) and RF input frequencies is found in the output ?
The Ratio.
The average.
The Sum and Difference.
The arithmetic product.
31

## Slide 32: G8B02 What is the term for interference from a signal at twice the IF frequency from the desired signal?
Quadrature response
Image response
Mixer interference
Intermediate interference

## Slide 33: G7C06 Which of the following is an advantage of a digital signal processing (DSP) filter compared to an analog filter?
A wide range of filter bandwidths and shapes can be created
Fewer digital components are required
Mixing products are greatly reduced
The DSP filter is much more effective at VHF frequencies

## Slide 34: G4A07 What happens as a receiver’s noise reduction control level is increased?
Received signals may become distorted
Received frequency may become unstable
CW signals may become severely attenuated
Received frequency may shift several kHz

## Slide 35: G4A03 How does a noise blanker work?
By temporarily increasing received bandwidth
By redirecting noise pulses into a filter capacitor
By reducing receiver gain during a noise pulse
By clipping noise peaks

## Slide 36: G4A01 What is the purpose of the notch filter found on many HF transceivers?
To restrict the transmitter voice bandwidth
To reduce interference from carriers in the receiver passband
To eliminate receiver interference from impulse noise sources
To remove interfering splatter generated by signals on adjacent frequencies

## Slide 37: G4A13 What is the purpose of using a receive attenuator?
To prevent receiver overload from strong incoming signals
To reduce the transmitter power when driving a linear amplifier
To reduce power consumption when operating from batteries
To reduce excessive audio level on strong signals

## Slide 38: G4D04 What does an S meter measure?
Carrier suppression
Impedance
Received signal strength
Transmitter power output

## Slide 39: G4D07 How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9?
Approximately 1.5 times
Approximately 2 times
Approximately 4 times
Approximately 8 times

## Slide 40: G4D05 How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter?
It is 10 times less powerful
It is 20 times less powerful
It is 20 times more powerful
It is 100 times more powerful

## Slide 41: G4D06 How much change in signal strength is typically represented by one S unit?
6 dB
12 dB
15 dB
18 dB

## Slide 42: Thank You!