## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: General Licensing Class Chapter 12
Oscillators & Components
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 6: Oscillators & Components
The basic components of virtually all sine wave oscillators are a filter and an amplifier operating in a feedback loop. (G7B07)
Sine wave
Square wave
Triangle wave
Sawtooth wave
Voltage waveforms

## Slide 7: Oscillators & Components
The inductance and capacitance in the tank circuit determines the frequency of an LC oscillator. (G7B09)
Tank Circuits
Inductors
(variable) Capacitors

## Slide 8: Oscillators & Components
The control grid is the element of a triode vacuum tube is used to regulate the flow of electrons between cathode and plate. (G6A10)
The primary purpose of a screen grid in a vacuum tube is to reduce grid-to-plate capacitance. (G6A12)
H=Heater/Filament; C=Cathode; S=Screen Grid; P=Plate
7

## Slide 9: Oscillators & Components
The stable operating points for a bipolar transistor used as a switch in a logic circuit are its saturation and cut-off regions. (G6A07)
    Saturation is where the transistor is Base biased for maximum emitter to collector current flow.
    Cut-off is where the transistor is base biased for minimum emitter to collector current flow.
In a MOSFET, the gate is separated from the channel with a thin insulating layer. (G6A09)

## Slide 10: Oscillators & Components
The approximate junction threshold voltage of a germanium diode is 0.3 volts. (G6A03)
    This is the voltage drop across the diode junction when it is conducting in the forward direction.
The approximate junction threshold voltage of a silicon diode is 0.7 volts. (G6A05)
    This is the voltage drop across the diode junction when it is conducting in the forward direction.
      A silicon diode will conduct current only if its anode is at a positive voltage compared to its cathode; it is then said to be forward biased.
      The Forward bias decreases the resistance of the diode whereas the reversed bias increases the resistance of the diode. In forward biasing the current is easily flowing through the circuit whereas reverse bias does not allow the current to flow through it.
1N34A Germanium Diode.
You can bet that when you see a quartet of large silicon diodes in close proximity that they are the main ingredients of a full-wave rectifier.

## Slide 11: Oscillators & Components
An LED is forward biased when emitting light. (G6B08)
Array of LEDs and resistors

## Slide 12: Oscillators & Components
LCDs do not emit light. Therefore, a liquid crystal display requires ambient or back lighting. (G6B09)
The black on amber LCD can easily be seen under any lighting condition!

## Slide 13: Oscillators & Components
The term MMIC means Monolithic Microwave Integrated Circuit. (G6B02)
Analog is also the term that describes an integrated circuit operational amplifier. (G6B06)
Schematic symbol
Integrated circuit
MMIC devices
Signal connections

## Slide 14: Oscillators & Components
A shift register is a clocked array of circuits that passes data in steps along the array. (G7B06)
Low power consumption is an advantage of CMOS integrated circuits compared to TTL integrated circuits. (G6B03)
    CMOS is the most commonly used digital logic family of integrated circuits.
The term ROM means Read Only Memory. (G6B04)
4-Bit SIPO Shift Register

## Slide 15: Oscillators & Components
ROM is characterized as “non-volatile,” meaning the stored information is maintained even if power is removed. (G6B05)
For a two input AND gate, the output is high only when both inputs are high. (G7B03)

## Slide 16: Oscillators & Components
For a two input NOR gate, the output is low when either or both inputs are high. (G7B04)
A 3-bit binary counter contains 8 states. (G7B05)
  Each flip-flop requires two input pulses to generate one output pulse.
  In short, being Base 2, 3-bit is 2 x 2 x 2 = 8.
Truth table for NOR Gate

## Slide 17
Element 3 General Class Question Pool
Oscillators & Components
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 18
G7B09
What determines the frequency of an LC oscillator?
The number of stages in the counter
The number of stages in the divider
The inductance and capacitance in the tank circuit
The time delay of the lag circuit

## Slide 19
G6A10
Which element of a vacuum tube regulates the flow of electrons between cathode and plate?
Control grid
Suppressor grid
Screen grid
Trigger electrode

## Slide 20
G6A12
What is the primary purpose of a screen grid in a vacuum tube?
To reduce grid-to-plate capacitance
To increase efficiency
To increase the high frequency response
To decrease plate resistance

## Slide 21
G6A07
What are the operating points for a bipolar transistor used as a switch?
Saturation and cutoff
The active region (between cutoff and saturation)
Peak and valley current points
Enhancement and depletion modes

## Slide 22
G6A08
Which of the following is characteristic of low voltage ceramic capacitors?
The gate is formed by a back-biased junction
The gate is separated from the channel by a thin insulating layer
The source is separated from the drain by a thin insulating layer
The source is formed by depositing metal on silicon

## Slide 23
G6A09
Which of the following describes MOSFET construction?
The gate is formed by a back-biased junction.
The gate is separated from the channel with a thin insulating layer.
The source is separated from the drain by a thin insulating layer.
The source is formed by depositing metal on silicon.

## Slide 24
G6A03
What is the approximate forward threshold voltage of a germanium diode?
0.1 volt
0.3 volts
0.7 volts
1.0 volts

## Slide 25
G6A05
What is the approximate forward threshold voltage of a silicon junction diode?
0.1 volt
0.3 volts
0.7 volts
1.0 volts

## Slide 26
G7B06
shift
In the tunnel-effect region
At the Zener voltage
Reverse biased
Forward biased

## Slide 27
G6B08
How is an LED biased when emitting light?
In the tunnel-effect region
At the Zener voltage
Reverse biased
Forward biased

## Slide 28
G6B02
What is meant by the term MMIC?
Multi Megabyte Integrated Circuit.
Monolithic Microwave Integrated Circuit.
Military-specification Manufactured Integrated Circuit.
Mode Modulated Integrated Circuit.

## Slide 29
G6B06
Which kind of device is an integrated circuit operational amplifier?
Digital.
MMIC.
Programmable Logic.
Analog.

## Slide 30
G6B03
Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits?
Low power consumption.
High power handling capability.
Better suited for RF amplification.
Better suited for power supply regulation.

## Slide 31
G7B03
Which of the following describes the function of a two input AND gate?
Output is high when either or both inputs are low.
Output is high only when both inputs are high.
Output is low when either or both inputs are high.
Output is low only when both inputs are high.

## Slide 32
G7B05
How many states does a 3-bit binary counter have?
3
6
8
16

## Slide 33: Thank You!