## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: General Licensing Class Chapter 13
Electrical Principles
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 6: Electrical Principles
245 volts would be the voltage across a 50-ohm dummy load dissipating 1200 watts. (G5B12)
    See E on chart
    E =√ (P*R)
    E = √ (1200*50)
    E = √ 60,000
    E = 244.9 Volts RMS
200 watts of electrical power are used if 400 VDC is supplied to an 800-ohm load. (G5B03) ​
    See P on chart
    P=E²/R
    P=(400)²/800
    P=160,000 / 800
    P= 200 Watts

## Slide 7: Electrical Principles
2.4 watts of electrical power are used by a 12-VDC light bulb that draws 0.2 amperes. (G5B04)
    P= I * E
    P=(12) * 0.2
    P= 2.4 Watts
Approximately 61 milliwatts are being dissipated when a current of 7.0 milliamperes flows through 1.25 kilo- ohms. (G5B05)
    P= I² R
    P =(0.007)² * 1250
    P = 0.000049 * 1250
    P=0.0613 watts
    0.061 Watts = 61.3 Milliwatts
    (close enough to 61)
See P on chart
See P on chart

## Slide 8: Electrical Principles
Root Mean Square (RMS) measurement of an AC signal (also called the effective value of an AC voltage) is the same as a DC voltage of the same value. (G5B07)
Root Mean Square Value This value of AC voltage produces same heating in a resistor as a DC voltage of the same value.
If you combined two or more sine wave voltages, the RMS voltage would be the square root of the average of the sum of the squares of each voltage waveform.
VPP = 2 X VPK
VRMS = 0.707 VPK
VPK = 1.414 VRMS
RMS (VRMS), Peak, (VPK), and Peak-to-Peak (VPP) Voltage

## Slide 9: Electrical Principles
12 volts is the RMS voltage of a sine wave with a value of 17 volts peak. (G5B09)
    RMS = Peak * 0.707
    RMS = 17 * 0.707
    RMS = 12 Volts

## Slide 10: Electrical Principles
One advantage of a switched-mode power supply as compared to a linear power supply is that high frequency operation allows the use of smaller components.(G7A08)
Regulated supply showing outputs
Interior view of a switched-mode
power supply:
A - bridge rectifier B - Input filter capacitors C - Transformer D - output filter coil E - output filter capacitors

## Slide 11: Electrical Principles
180 degrees is the portion of the AC cycle that is converted to DC by a half-wave rectifier. (G7A05)
Half-wave rectifier power supply
Input

## Slide 12: Electrical Principles
Only one diode is required in a half-wave rectifier power supply. (G7A04)
Half-wave rectifier power supply

## Slide 13: Electrical Principles
360 degrees is the portion of the AC cycle is converted to DC by a full-wave rectifier. (G7A06)
A full wave rectifier uses two diodes and a center-tapped transformer. (G7A03)
Full-wave rectifier power supply

## Slide 14: Electrical Principles
A series of DC pulses at twice the frequency of the AC input is the output waveform of an unfiltered full-wave rectifier connected to a resistive load (G7A07)
Full-wave rectifier power supply

## Slide 15: Electrical Principles
The output of a rectifier connects to a filter made up of capacitors and inductors. Capacitors and inductors are used in a power-supply filter network. (G7A02)
High capacitance for given volume is an advantage of an electrolytic capacitor. (G6A04)
Typical Pi filter network
Filter Capacitor
Filter Choke
Electrolytic capacitors are used in just about every power supply as they can contain a lot of capacitance in a small space.

## Slide 16: Electrical Principles
  Most electrolytic capacitors are polarized, meaning they care deeply about which way you wire them up.
Polarity of applied voltages is very important for polarized capacitors. (G6A13)
  Incorrect polarity can cause the capacitor to short-circuit.
  Reverse voltages can destroy the dielectric layer of an electrolytic capacitor.
  The capacitor could overheat and explode.
    All of these choices are correct.
Electrolytic capacitors

## Slide 17: Electrical Principles
A useful feature of a bleeder resistor in a power supply is that it ensures that the filter capacitors are discharged when power is removed. (G7A01)
Full-Wave Bridge Solid State Power Supply with pi network filter and resistive load
Bleeder resistor

## Slide 18: Electrical Principles
An advantage of a digital voltmeter as compared to an analog voltmeter is that it has better precision for most uses. (G4B06)
When adjusting tuned circuits, the use of an instrument with analog readout may be preferred over an instrument with a numerical digital readout. (G4B14)
Digital Voltmeter
Analog Voltmeter

## Slide 19: Electrical Principles
High input impedance is desirable for a voltmeter because it decreases the loading on circuits being measured. (G4B05)
  The analog needle movement can give the “feel,” visually, of Tuned Circuits, as long as that particular tuned circuit does not call for specialized, non-loading measurements.
Simpson 260 Series 8P Analog Multimeter

## Slide 20: Electrical Principles
An advantage of the low internal resistance of nickel-cadmium batteries is that they can supply large quantities of current very quickly. (G6A02)
The minimum allowable discharge voltage for maximum life of a standard 12-volt lead-acid battery is 10.5 volts. (G6A01)
  Each cell should not be discharged below 1.75 volts to avoid causing irreversible chemical changes that damage the cell.
Always check the polarity of your batteries. Many “dead” radios are simply the result of one or more batteries being installed backwards!

## Slide 21: Electrical Principles
The process by which sunlight is changed directly into electricity is called photovoltaic conversion. (G4E08)
Solar panels
Schematic of Solar Panel for Charging Storage Batteries.

## Slide 22: Electrical Principles
The approximate open-circuit voltage from a modern, well-illuminated photovoltaic cell is 0.5 VDC. (G4E09)
The reason a series diode is connected between a solar panel and a storage battery that is being charged by the panel is that the diode prevents self discharge of the battery though the panel during times of low or no illumination. (G4E10)
One disadvantage of using wind as the primary source of power for an emergency station is that a large energy storage system is needed to supply power when the wind is not blowing. (G4E11)
This small wind generator can keep a charge on a portable battery system as long as the wind is greater than 5 mph.

## Slide 23: Electrical Principles
A direct, fused power connection to the battery using heavy gauge wire would be the best for a 100-watt HF mobile installation. (G4E03)
It is best NOT to draw the DC power for a 100-watt HF transceiver from an automobile's auxiliary power socket because the socket's wiring may be inadequate for the current being drawn by the transceiver. (G4E04)

## Slide 24: General Licensing Class Chapter 13
Electrical Principles
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 24

## Slide 25
G5B12
What would be the RMS voltage across a 50-ohm dummy load dissipating 1200 watts?
173 volts.
245 volts.
346 volts.
692 volts.
Notes: 25

## Slide 26
G5B03
How many watts of electrical power are used if 400 VDC is supplied to an 800-ohm load?
0.5 watts.
200 watts.
400 watts.
3200 watts.

## Slide 27
G5B04
How many watts of electrical power are used by a 12-VDC light bulb that draws 0.2 amperes?
2.4 watts.
24 watts.
6 watts.
60 watts.

## Slide 28
G5B05
How many watts are consumed when a current of 7.0 milliamperes flows through a 1,250-ohm resistance?
Approximately 61 milliwatts.
Approximately 61 watts.
Approximately 11 milliwatts.
Approximately 11 watts.

## Slide 29
G5B06
What is the PEP produced by 200 volts peak-to-peak across a 50-ohm dummy load?
1.4 watts
100 watts
353.5 watts
400 watts

## Slide 30
G5B07
Which value of an AC signal results in the same power dissipation as a DC voltage of the same value?
The peak-to-peak value.
The peak value.
The RMS value.
The reciprocal of the RMS value.

## Slide 31
G5B08
What is the peak-to-peak voltage of a sine wave with an RMS voltage of 120 volts?
84.8 volts
169.7 volts
240.0 volts
339.4 volts

## Slide 32
G5B09
What is the RMS voltage of sine wave with a value of 17 volts peak?
8.5 volts.
12 volts.
24 volts.
34 volts.

## Slide 33
G7A08
Which of the following is characteristic of a switchmode power supply as compared to a linear power supply?
Faster switching time makes higher output voltage possible
Fewer circuit components are required
High-frequency operation allows the use of smaller components
Inherently more stable

## Slide 34
G7A04
What is characteristic of a half-wave rectifier in a power supply?
Only one diode is required
The ripple frequency is twice that of a full-wave rectifier
More current can be drawn from the half-wave rectifier
The output voltage is two times the peak input voltage

## Slide 35
G7A05
What portion of the AC cycle is converted to DC by a half-wave rectifier?
90 degrees.
180 degrees.
270 degrees.
360 degrees.

## Slide 36
G7A06
What portion of the AC cycle is converted to DC by a full-wave rectifier ?
90 degrees.
180 degrees.
270 degrees.
360 degrees.

## Slide 37
G7A03
Which type of rectifier circuit uses two diodes and a center-tapped transformer?
Full wave.
Full Wave Bridge.
Half-wave.
Synchronous.

## Slide 38
G7A07
What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
A series of DC pulses at twice the frequency of the AC input.
A series of DC pulses at the same frequency as the AC input.
A sine wave at half the frequency of the AC input.
A steady DC voltage.

## Slide 39
G7A02
Which of the following components are used in a power supply filter network?
Diodes
Transformers and transducers
Capacitors and inductors
All these choices are correct

## Slide 40
G6A04
Which of the following is characteristic of an electrolytic capacitor?
Tight tolerance
Much less leakage than any other type
High capacitance for a given volume
Inexpensive RF capacitor

## Slide 41
G7A01
What is the function of a power supply bleeder resistor?
It acts as a fuse for excess voltage
It discharges the filter capacitors when power is removed
It removes shock hazards from the induction coils
It eliminates ground loop current

## Slide 42
G4B06
What is an advantage of a digital multimeter as compared to an analog multimeter?
Better for measuring computer circuits
Less prone to overload
Higher precision
Faster response

## Slide 43
G4B09
When is an analog multimeter preferred to a digital multimeter?
When testing logic circuits
When high precision is desired
When measuring the frequency of an oscillator
When adjusting circuits for maximum or minimum values

## Slide 44
G4B05
Why do voltmeters have high input impedance?
It improves the frequency response
It allows for higher voltages to be safely measured
It improves the resolution of the readings
It decreases the loading on circuits being measured

## Slide 45
G6A02
What is an advantage of batteries with low internal resistance?
Long life
High discharge current
High voltage
Rapid recharge

## Slide 46
G6A01
What is the minimum allowable discharge voltage for maximum life of a standard 12-volt lead-acid battery?
6 volts
8.5 volts
10.5 volts
12 volts

## Slide 47
G4E09
What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell?
0.02 VDC
0.5 VDC
0.2 VDC
1.38 VDC

## Slide 48
G4E08
In what configuration are the individual cells in a solar panel connected together?
Series-parallel
Shunt
Bypass
Full-wave bridge

## Slide 49
G4E10
Why should a series diode be connected between a solar panel and a storage battery that is being charged by the panel?
To prevent overload by regulating the charging voltage
To prevent discharge of the battery through the panel during times of low or no illumination
To limit the current flowing from the panel to a safe value
To prevent damage to the battery due to excessive voltage at high illumination levels

## Slide 50
G4E11
What precaution should be taken when connecting a solar panel to a lithium iron phosphate battery?
Ground the solar panel outer metal framework
Ensure the battery is placed terminals-up
A series resistor must be in place
The solar panel must have a charge controller

## Slide 51
G4E03
Which of the following direct, fused power connections would be the best for a 100-watt HF mobile installation?
To the battery using heavy-gauge wire
To the alternator or generator using heavy-gauge wire
To the battery using insulated heavy duty balanced transmission line
To the alternator or generator using insulated heavy duty balanced transmission line

## Slide 52
G4E04
Why should DC power for a 100-watt HF transceiver not be supplied by a vehicle’s auxiliary power socket?
The socket is not wired with an RF-shielded power cable
The socket’s wiring may be inadequate for the current drawn by the transceiver
The DC polarity of the socket is reversed from the polarity of modern HF transceivers
Drawing more than 50 watts from this socket could cause the engine to overheat

## Slide 53: Thank You!