## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2024 ARRL
All Rights Reserved

## Slide 2: Circuits

## Slide 3
General Licensing Class
Circuits
Question Pool valid
July 1st, 2023 Through June 30th, 2027
Notes: 3

## Slide 4
4
Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 - Voice Operations
  6 - CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
5
Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 - Coax Cable
  18 -RF & Electrical Safety

## Slide 6: Circuits
Symbol 1 in figure G7-1 represents a field effect transistor. (G7A09)
Schematic symbol for:
Field Effect Transistor.

## Slide 7: Circuits
Symbol 5 in figure G7-1 represents a Zener diode. (G7A10)
Schematic symbol for:
Zener Diode.

## Slide 8: Circuits
Symbol 2 in figure G7-1 represents an NPN junction transistor. (G7A11)
Schematic symbol for:
NPN Junction Transistor

## Slide 9: Circuits
Symbol 6 in Figure G7-1 represents a multiple-winding transformer. (G7A12)
Schematic symbol for:
Multiple-winding transformer.

## Slide 10: Circuits
Symbol 7 in Figure G7-1 represents a tapped inductor. (G7A13)
Schematic symbol for:
Tapped Inductor.

## Slide 11: Circuits
The total resistance of three 100-ohm resistors in parallel is 33.3 ohms. (G5C04)
  For identical resistors in parallel simply divide the resistance of one resistor by the number of resistors to find the total network resistance.
  R = resistor value / number of resistors
  R = 100 / 3
  R = 33.333 Ohms
The total current entering a parallel circuit equals the sum of the currents through each branch. (G5B02)
Or the long way.
IT = I1 + I2 + I3

## Slide 12: Circuits
Three equal value resistors in series produce 450 ohms total mean each resistor was 150 ohms in value. (G5C05)

## Slide 13: Circuits
5.9 ohms is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor in parallel. (G5C15)
  RT= 1/ [(1/R1) + (1/R2) + (1/R3)]
  RT= 1/ [(1/10) + (1/20) + (1/50)]
  RT = 1/ [(0.1) + (0.05) + (0.02)]
  RT =1/ .17
  RT = 5.88 ohms (close enough to 5.9)
    Remember that the total resistance in a parallel circuit will always be less than the smallest resistor in the parallel network.
A resistor in series should be added to an existing resistor in a circuit to increase circuit resistance. (G5C03)

## Slide 14: Circuits
The equivalent capacitance of two 5000 nanofarad capacitors and one 750 picofarad capacitor connected in parallel is 10750 picofarads or 10.750 nanofarads. (G5C08)
    Capacitors in parallel simply add together,
    therefore the total capacity would be:
    5000 pf + 5000pf + 750 pf
    10750 picofarads or 10.750 nanofarads
Capacitors in parallel.
Capacitors in parallel formula.

## Slide 15: Circuits
The capacitance of three 100 microfarad capacitors connected in series 33.3 microfarads. (G5C09)
  For identical capacitors in series simply divide the capacitance of one capacitor by the number of Capacitors.
  C=capacitance value / number of capacitors
  C = 100 / 3
  C = 33.333 microfarads
(Only for equal values.)

## Slide 16: Circuits
The capacitance of a 20 microfarad capacitor in series with a 50 microfarad capacitor is 14.3 microfarads. (G5C12)
    CT= 1/ [(1/C1) + (1/C2)]
    CT = 1/ [(1/20) + (1/50)]
    CT = 1/ [(.050)+(1/.020)]
    CT = (1/.07)
    CT = 14.285 microfarads
The value of a 22,000 picofarads (pf) capacitor in nanofarads is 22. (nf). (G5C17)
The value in microfarads (mf) of a 4700 nanofarad (nf) is 4.7mf. (G5C18)
To increase the capacitance in a circuit, a capacitor in parallel should be added. (G5C13)
To increase the inductance in a circuit, add an inductor in series. (G5C14)

## Slide 17: Circuits
The inductance of three 10 millihenry inductors connected in parallel is 3.3 millihenrys. (G5C10)
  For identical inductors in parallel simply divide the inductance of one inductor by the number of inductors.
  L=Inductor value / number of inductors
  L = 10 / 3
  L = 3.333 millihenrys
The inductance of a 20 millihenry inductor in series with a 50 millihenry inductor is 70 millihenrys (G5C11)
  Inductors in series simply add. (Just like resistors in series.)
  Therfore L = 20 + 50
  L = 70 millihenrys.
Or the long way.

## Slide 18: Circuits
Reactance is opposition to the flow of alternating current caused by capacitance or inductance. (G5A02)
All real world inductors have a certain amount of parasitic capacitance. As frequency goes up, capacitive reactance is reciprocal, so the circuit become capacitive. (G6A11)
Inductive reactance
Capacitive reactance
When XL equals XC, it creates a special frequency called ‘resonant frequency’.
XL=2pFL
XC=
2pFC
1

## Slide 19: Electrical Principles
Resonance occurs in a circuit when XL is equal to XC.
Therefore…..
What we do to the left side of the equation, we must do to the right side, and what we do to the numerator we must do to the denominator, to maintain equality.
This is XL=XC
Mulitplied both sides by F and divided both sides by 2pL
Multiplied denominator
F2=
(2pL)(2pC)
1
(2p)2(LC)
F2=
1

## Slide 20
This is the resonant frequency formula.
Electrical Principles
2p √LC
F2=
(2p)2 LC
1
F=
1
Take square root of both sides of equation
From previous slide

## Slide 21: Circuits
Reactance causes opposition to the flow of alternating current in an inductor. (G5A03)
Ohm is the unit used to measure reactance. (G5A09)
Reactance causes opposition to the flow of alternating current in a capacitor. (G5A04)
As the frequency of the applied AC increases, the reactance of a capacitor decreases. (G5A06)
As the frequency of the applied AC increases, the reactance of an inductor increases. (G5A05)
Impedance Z, is the opposition to the flow of current in an AC circuit. (G5A01)
See XC formula
See XL formula

## Slide 22: Circuits
One method of impedance matching between two AC circuits is to insert an LC network between the two circuits. (G5A11)
Impedance matching is important so the source can deliver maximum power to the load. (G5A08)
Devices that can be used for impedance matching at radio frequencies: (G5A10)
  A transformer
  A Pi-network
  A length of transmission line
All of these choices are correct.

## Slide 23: Circuits
When the impedance of an electrical load is equal to the internal impedance of the power source, the source can deliver maximum power to the load. (G5A07)
The impedance of a low-pass filter should be about the same as the impedance of the transmission line into which it is inserted. (G7C06)

## Slide 24: Circuits
The cutoff frequency is a low-pass filter’s output power that is less than half the input power. (G7C12)
Ultimate rejection specifies a filter’s ability to reject signals outside the passband. (G7C13)
  Generally specified as the -60db point.

## Slide 25: Circuits
Insertion loss specifies a filter’s attenuation inside its passband. (G7C15)
A reason not to use wire-wound resistors in an RF circuit is that the resistor's inductance could make circuit performance unpredictable. (G6A06)
The Upper and Lower half-power points in frequency determine the bandwidth of a band-pass filter. (G7C14)
Wire wound resistors can act like an inductor at certain frequencies.

## Slide 26: Circuits
An advantage of ceramic capacitors as compared to other types of capacitors is comparatively low cost. (G6A14)
The advantages of using a ferrite core with a toroidal inductor: (G6A08):
  Large values of inductance may be obtained.
  The magnetic properties of the core may be optimized for a specific range of frequencies.
  Most of the magnetic field is contained in the core.
All of these choices are correct.

## Slide 27: Circuits
The composition, or “mix,” of materials used determine, the performance of a ferrite core at different frequencies. (G6B01)
Mutual inductance causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding. (G5C01)
In order to accommodate the higher current of the primary, the conductor of the primary winding of many voltage step-up transformers is larger than the conductor of the secondary winding. (G5C16)

## Slide 28: Circuits
The voltage across a 500-turn secondary winding of a transformer is 26.7 volts if the 2250-turn primary is connected to 120 VA. (G5C06)
    500 / 2250 (SecondaryVoltage/PrimaryVoltage)
    0.222
    (Therefore the Secondary output voltage
    will be .222 times the input voltage)
    0.222 * 120
    26.666) Volts (Close enough to 26.7)
The output voltage is multiplied by 4 if a signal is applied to the secondary winding of a 4:1 voltage step-down transformer instead of the primary winding. (G5C02)
Three of the four are given. Solve for the unknown.
NS
NP
VP
VS NS
VP NP
=

## Slide 29: Circuits
The turns ratio of a transformer used to match an audio amplifier having a 600-ohm output impedance to a speaker having a 4-ohm impedance is 12.2 to 1. (G5C07)
NP = turns on the primary
NS = turns on the secondary
ZP = primary impedance
ZS = secondary impedance
=
12.2
=
=
NP
NS
=
ZP
ZS
600
4
150
This is a ‘turns ratio’ problem.
This is a ‘turns ratio’ problem.

## Slide 30
Element 3 General Class Question Pool
Circuits
Question Pool valid
July 1st, 2023 Through June 30th, 2027

## Slide 31: G7A09 Which symbol in figure G7-1 represents a field effect transistor?
Symbol 2.
Symbol 5.
Symbol 1.
Symbol 4.

## Slide 32: G7A10 Which symbol in figure G7-1 represents a Zener diode?
Symbol 4.
Symbol 1.
Symbol 11.
Symbol 5.

## Slide 33: G7A11 Which symbol in figure G7-1 represents an NPN junction transistor?
Symbol 1.
Symbol 2.
Symbol 7.
Symbol 11.

## Slide 34: G7A12 Which symbol in figure G7-1 represents a multiple-winding transformer?
Symbol 4.
Symbol 7.
Symbol 6.
Symbol 1.

## Slide 35: G7A13 Which symbol in figure G7-1 represents a tapped inductor?
Symbol 7.
Symbol 11.
Symbol 6.
Symbol 1.

## Slide 36
G5B02 How does the total current relate to the individual currents in a circuit of parallel resistors? in each branch of a parallel circuit?
It equals the average of each branch current.
It decreases as more parallel branches are added to the circuit.
It equals the sum of the currents through each branch.
It is the sum of the reciprocal of each individual voltage drop.

## Slide 37: G5C05 Why is the conductor of the primary winding of many voltage step-up transformers large in diameter than the conductor of the secondary winding ?
To improve the coupling between the primary and secondary.
To accommodate the higher current of the primary.
To prevent parasitic oscillations due to the resistive losses in the primary.
To ensure that the volume of the primary winding is equal to the volume of the secondary winding.

## Slide 38
G5C03 What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor in parallel?
5.9 ohms.
0.17 ohms.
10000 ohms.
80 ohms.

## Slide 39
G5C04 What is the approximate total resistance of a 100- and a 200-ohm resistor in parallel?
300 ohms
150 ohms.
75 ohms.
67 ohms.

## Slide 40
G5C08 What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel?
576.9 nanofarads.
1733 picofarads.
3583 picofarads.
10.750 nanofarads.

## Slide 41
G5C09 What is the capacitance of three 100 microfarad capacitors connected in series?
0.30 microfarads.
0.33 microfarads.
33.3 microfarads.
300 microfarads.

## Slide 42
G5C12 What is the capacitance of a 20 microfarad capacitor in series with a 50 microfarad capacitor?
0.07 microfarads.
14.3 microfarads.
70 microfarads.
1000 microfarads.

## Slide 43
G5C13 Which of the following components should be added to a capacitor to increase the capacitance?
An inductor in series.
A resistor in series.
A capacitor in parallel.
A capacitor in series.

## Slide 44
G5C14 Which of the following components should be added to an inductor to increase the inductance?
A capacitor in series.
A resistor in parallel.
An inductor in parallel.
An inductor in series.

## Slide 45
G5C10 What is the inductance of three 10 millihenry inductors connected in parallel?
0.30 Henrys.
3.3 Henrys.
3.3 millihenrys.
30 millihenrys.

## Slide 46
G5C11 What is the inductance of a 20 millihenry inductor in series with a 50 millihenry inductor?
0.07 millihenrys.
14.3 millihenrys.
70 millihenrys.
1000 millihenrys.

## Slide 47
G6A11 What happen when an inductor is operated above it self-resonant frequency ?
Its reactance increases.
Harmonics are generated.
It becomes capacitive.
Catastrophic failure is likely.

## Slide 48
G5A02 What is reactance?
Opposition to the flow of direct current caused by resistance
Opposition to the flow of alternating current caused by capacitance or inductance
Reinforcement of the flow of direct current caused by resistance
Reinforcement of the flow of alternating current caused by capacitance or inductance

## Slide 49: G5A12 What occurs in an LC circuit at resonance?
Current and Voltages are equal
Resistance is cancelled
The circuit radiates all its energy in the form of radio waves
Inductive reactance and capacitive reactance cancel

## Slide 50
G5A01 What happens when inductive and capacitive reactance are equal in a series LC circuit?
Resonance causes impedance to be very high
B. Impedance is equal to the geometric mean of the inductance and capacitance
C. Resonance causes impedance to be very low
D. Impedance is equal to the arithmetic mean of the inductance and capacitance

## Slide 51
G5A03 Which of the following is opposition to the flow of alternating current in an inductor?
Conductance
Reluctance
Admittance
Reactance

## Slide 52
G5A09 What unit is used to measure reactance?
Farad.
Ohm.
Ampere.
Reactance.

## Slide 53: G5A04 Which of the following causes opposition to the flow of alternating current in a capacitor?
Conductance.
Reluctance.
Reactance.
Admittance.

## Slide 54: G5A05 How does an inductor react to AC?
As the frequency of the applied AC increases, the reactance decreases.
As the amplitude of the applied AC increases, the reactance increases.
As the amplitude of the applied AC increases, the reactance decreases.
As the frequency of the applied AC increases, the reactance increases.

## Slide 55: G5A06 How does a capacitor react to AC?
As the frequency of the applied AC increases, the reactance decreases.
As the frequency of the applied AC increases, the reactance increases.
As the amplitude of the applied AC increases, the reactance increases.
As the amplitude of the applied AC increases, the reactance decreases.

## Slide 56: G5A11 What letter is used to represent reactance?
Z
X
B
Y

## Slide 57: G5A08 What is impedance?
The ratio of current to voltage
The product of current and voltage
The ratio of voltage to current
The product of current and reactance

## Slide 58: G5A07 What is the term for the inverse of impedance?
Conductance
Susceptance
Reluctance
Admittance

## Slide 59: G5A10 Which of the following devices can be used for impedance matching at radio frequencies?
A transformer.
A Pi-network.
A length of transmission line.
All of these choices are correct.

## Slide 60
G7C12 What is the frequency above which the low-pass filter’s output power is less than half the input power ?
Notch Frequency.
Neper Frequency.
Cutoff Frequency.
Rolloff Frequency.

## Slide 61
G7C13 What term specifies a filter’s maximum ability to reject signals outside its passband ?
Notch depth.
Rolloff.
Insertion loss.
Ultimate rejection.

## Slide 62
G7C14 The bandwidth of a band-pass filter is measured between what two frequencies?
Upper and lower half-power.
Cutoff and Rolloff.
Pole and zero.
Image and harmonic.

## Slide 63
G7C07 What term specifies a filters attenuation inside its passband ?
Insertion loss.
Return loss.
Q.
Ultimate rejection.

## Slide 64: G6A06 Why should wire-wound resistors not be used in RF circuits?
The resistor's tolerance value would not be adequate for such a circuit.
The resistor’s inductance could make the circuit performance unpredictable.
The resistor could overheat.
The resistor’s internal capacitance would detune the circuit.

## Slide 65: G6B05 What is an advantage of using a ferrite core toroidal inductor?
Large values of inductance may be obtained.
The magnetic properties of the core may be optimized for a specific range of frequencies.
Most of the magnetic field is contained in the core.
All of these choices are correct.

## Slide 66: G6B01 What determines the performance of a ferrite core at different frequencies?
Its conductivity.
Its thickness.
The composition, or “mix,” of materials used.
The ratio of outer diameter to inner diameter.

## Slide 67
G5C01 What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding? voltage source is connected across its primary ?
Capacitive coupling
Displacement current coupling
Mutual inductance
Mutual capacitance

## Slide 68: G5C06 What is the voltage output of a transformer with a 500-turn primary and a 1500-turn secondary when 120 VAC is applied to the primary? s connected to 120 VAC?
360 volts.
120 volts.
40 volts.
25.5 volts.

## Slide 69
G5C02 What is the output voltage if an input signal is applied to the secondary winding of a 4:1 voltage step-down transformer instead of the primary winding?
The input voltage is multiplied by 4.
The input voltage is divided by 4.
Additional resistance must be added in series with the primary to prevent overload.
Additional resistance must be added in parallel with the secondary to prevent overload.

## Slide 70
G5C07 What transformer turns ratio matches an antenna’s 600-ohm feed point impedance to a 50-ohm coaxial cable? impedance to a speaker having a 4-ohm impedance?
3.5 to 1.
12 to 1.
24 to 1.
144 to 1.

## Slide 71
71
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 72: Thank You!