## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2024 ARRL
All Rights Reserved

## Slide 2
2
General Course
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 3: Good Grounds

## Slide 4
General Licensing Class
Good Grounds
Question Pool valid
July 1st, 2023 Through June 30th, 2027
Notes: 4

## Slide 5
5
Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 - Voice Operations
  6 - CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement

## Slide 6
ELEMENT 3 SUB-ELEMENTS (Groupings)
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 -HF Antennas
  17 - Coax Cable
  18 -RF & Electrical Safety
Amateur Radio General Class Element 3 Course Presentation

## Slide 7: Good Grounds
If you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod, the ground wire has high impedance on that frequency. (G4C05)
    This is because at some frequencies the ground wire is inductive and may become resonant at some frequencies.
    Using a lower inductance ground wire will reduce this problem.
    Could be a ¼ wavelength and a good antenna.
Parts for grounding.
5

## Slide 8: Good Grounds
Symptoms of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver can be caused by: (G4A15)
    The VOX circuit does not un-key the transmitter.
    The transmitter signal is distorted.
    Frequent connection timeouts.
    All these choices are correct.
        The RF signal is being rectified into an audio signal,
        which modulates the transmitter and feeds back again as RF,
        turning the whole transmitter into a kind of oscillator.
6

## Slide 9: Good Grounds
Connect all ground conductors to a single point to avoid a ground loop. (G4C09)
If you receive reports of "hum" on your station's transmitted signal, this could be a symptom of a ground loop somewhere in your station. (G4C10)
Ground straps
7

## Slide 10: Good Grounds
  All metal enclosures of every item of station equipment should be grounded to ensure hazardous voltages cannot appear on the chassis. (G4C13)
  A resonant ground connection could cause high RF voltages on the enclosures of station equipment. (G4C06)
            Keep the station's ground wire as short as possible.
            Good way to avoid stray RF energy in an amateur station.
TRANSCEIVER
POWER SUPPLY
ANTENNA SWITCH
HEAVY GAUGE COPPER BRAID
HEAVY GAUGE COPPER BRAID
COPPER PIPE
COPPER GROUND ROD
8

## Slide 11
Bypass capacitors might be useful in reducing RF interference to audio-frequency devices. (G4C01)
Placing a ferrite bead around the cable would reduce RF interference caused by common-mode current on an audio cable. (G4C08)
Good Grounds
For an AC signal, the capacitor performs short and bypasses it.
The DC gone through the capacitor behaves as an open for DC.

## Slide 12
Distorted speech is heard from an audio device or telephone if there is interference from a nearby single-sideband phone transmitter. (G4C03)
    Am and CB transmissions will come through loud and clear.
On-and-off humming or clicking is one effect that a nearby CW transmitter may have on an audio device or telephone system. (G4C04)
Arcing at a poor electrical connection could be a cause of interference covering a wide range of frequencies. (G4C02)
    Regularly check and tighten up connections on your ham equipment. (and your homes.)
Good Grounds
Electrical outlet melted.
Many Code violations.
Loose electrical connection.

## Slide 13: Good Grounds
Receive interference in a radio installed in a vehicle may be caused by: (G4E07)
    The battery charging system.
    The fuel delivery system.
    The vehicle control system.
    All these choices are correct.
          A steady, raspy carrier that only disappears with engine off. (vehicle computer)
          Whistle sound that changes pitch with engine rev. (alternator)
          Ticking sounds all over band. (electric fuel pump)
11

## Slide 14
Element 3 General Class Question Pool
Good Grounds

## Slide 15
G4C05 What is a possible cause of high voltages that produce RF burns?
Flat braid rather than round wire has been used for the ground wire.
Insulated wire has been used for the ground wire.
The ground rod is resonant.
The ground wire has high impedance on that frequency.

## Slide 16: G4A15 Which of the following can be a syptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver?
The VOX circuit does not un-key the transmitter.
The transmitter signal is distorted.
Frequent connection timeouts.
All of these choices are correct.
14

## Slide 17
G4C09 How can the effects of ground loops be minimized?
Connect all ground conductors in series.
Connect the AC neutral conductor to the ground wire.
Avoid using lock washers and star washers when making ground connections.
Connect all ground conductors to a single point.

## Slide 18
G4C10 What could be a symptom caused by a ground loop in your station’s audio connections?
You receive reports of “hum” on your station’s transmitted signal.
The SWR reading for one or more antennas is suddenly very high.
An item of station equipment starts to draw excessive amounts of current.
You receive reports of harmonic interference from your station.

## Slide 19
G4C13 Why must the metal enclosure of every item of station equipment be grounded?
It prevents a blown fuse in the event of an internal short.
It prevents signal overload.
It ensures the neutral wire is grounded.
It ensures that hazardous voltages cannot appear on the chassis.

## Slide 20
G4C06 What is a possible effect of a resonant ground connection?
Overheating of ground straps.
Corrosion of the ground rod.
High RF voltages on the enclosures of station equipment.
A ground loop.

## Slide 21
G4C01 Which of the following might be useful in reducing RF interference to audio frequency circuits?
Bypass inductor.
Bypass capacitor.
Forward-biased diode.
Reverse-biased diode.
19

## Slide 22
G4C08 Which of the following would reduce RF interference caused by common-mode on an audio cable?
Placing a ferrite choke around the cable.
Adding series capacitors to the conductors.
Adding shunt inductors to the conductors.
Adding an additional insulating jacket to the cable.

## Slide 23
G4C03 What sound is heard from an audio device experiencing RF interference from a single sideband phone transmitter? phone transmitter?
A steady hum whenever the transmitter is on the air.
On-and-off humming or clicking.
Distorted speech.
Clearly audible speech.

## Slide 24
G4C04 What sound is heard from an audio device experiencing RF interference from a CW transmitter? from a nearby CW transmitter?
On-and-off humming or clicking.
A CW signal at a nearly pure audio frequency.
A chirpy CW signal.
Severely distorted audio.

## Slide 25
G4C02 Which of the following could be a cause of interference covering a wide range of frequencies?
Not using a balun or line isolator to feed balanced antennas.
Lack of rectification of the transmitter's signal in power conductors.
Arcing at a poor electrical connection.
Using a balun to feed an unbalanced antenna.

## Slide 26: G4E07 Which of the following may cause receive interference to an HF transceiver installed in a vehicle?
The battery charging system.
The fuel delivery system.
The control computer.
All of these choices are correct.
24

## Slide 27
27
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 28: Thank You!