## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: Chapter 2 Section XX
Your New General Bands
Question Pool valid
July 1st, 2023 Through June 30th, 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 -Your Passing CSCE
  2 -Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 - Voice Operations
  6 - CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement

## Slide 6: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 - Coax Cable
  18 - RF & Electrical Safety

## Slide 7: Your New General Bands
General class control operator frequency privileges
  A General Class license holder is granted all amateur frequency privileges on the following: (G1A01)
    CW, RTTY, data, phone, and image
160
60
30
17
12
10
Meters

## Slide 8: Your New General Bands
General class control operator frequency privileges (cont)
  A General Class license holder is granted all amateur frequency privileges on the following: (G1A01)
    CW, RTTY, data, phone, and image
160
60
30
17
12
10
Meters
5330.5 kHz
5346.5 kHz
5357.0 kHz
5371.5 kHz
5403.5 kHz

## Slide 9: Your New General Bands
General class control operator frequency privileges (cont)
  A General Class license holder is granted all amateur frequency privileges on the following: (G1A01)
    CW, RTTY, and Data
160
60
30
17
12
10
Meters

## Slide 10: Your New General Bands
General class control operator frequency privileges (cont)
  A General Class license holder is granted all amateur frequency privileges on the following: (G1A01)
    CW, RTTY, data, phone, and image
160
60
30
17
12
10
Meters

## Slide 11: Your New General Bands
General class control operator frequency privileges (cont)
  A General Class license holder is granted all amateur frequency privileges on the following: (G1A01)
    CW, RTTY, data, phone, and image
160
60
30
17
12
10
Meters

## Slide 12: Your New General Bands
General class control operator frequency privileges (cont)
  A General Class license holder is granted all amateur frequency privileges on the following: (G1A01)
    CW, RTTY, data, phone, and image
160
60
30
17
12
10
Meters

## Slide 13: Your New General Bands
General class control operator frequency privileges (cont)
    (Recap)
  A General Class license holder is granted all amateur frequency privileges on the following: (G1A01)
      160-meters
      60-meters
      30-meters
      17-meters
      12-meters
      10-meters
    All of these bands…..all privileges for General.
(answer is six bands)

## Slide 14: Your New General Bands
General class control operator frequency privileges
  The following frequencies are available to a control operator holding a General Class license: (G1A10)
28.020 MHz
28.350 MHz
28.550 MHz
28.020
28.350
28.550
All of these answers are correct

## Slide 15: Your New General Bands
General class control operator frequency privileges
  The upper 200kHz of the 10-meter band, beginning at 29.5MHz is available for repeater operation. (G1A15)

## Slide 16: Your New General Bands
The maximum transmitting power a station with a General Class control operator may use on the 28 MHz band (10-Meter Band) is 1500 watts PEP output. (G1C05)
A 10 meter repeater may retransmit a 2-meter signal from a Technician, ONLY if there is an active duty control operator holding a General Class or higher. (G1E02)

## Slide 17: Your New General Bands
The maximum transmitting power an amateur station may use on the Amateur Radio12-meter band is 1500 watts PEP output. (G1C02)
CW, RTTY and data … CW, phone and image

## Slide 18: Your New General Bands
General class control operator frequency privileges
  The 21,300 kHz frequency is within the General class portion of the 15-meter phone band. (G1A09)
CW, RTTY, data, phone and image
21,300 kHz

## Slide 19: Your New General Bands
General class control operator frequency privileges
  The 14,305 kHz frequency is within the General class portion of the 20-meter phone band. (G1A07)
CW, RTTY, phone, image, and data …
14,305 kHz

## Slide 20: Your New General Bands
  The power output limitation on the 14 MHz band is the minimum power necessary to carry out the desired communications. (G1C04)
  [Technically this applies to ALL transmissions by an Amateur Radio operator]
  The measurement specified by the FCC rules that regulate maximum power output is PEP, or Peak Envelope Power. (G1C15)
  Phone operation is prohibited on the 30-meter band. (G1A02) A N D
  Image transmission is prohibited on the 30-meter band. (G1A03)
CW, RTTY and data

## Slide 21: Your New General Bands
  The maximum transmitting power an amateur station may use on 10.140 MHz is 200 watts PEP output. (G1C01)
CW, RTTY and data
10.140 MHz

## Slide 22: Your New General Bands
CW, RTTY and data … CW, phone and image
General class control operator frequency privileges
  7.250 MHz frequency is in the General Class portion of the 40-meter band. (G1A05)
7250 kHz

## Slide 23: Your New General Bands
The frequency allocations of ITU region 2 apply to radio amateurs operating in North and South America.(G1E06)
Under FCC jurisdiction outside of ITU Region 2, frequency allocations may differ. (G1A14)

## Slide 24: Your New General Bands+
60-meters is the only band with restricted communications on specific channels rather than frequency ranges. (G1A04)
  Five discreet, upper sideband voice channels
  No Morse code and no data transmissions
5357.0 kHz
5371.5 kHz
5346.5 kHz
5330.5 kHz
5403.5 kHz

## Slide 25: Your New General Bands
2.8 kHz is the maximum bandwidth permitted by FCC rules for Amateur Radio stations transmitting on USB frequencies in the 60-meter band. (G1C03)
    Only Upper Sideband
    Turn off speech processor to prevent exceeding 2.8 kHz
The maximum power limit on the 60-meter band is ERP of 100 watts PEP with respect to a dipole. (G1C14)
    Limitations on effective radiated power (ERP) rather than transmitter power.
FCC rules require records be kept of the gain of your antenna on the 60-meter band if your antenna is other than a dipole. (G1C12)
  Dipole gain is zero;
  Must not exceed 50 watts effective radiated power output.
  Notes kept in station logbook as permanent record

## Slide 26: Your New General Bands
Move to a clear frequency when operating on 30-meters or 60-meters if a station in the primary service interferes with your contact. (G1A13)
        Secondary users do not have priority use
FCC rules designate Amateur Service as a secondary user on certain bands, as such amateur stations are permitted to use such bands only if there is no harmful interference to primary users. (G1A12)
        Primary users have priority use
A frequency of 3,900 kHz is within the General Class portion of the 75-meter band. (G1A06)
3.900 MHz
Notice areas where there are no privileges for General Class.
Generally on this band:
phone operation is called 75 meters; CW operation is called 80 meters.

## Slide 27: Your New General Bands
General class control operator frequency privileges
  3560 kHz frequency is within the General class portion of the 80-meter band. (G1A08)
CW, RTTY, phone, and data …
3560 kHz

## Slide 28: Your New General Bands
General class control operator frequency privileges
  A General Class license holder is permitted to run up to 1500 watts of Peak Envelope Power on the 1.8 MHz band. (G1C06)
  1500 watts on all bands except 60-meters and-30 meters.
  However, always run the minimum power necessary.
    CW, RTTY, data, phone, and image

## Slide 29: Your New General Bands
General class control operator frequency privileges
  When a General Class licensee is not permitted to use the entire voice portion of a particular band, the upper frequency end or portion of the voice segment is generally available to them. (G1A11)

## Slide 30: Your New General Bands
Voice privileges are usually at the top end of the band….except for 60 meters which has specific 5 channels of voice.
The 50.1 to 50.125 MHz band segment is used in a voluntary basis called the “DX window” and should not be used for stateside U.S. contacts when transmitting in the 48 contiguous states. (G2B08))

## Slide 31: G1A01 On which HF and/or MF amateur bands are there portions where General class licensees cannot transmit?
  A. 60 meters, 30 meters, 17 meters, and 12 meters
  B. 160 meters, 60 meters, 15 meters, and 12 meters
  C. 80 meters, 40 meters, 20 meters, and 15 meters
  D. 80 meters, 20 meters, 15 meters, and 10 meters

## Slide 32: G1A08 Which HF bands have segments exclusively allocated to Amateur Extra licensees?
  All HF bands
  B. 80 meters, 40 meters, 20 meters, and 15 meters
  C. All HF bands except 160 meters and 10 meters
  D. 60 meters, 30 meters, 17 meters, and 12 meters

## Slide 33: G1A11 When General class licensees are not permitted to use the entire voice portion of a band, which portion of the voice segment is available to them??
The lower frequency portion
The upper frequency portion
The lower frequency portion on frequencies below 7.3 MHz, and the upper portion on frequencies above 14.150 MHz
The upper frequency portion on frequencies below 7.3 MHz, and the lower portion on frequencies above 14.150 MHz

## Slide 34: G1A07 On which amateur frequencies in the 10-meter band may stations with a General class control operator transmit CW emissions?
28.000 MHz to 28.025 MHz only
28.000 MHz to 28.300 MHz only
28.025 MHz to 28.300 MHz only
The entire band

## Slide 35: G1A10 What portion of the 10-meter band is available for repeater use?
A. The entire band
B. The portion between 28.1 MHz and 28.2 MHz
C. The portion between 28.3 MHz and 28.5 MHz
D. The portion above 29.5 MHz

## Slide 36: G1C05 What is the limit for transmitter power on the 28 MHz band for a General Class control operator?
100 watts PEP output
1000 watts PEP output
1500 watts PEP output
2000 watts PEP output

## Slide 37
Under no circumstances.
Only if the station on 10 meters is operating under a Special Temporary Authorization allowing such retransmission.
Only during an FCC-declared general state of communications emergency.
Only if the 10-meter control operator holds at least a General class license.
G1E02 When may a 10-meter repeater retransmit the 2-meter signal from a station having a Technician Class control operator?

## Slide 38
50 watts PEP output.
200 watts PEP output.
1500 watts PEP output.
An effective radiated power equivalent to 100 watts from a half-wave dipole.
G1C02 What is the maximum transmitting power an amateur station may use on the 12 meter band?

## Slide 39
14250 kHz.
18155 kHz.
21300 kHz.
24900 kHz.
G1A09 Which of the following frequencies is within the General Class portion of the 15-meter band?

## Slide 40
160-meters. ​
30-meters. ​
17-meters.​
12-meters.
G1A02 On which of the following bands is phone operation prohibited?

## Slide 41
160-meters. ​
30-meters. ​
20-meters.​
12-meters.
G1A03 On which of the following bands is image transmisison prohibited?

## Slide 42
7.125 MHz to 7.175 MHz
28.000 MHz to 28.025 MHz
21.275 MHz to 21.300 MHz
All of the above
G1A05 Which of the following frequencies is in the General Class licensees prohibited operating as a control operator

## Slide 43
200 watts PEP output. ​
1000 watts PEP output. ​
1500 watts PEP output.​
2000 watts PEP output.
G1C01 What is the maximum transmitting power an amateur station may use on 10.140 MHz?

## Slide 44
11-meters.
12-meters.
30-meters.
60-meters.
G1A04 Which of the following amateur bands is restricted to communication only on specific channels, rather than frequency ranges?

## Slide 45
2.8 kHz.
5.6 kHz.
1.8kHz.
3kHz.
G1C03 What is the maximum bandwidth permitted by FCC rules for Amateur Radio stations transmitting on USB frequencies in the 60-meter band?

## Slide 46: G1C09 What is the maximum power limit on the 60-meter band?
1500 watts PEP.
10 watts RMS.
ERP of 100 watts PEP with respect to a dipole.
ERP of 100 watts PEP with respect to an isotropic antenna

## Slide 47
Only the minimum power necessary to carry out the desired communications should be used.
Power must be limited to 200 watts when using data transmissions.
Power should be limited as necessary to avoid interference to another radio service on the frequency.
Effective radiated power cannot exceed 1500 watts.
G1C04 Which of the following limitations apply to transmitter power on every amateur band?

## Slide 48
A. Amateur stations must record the call sign of the primary service station before operating on a frequency assigned to that station
B. Amateur stations may use the band only during emergencies
C. Amateur stations must not cause harmful interference to primary users and must accept interference from primary users
D. Amateur stations may only operate during specific hours of the day, while primary users are permitted 24-hour use of the band
GA106 Which of the following applies when the FCC rules designate the amateur service as a secondary user on a band?

## Slide 49: G1C06 Which of the following is a limitation on transmitting power on the 1.8 MHz band?
200 watts PEP output.
1000 watts PEP output.
1200 watts PEP output.
1500 watts PEP output.

## Slide 50: Thank You!
Add content here or remove