## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: Chapter 5
Voice Operation
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 - Voice Operations
  6 - CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement

## Slide 6: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 7: Voice Operation
A practical way to avoid harmful interference when selecting a frequency to call CQ on CW or phone is to send "QRL?" on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign. (G2B06)
To comply with good amateur practice when choosing a frequency on which to initiate a call, follow the voluntary band plan for the operating mode you intend to use. (G2B07)
No amateur station has priority access to any frequency, except during emergencies, common courtesy should be a guide. (G2B01)
  Except during emergencies, no amateur station has priority access to any frequency.
The recommended way to break into a conversation when using phone is to say your call once sign during a break between transmissions from the other stations. (G2A08)

## Slide 8: Voice Operation
A good way to indicate on a clear frequency in the HF phone bands that you are looking for a contact with any station is to repeat “CQ” a few times, followed by “this is” and then your call sign a few times. Pause to listen, repeat if necessary. (G2D05)
When the expression "CQ DX" is heard from a station in the contiguous 48 states, The caller is looking for any station outside the lower 48 states. (G2A11)
A DX station like this one, on top of a hill, will enjoy some great contacts world wide.

## Slide 9: Voice Operation
      HF/VHF/UHF All Mode Transceiver YAESU FT-991
VFO A
VFO B
When participating in a contest on HF frequencies, identify your station per normal FCC regulations. (G2D09)
Operating a transceiver in "split" mode means that the transceiver is set to different transmit and receive frequencies. (G4A03)

## Slide 10: Voice Operation
A common use for the dual VFO feature on a transceiver is to permit ease of monitoring the transmit and receive frequencies when they are not the same. (G4A12)
If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, attempt to resolve the interference problem with the other station in a mutually acceptable manner. (G2B03)
The customary minimum frequency separation between SSB signals under normal conditions is approximately 3 kHz. (G2B05)

## Slide 11: Voice Operation
When operating in the 40 meter General Class phone segment when using 3 kHz wide LSB, your displayed carrier frequency should be 3 kHz above the edge of the segment. (G4D10)
When the displayed carrier frequency is set to 7.178 MHz, a 3 kHz LSB signal occupies 7.175 to 7.178 MHz. (G4D08)
Your displayed carrier frequency should be no less than 3 kHz below the edge of the band when using 3 kHz wide USB. (G4D11)
With the displayed carrier frequency set to 14.347 MHz, a 3 kHz USB signal occupies 14.347 to 14.350 MHz. (G4D09)
  When operating USB, your signal occupies a space starting at the displayed carrier frequency and extending up 3 kHz.

## Slide 12: Voice Operation
One use for the IF shift control on a receiver is to avoid interference from stations very close to the receive frequency. (G4A11)
QRP operation refers to low power transmit operation. (G2D10)
VOX allows "hands free" operation. (G2A10)
  When operating SSB, many amateurs like to use the VOX, or voice-operated control, feature of their transceivers.
Using a headset with an attached mike on VOX will keep both hands free when you’re taking on the worldwide bands while at your home station.

## Slide 13: Voice Operation
Conditions that require an Amateur Radio station to take specific steps to avoid harmful interference to other users or facilities: (G1E04)
    When operating within one mile of an FCC Monitoring Station.
    When using a band where the Amateur Service is secondary.
    When a station is transmitting spread spectrum emissions.
    [All of these choices are correct]
Single sideband is the mode of voice communication most commonly used on the high frequency amateur bands. (G2A05)

## Slide 14: Voice Operation
Because only one sideband is transmitted, less bandwidth used and higher power efficiency is an advantage when using single sideband as compared to other analog voice modes on the HF amateur bands. (G2A06)
Frequency 
Frequency in kHz
SSB signals are Amplitude Modulated (AM) with the carrier and one sideband suppressed.

## Slide 15: Voice Operation
When using single sideband (SSB) voice mode, only one sideband is transmitted; the other sideband and carrier are suppressed. (G2A07)
Accordingly, upper sideband is most commonly used for voice communications on the 17 and 12 meter bands (G2A04)
Upper sideband is the sideband most commonly used for voice communications on frequencies of 14 MHz or higher. (G2A01)
      Make sure you use the correct sideband

## Slide 16: Voice Operation
Lower sideband is the mode most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands. (G2A02)
The reason most amateur stations use lower sideband on the 160-meter, 75-meter and 40-meter bands is that current amateur practice is to use lower sideband on these frequency bands. (G2A09)
Upper sideband is most commonly used for SSB voice communications in the VHF and UHF bands. (G2A03)
Modern HF transceivers automatically select the correct sideband, a feature that lets General Class operators really enjoy field day.

## Slide 17: Voice Operation
Alpha, Bravo, Charlie, and Delta are examples of the NATO Phonetic Alphabet. (G2D07)
Recap of which sideband is used on which bands.
Sideband Usage on Amateur Radio Bands

## Slide 18: Element 3 General Class Question Pool
Voice Operation
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 19: G2B06 What is a practical way to avoid harmful interference on an apparently clear frequency before calling CQ on CW or phone?
Send “QRL?” on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign.
Listen for 2 minutes before calling CQ.
Send the letter “V” in Morse code several times and listen for a response.
Send “QSY” on CW or if using phone announce “the frequency is in use,” then send your call and listen for a response.

## Slide 20: G2B07 Which of the following complies with good amateur practice when choosing a frequency on which to initiate a call?
Check to see if the channel is assigned to another station.
Identify your station by transmitting your call sign at least 3 times.
Follow your voluntary band plan for the operating mode you intend to use.
All of these choices are correct.

## Slide 21: G2B01 Which of the following is true concerning access to frequencies?
Nets always have priority.
QSO’s in process always have priority.
Except during emergencies, no amateur station has priority access to any frequency.
Contest operations must always yield to non-contest use of frequencies.

## Slide 22: G2A08 What is the recommended way to break into a phone contact?
Say "QRZ" several times followed by your call sign.
Say your call sign once.
Say "Breaker Breaker."
Say "CQ" followed by the call sign of either station.

## Slide 23: G2D11 Why are signal reports typically exchanged at the beginning of an HF contact? ? looking for a contact with any stations?
A. To allow each station to operate according to conditions
B. To be sure the contact will count for award programs
C. To follow standard radiogram structure
D. To allow each station to calibrate their frequency display

## Slide 24: G2D05 Which if the following is a good way to G2D05 Which of the following indicates that you are looking for an HF contact with any station? looking for a contact with any stations?
A. Sign your call sign once, followed by the words “listening for a call” -- if no answer, change frequency and repeat
B. Say “QTC” followed by “this is” and your call sign -- if no answer, change frequency and repeat
C. Repeat “CQ” a few times, followed by “this is,” then your call sign a few times, then pause to listen, repeat as necessary
D. Transmit an unmodulated carried for approximately 10 seconds, followed by “this is” and your call sign, and pause to listen -- repeat as necessary

## Slide 25: G2A11 Generally, who should respond to a station in the contiguous 48 states who calls “CQ DX”?
Any caller is welcome to respond.
Only stations in Germany.
Any stations outside the lower 48 states.
Only contest stations.

## Slide 26: G2B08 What is the voluntary band plan restriction for US stations transmitting within the 48 contiguous states in the 50.1 MHz to 50.125 MHz band segment?
Only contacts with stations not within the 48 contiguous states
Only contacts with other stations within the 48 contiguous states
Only digital contacts
Only SSTV contacts

## Slide 27: G2D09 Which of the following is required when participating in a contest on HF frequencies?
Submit a log to the contest sponsor.
Send a QSL card to the stations worked, or QSL via Logbook of The World.
Identify your station per normal FCC regulations.
All these choices are correct.

## Slide 28: G4A12 Which of the following is a common use for the dual-VFO feature on a transceiver?
To allow transmitting on two frequencies at once.
To permit full duplex operation, -- that is, transmitting and receiving at the same time.
To permit monitoring of two different frequencies.
To facilitate computer interface.

## Slide 29: G2B03 What is good amateur practice if propagation changes during a contact and you notice interference from other stations on the frequency?
Tell the interfering stations to change frequency.
Report the interference to your local Amateur Auxiliary Coordinator.
Attempt to resolve the interference problem with the other stations in a mutually acceptable manner.
Increase power to overcome interference.

## Slide 30: G2B05 When selecting an SSB transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies?
5 to 50 Hz.
150 to 500 Hz.
Approximately 3 kHz.
Approximately 6 kHz.

## Slide 31: G4D10 How close to the lower edge of the phone segment should your displayed carrier frequency be when using 3 kHz wide LSB?
At least 3 kHz above the edge of the segment.
At least 3 kHz below the edge of the segment.
At least 1 kHz below the edge of the segment.
At least 1 kHz above the edge of the segment.

## Slide 32: G4D08 What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz?
7.178 to 7.181 MHz.
7.178 to 7.184 MHz.
7.175 to 7.178 MHz.
7.1765 to 7.1795 MHz.

## Slide 33: G4D11 How close to the upper edge of the phone segment should your displayed carrier frequency be when using a 3 kHz wide USB?
At least 3 kHz above the edge of the band.
At least 3 kHz below the edge of the band.
At least 1 kHz above the edge of the band.
At least 1 kHz below the edge of the band.

## Slide 34: G4D09 What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz?
14.347 to 14.647 MHz.
14.347 to 14.350 MHz.
14.344 to 14.347 MHz.
14.3455 to 14.3485 MHz.

## Slide 35: G2D10 What is QRP operation?
Remote piloted model control.
Low-power transmit operation.
Transmission using Quick Response Protocol.
Traffic relay procedure net operation.

## Slide 36: G2A10 Which of the following statements is true of voice VOX operation versus PTT operation?
The received signal is more natural sounding.
It allows "hands free" operation.
It occupies less bandwidth.
It provides more power output.

## Slide 37: G1E04 Which of the following conditions require a licensed Amateur radio operator to take specific steps to avoid harmful interference to other users or facilities?
When operating within one mile of an FCC Monitoring Station.
When using a band where the Amateur Service is secondary.
When a station is transmitting spread spectrum emissions.
All of these choices are correct.

## Slide 38: G2A05 Which mode of voice communication is most commonly used on the HF frequency amateur bands?
Frequency Modulation.
Double sideband.
Single sideband.
Phase modulation.

## Slide 39: G2A06 Which of the following is an advantage when using single sideband as compared to other analog voice modes on the HF amateur bands?
Very high fidelity voice modulation.
Less subject to interference from atmospheric static crashes.
Ease of tuning on receive and immunity to impulse noise.
Less bandwidth used and greater power efficiency.

## Slide 40: G2A07 Which of the following statements is true of the single sideband voice mode?
Only one sideband and the carrier are transmitted; the other sideband is suppressed.
Only one sideband is transmitted; the other sideband and carrier are suppressed.
SSB is the only voice mode that is authorized on the 20-meter, 15-meter, and 10-meter amateur bands.
SSB is the only mode that is authorized on the 160-meter, 75-meter, and 40-meter amateur bands.

## Slide 41: G2A04 Which mode is most commonly used for voice communications on the 17-meter and 12-meter bands?
Upper sideband.
Lower sideband.
Vestigial sideband.
Double sideband.

## Slide 42: G2A01 Which sideband is most commonly used for phone communications on frequencies of 14 MHz or higher?
Upper sideband.
Lower sideband.
Vestigial sideband.
Double sideband.

## Slide 43: G2A03 Which of the following is the most commonly used SSB voice communications in the VHF and UHF bands?
Upper sideband.
Lower sideband.
Vestigial sideband.
Double sideband.

## Slide 44: G2A02 Which of the following modes is most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands?
Upper sideband.
Lower sideband.
Vestigial sideband.
Double sideband.

## Slide 45: G2D09 Why do most amateur stations use lower sideband on the 160-meter, 75-meter, and 40- meter bands?
Lower sideband is more efficient than upper sideband on these frequencies.
Lower sideband is the only sideband legal on these frequencies.
Because it is fully compatible with an AM detector.
It is good amateur practice.

## Slide 46: G2D07 Which of the following are examples of the NATO Phonetic Alphabet?
Able, Baker, Charlie, Dog.
Adam, Boy, Charles, David.
America, Boston, Canada, Denmark.
Alpha, Bravo, Charlie, Delta.

## Slide 47: Thank You!

## Slide 49: G4A11 Which of the following is a use for the IF shift control on a receiver?
To avoid interference from stations very close to the receive frequency.
To change frequency rapidly.
To permit listening on a different frequency from that on which you are transmitting.
To tune in stations that are slightly off frequency without changing your transmit frequency.