## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: CW Lives

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: Chapter 6
CW Lives
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 - CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement

## Slide 6: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 7: CW Lives
When selecting a CW transmitting frequency, 150 to 500 Hz is the minimum frequency separation you should allow in order to minimize interference to stations on adjacent frequencies. (G2B04)
The term “zero beat” in CW operation means matching your transmit frequency to the frequency of a received signal. (G2C06)
The best speed to use answering a CQ in Morse Code is the speed at which the CQ was sent. (G2C05)
    which should be the fastest speed you’re comfortable copying
When sending CW, a “C” added to the RST report means a chirpy or unstable signal. (G2C07)
RST stands for Readability … Signal Strength … Tone

## Slide 8: CW Lives
READABILITY (R) for Voice + CW
1 – Unreadable
2 – Barely readable, occasional
words distinguishable
3 – Readable with considerable
difficulty
4 – Readable with practically
no difficulty
5 – Perfectly readable
No exam questions on these items.

## Slide 9: CW Lives
SIGNAL STRENGTH (S) for Voice + CW
1 – Faint, barely perceptible signals
2 – Very weak signals
3 – Weak signals
4 – Fair signals
5 – Fairly good signals
6 – Good signals
7 – Moderately strong signals
8 – Strong signals
9 – Extremely strong signals
No exam questions on these items.

## Slide 10: CW Lives
Tone (T) Use on CW only
1 – Very rough, broad signals, 60 cycle AC may be present
2 – Very rough AC tone, harsh, broad
3 – Rough AC tone, rectified but not filtered
4 – Rough note, some trace of filtering
5 – Filtered rectified AC but strongly ripple-modulated
6 – Filtered tone, definite trace of ripple modulation
7 – Near pure tone, trace of ripple modulation
8 – Near perfect tone, slight trace of modulation
9 – Perfect tone, no trace of ripple or modulation of any kind
No exam questions on these items.

## Slide 11
Q signals are three letter combinations that begin with the letter ‘Q’
  If a CW station sends "QRS", send slower. (G2C02)
  The Q signal “QRL” means “are you busy?” or “Is this frequency in use?”(G2C04)
  The Q signal "QRN" means “I am troubled by static.” (G2C10)
  The Q signal “QRV” means, “I am ready to receive messages.” (G2C11)
  The Q signal "QSL" means, “I acknowledge receipt.” (G2C09)
Q signals always begin with the letter ‘Q’ and only have three letters.
CW Lives

## Slide 12
CW Lives
QRS
QTH
QRT
QRL
QRN
QRM
QRV
QRZ
QSL
QSY
Send more slowly ( ___ WPM)
My location is ….
I am busy.
Stop sending..
I am troubled with static.
Your transmission is being interfered with.
I am ready.
Who is calling me?
I am acknowledging receipt.
Change to another frequency.
These five are the only ones that may be on the exam.
10
CW Lives

## Slide 13: CW Lives
When a CW operator sends "KN" at the end of a transmission, it means the operator is listening only for a specific station or stations. (G2C03)
This is called a ‘prosign’ and is used on CW only.
AR is the prosign that is sent to indicate the end of a formal message when using CW. (G2C08)
CW Lives
Newer HF rigs have the electronic keyer built in. Older radios can take an external CW keyer box.
The purpose of an electronic keyer, for example, is automatic generation of strings of dots and dashes for CW operation. (G4A10)

## Slide 14: CW Lives
When using full break-in telegraphy (QSK), transmitting stations can receive between code characters and elements. (G2C01)
Icom 7300 has full break-in telegraphy (QSK).
CW Lives

## Slide 15
Observation of propagation and reception is a purpose of a beacon station as identified in the FCC Rules. (G1B03)
100 watts PEP output is the power limit for beacon stations. (G1B10)
CW Lives

## Slide 16: CW Lives
One of the conditions with which beacon stations must comply is that there must be no more than one beacon signal in the same band from a single location.(G1B02)
Slot Country Call 14.100 18.110 21.150 24.930 28.200 Operator
1 United Nations 4U1UN 00:00 00:10 00:20 00:30 00:40 UNRC
2 Canada VE8AT 00:10 00:20 00:30 00:40 00:50 RAC
3 USA W6WX 00:20 00:30 00:40 00:50 01:00 NCDXF
4 Hawaii KH6WO 00:30 00:40 00:50 01:00 01:10 UHRO
5 New Zealand ZL 00:40 00:50 01:00 01:10 01:20 NZART
6 Australia VK8 00:50 01:00 01:10 01:20 01:30 W1A
7 Japan JA21CY 01:00 01:10 01:20 01:30 01:40 JARL
8 China BY 01:10 01:20 01:30 01:40 01:50 CRSA
9 Russia UA 01:20 01:30 01:40 01:50 02:00 TBO
10 Sri Lanka 4S7B 01:30 01:40 01:50 02:00 02:10 RSSL
11 South Africa ZS6DN 01:40 01:50 02:00 02:10 02:20 ZS6DN
12 Kenya 5Z4B 01:50 02:00 02:10 02:20 02:30 RSK
13 Israel 4X6TU 02:00 02:10 02:20 02:30 02:40 U of Tel Aviv
14 Finland OH2B 02:10 02:20 02:30 02:40 02:50 U oh Helsinki
15 Madeira CS3B 02:20 02:30 02:40 02:50 00:00 ARRM
16 Argentina LU4AA 02:30 02:40 02:50 00:00 00:10 RCA
17 Peru OA4B 02:40 02:50 00:00 00:10 00:20 RCP
18 Venezuela YV5B 02:50 00:00 00:10 00:20 00:30 RCV
Radio Beacon Stations
The 10-second, phase-3, message format is: “W6WX dah-dah-dah-dah” — each “dah” lasts a little more than one second. W6WX is transmitted at 100 watts, then each “dah” is attenuated in order, beginning at 100 watts, then 10 watts, then 1 watt, and finally 0.1 watt.

## Slide 17: CW Lives
On HF frequencies between 28.20 MHz to 28.30 KHz automatically controlled beacons are permitted. (G1B09)
An advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver is that it may be possible to reduce or eliminate interference from other signals. (G4A02)
It is good to match receiver bandwidth to the bandwidth of the operating mode because it results in the best signal to noise ratio. (G8B09)
About the CW Reverse mode
The CW-R (W Reverse mode reverses the receive Beat Frequency Oscillator (BFO) to receive CW signals.
Use when interfering signals are near the desired signal you want to use W-R to reduce interference.

## Slide 18: Element 3 General Class Question Pool
CW Lives
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 19: G2B04 When selecting a CW transmitting frequency, what separation should be used to minimize interference to stations on adjacent frequencies?
5 to 50 Hz.
150 to 500 Hz.
1 to 3 kHz.
3 to 6 kHz.
17

## Slide 20: G2C06 What does the term “zero beat” mean in CW operation?
Matching the speed of the transmitting station.
Operating split to avoid interference on frequency.
Sending without error.
Matching your transmit frequency of a received signal.
18

## Slide 21: G2C05 What is the best speed to use answering a CQ in Morse Code?
The fastest speed at which you are comfortable copying, but no slower than the CQ.
The fastest speed at which you are comfortable copying, but no faster than the CQ.
At the standard calling speed of 10 wpm.
At the standard calling speed of 5 wpm.

## Slide 22: G2CO7 When sending CW, what does a “C” mean when added to the RST report?
Chirpy or unstable signal.
Report was read from S meter reading rather than estimated.
100 percent copy.
Key clicks.
20

## Slide 23: G2C02 What should you do if a CW station sends "QRS"?
Send slower.
Change frequency.
Increase your power.
Repeat everything twice.
21

## Slide 24: G2C04 What does the Q signal “QRL” mean?
“Will you keep the frequency clear?”
“Are you operating full break-in? or “Can you operate full break-in?”
Are you listening only for a specific station?”
“Are you busy?” or “Is this frequency in use?”
22

## Slide 25: G2C10 What does the Q signal “QRN” mean?
Send more slowly.
Stop sending.
Zero beat my signal.
I am troubled by static.
23

## Slide 26: G2C11 What does the Q signal “QRV” mean?
You are sending too fast.
There is interference on the frequency.
I am quitting for the day.
I am ready to receive messages.
24

## Slide 27: G2C09 What does the Q signal "QSL" mean?
Send slower.
We have already confirmed by card.
I acknowledge receipt.
We have worked before.
25

## Slide 28: G2C03 What does it mean when a CW operator sends "KN" at the end of a transmission?
Listening for novice stations.
Operating full break-in.
Listening only for a specific station or stations.
Closing station now.
26

## Slide 29: G2C08 What prosign is sent to indicate the end of a formal message when using CW ?
SK.
BK.
AR.
KN.
27

## Slide 30: G4A10 What is the purpose of an electronic keyer?
Automatic transmit/receive switching.
Automatic generation of strings of dots and dashes for CW operation.
VOX operation.
Computer interface for PSK and RTTY operation.

## Slide 31: G2C01 Which of the following describes full break-in CW Operation (QSK)?
Breaking stations send the Morse code prosign “BK”.
Automatic keyers, instead of hand keys, are used to send More code.
An operator must activate a manual send/receive switch before and after every transmission.
Transmitting stations can receive between code characters and elements.
29

## Slide 32: G1B03 Which of the following is a purpose of a beacon station as identified in the FCC Rules?
Observation of propagation and reception.
Automatic Identification of Repeaters.
Transmission of bulletins of general interest to Amateur Radio licensees.
Identifying Net Frequencies.
30

## Slide 33: G1E10 Why should an amateur operator normally avoid transmitting on 14.100, 18.110, 21.150, 24.930 and 28.200 MHz?
A. A system of propagation beacon stations operates on those frequencies
B. A system of automatic digital stations operates on those frequencies
C. These frequencies are set aside for emergency operations
D. These frequencies are set aside for bulletins from the FCC
30

## Slide 34: G1B10 What is the power limit for beacon stations?
10 watts PEP output.
20 watts PEP output.
100 watts PEP output.
200 watts PEP output.
32

## Slide 35: G1B02 With which of the following conditions must beacon stations comply?
A beacon station may not use automatic control.
The frequency must be coordinated with the National Beacon Organization.
The frequency must be posted on the Internet or published in a national periodical.
There must be no more than one beacon signal transmitting in the same band from the same station location.
33

## Slide 36: G1B09 On what HF frequencies are automatically controlled beacons permitted?
On any frequency if power is less than 1 watt.
On any frequency if transmissions are in Morse code.
21.08 MHz to 21.09 MHz.
28.20 Mhz to 28.30 MHz.
34

## Slide 37: G4A02 What is one advantage of selecting the opposite or “reverse” sideband when receiving CW signals on a typical HF transceiver.
Interference from impulse noise will be eliminated.
More stations can be accommodated within a given signal passband.
It may be possible to reduce or eliminate interference from other signals.
Accidental out-of-band operation can be prevented.
35

## Slide 38: G8B09 Why is it good to match receiver bandwidth to the bandwidth of the operating mode?
It is required by FCC rules.
It minimizes power consumption in the receiver.
It improves impedance matching of the antenna.
It results in the best signal to noise ratio.
36

## Slide 39: Thank You!