## Slide 1
The following presentation and all materials provided are the intellectual property of The American Radio Relay League, Inc. (“ARRL”). No part of this presentation may be copied, recorded, reproduced, or distributed in any manner without express written permission from an authorized representative of the ARRL specifically referencing this presentation and material.
Copyright 2021 ARRL
All Rights Reserved

## Slide 2: General Licensing Course
MyFirstName MyLastName My arrl.net email address

## Slide 3
3
General Class
Notes: Right-click on photo to change photo. Consider using a black and white photo for impact.

## Slide 4: Chapter 7
Digital Operating​
Question Pool valid
July 1st, 2023 Through June 30th 2027
Notes: 4

## Slide 5: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  1 - Your Passing CSCE
  2 - Your New General Bands
  3 - FCC Rules
  4 - Be a VE
  5 Voice Operations
  6 CW Lives
  7 - Digital Operating
  8 - In An Emergency
  9 - Skywave Excitement

## Slide 6: Amateur Radio General Class Element 3 Course Presentation
ELEMENT 3 SUB-ELEMENTS (Groupings)
  10 - Your HF Transmitter
  11 - Your Receiver
  12 - Oscillators & Components
  13 - Electrical Principles
  14 - Circuits
  15 - Good Grounds
  16 - HF Antennas
  17 -Coax Cable
  18 - RF & Electrical Safety

## Slide 7: Digital Operating
14.070 - 14.112 MHz is the segment of the 20 meter band that is most often used for data transmissions. (G2E04)
3570 – 3600 kHz is the segment of the 80 meter band most commonly used for data transmissions. (G2E07)
Baudot code is a 5-bit code, with additional start and stop bits. (G8C04)
14.070 MHz
14.112 MHz
3600 kHz
3570 kHz

## Slide 8: Digital Operating
170 Hz is the most common frequency shift for RTTY emissions in the amateur HF bands. (G2E06)
Mark and Space define the two separate frequencies of a Frequency Shift Keyed (FSK) signal. (G8C11)
LSB is the mode normally used when sending an RTTY signal via AFSK with an SSB transmitter. (G2E01)
If you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly: (G2E14)
      The mark and space frequencies may be reversed.
      You may have selected the wrong baud rate.
      You may be listening on the wrong sideband.
          All of these choices are correct.

## Slide 9: Digital Operating
The standard sideband used to generate JT65, JT9, or FT8 digital signal when using AFSK in any amateur band is USB. (G2E05)
    This digital format modulation does not follow the normal upper or Lower SSB rule.
Below the RTTY segment, near 14.070 MHz is the segment of the 20 meter band where most PSK31 operations are commonly found. (G2E08)
Upper case letters use longer Varicode bit sequences and thus slow down transmission when using PSK31. (G8C08)
14.070 MHz

## Slide 10: Digital Operating
The standard waterfall display shows:
      Frequency is horizontal;
      Signal strength is intensity;
      Time is vertical; (G8C14)
Vertical lines on either side of a digital signal on a waterfall display indicates Overmodulation. (G8C13)

## Slide 11: Digital Operating
The number 31 in the term PSK31 represents the approximate transmitted symbol rate. (G8C09)
PSK31 uses a code known as Varicode for its different symbol lengths. (G8C12)
    Just like Morse Code more frequently used character are transmitted with shorter code to speed up communication.
Characteristics of QPSK31 are:
        It is sideband sensitive;
        Its encoding provides error correction;
        Its bandwidth is approximately the same as PBSK31. (G8A06)
All of these choices are correct.
Creating FSK signal is done by changing an oscillator’s frequency directly with a digital control signal. (G8A01)

## Slide 12: Digital Operating
The relationship between transmitted symbol and bandwidth is higher symbol rates require wider bandwidth. (G8B10)
  If you’re going to send fast, you’ll need to go to higher bands that will permit the faster sending speed and wider bandwidth.
300 baud is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz.(G1C08)
300 baud is the maximum symbol rate permitted for RTTY or data emission transmission on the 20 meter band.(G1C07)
1200 baud is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10 meter band.(G1C10)
19.6 kilobaud is the maximum symbol rate permitted for RTTY or data emission transmissions on the 2 meter band.(G1C11)
56 kilobaud is the maximum symbol rate permitted for RTTY or data emission transmitted on the 1.25 meter and 70 centimeter bands.(G1C09)

## Slide 13: Digital Operating
Recap of maximum speeds for RTTY.
The header is the part of a data packet that contains the routing and handling information. (G8C03)
Anywhere in the 6-meter or shorter wavelength bands, and in limited segments of some of the HF bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations. (G1E11)

## Slide 14: Digital Operating
A requirement to conduct communications with a digital station operating under automatic control outside the automatic control band segments is that the station initiating the contact must be under local or remote control. (G1E03)
      All amateur radio communications must be made by a control operator.
Publicly documenting the technical characteristics of a protocol must be done before using a new digital protocol on the air. (G1C13)
      The use of encryption is contrary to the very nature of amateur radio.
      From the very beginning Amateur Radio was intended to be fully open.
A DE-9 connector would be a good choice for a serial data port. (G2E12))
    Usually called a DB-9, but DE-9 is the original name. (and for the exam)
An RCA Phono connector is commonly used for audio signals in
Amateur Radio stations. (G6B12))

## Slide 15: Digital Operating
It is important to know the duty cycle of the data mode you are using when transmitting because some modes have high duty cycles which could exceed the transmitter's average power rating. (G8B08)
Winlink is a communication system that can use the Internet to transfer messages. (G2E13)
        Via an “RMS” (Remote Messaging Station).
To establish contact with a digital messaging system gateway station, transmit a connect message on the station’s published frequency. (G2E10)
Joining an existing contact using PACTOR is not possible due to connections are limited to two stations only. (G2E09)
Putting a PACTOR modem or controller in a mode which allows monitoring communications without a connection to determine if the channel is in use by other PACTOR stations. (G2E02)
    The “unconnected” or monitor mode of a PACTOR controller allows the control operator to do this.

## Slide 16: Digital Operating
These symptoms may result from other signals interfering with a PACTOR or WINMOR transmissions:
      Frequent retries or timeouts.
      Long pauses in message transmission.
      Failure to establish a connection between stations. (G2E03)
        All these choices are correct.
      WINMOR is a radio transmission protocol intended to be used in the Winlink 2000 Global Radio E-mail System by amateur radio operators. WINMOR will complement the PACTOR modes in the high frequency portion of the Winlink system.
The approximate bandwidth of a PACTOR-III signal at maximum data rate is 2300 Hz. (G8B05)
Failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR will result in the connection is dropped. (G8C06)

## Slide 17: Digital Operating
In the PACTOR protocol, a NAK response to a transmitted packet means the receiver is requesting the packet be retransmitted. (G8C05)
Forward error correction (FEC) allows the receiver to correct errors in received data packets by transmitting redundant information with the data. (G8C10)
When the receiving station detects errors in the reception of data, it sends ARQ, which requests the packet be retransmitted. (G8C07)
    ARQ stands for Automatic Repeat Request.
FT8 is a narrow-band digital mode that can receive signals with very low signal-to-noise ratios. (G8A12)
8-tone frequency shift keying is the type of modulation used by the FT8 digital mode. (G8A09))

## Slide 18: Digital Operating
Typical exchanges limited to call signs, grid locators, and signal reports are a characteristic of the FT8 mode of the WSJT-X family. (G2E11)
    WSJT is a computer program used for weak-signal radio
    communication between amateur radio operators.
A requirement when using FT8 digital mode is Computer time accurate within approximately 1 second. (G2E15)
When decoded on a computer screen,
FT8 provides basic information
about the received signal’s call sign,
grid location, and signal report.

## Slide 19: Digital Operating
The maximum PEP output allowed for spread spectrum transmissions is 10 watts. (G1E08)
    Spread Spectrum (or SS) is a mode where a radio signal is “hopped” over a relatively large frequency range.
In No Part of the 13-centimeter band may an amateur station communicate with non-licensed Wi-Fi stations. (G1E07))
On the 2.4 GHz band amateurs share channels with the unlicensed Wi-Fi service. (G8C01))

## Slide 20: Element 3 General Class Question Pool
Digital Operating
Question Pool valid
July 1st, 2023 Through June 30th 2027

## Slide 21: G8C04 Which of the following describes Baudot code? 04 Which of the following describes Baudot code?
A 7-bit code with start, stop, and parity bits.
A code using error detection and correction.
A 5-bit code with additional start and stop bits.
A code using SELCAL and LISTEN.

## Slide 22: G2E06 What is the most common frequency shift for RTTY emissions in the amateur HF bands?
85 Hz.
170 Hz.
425 Hz.
850 Hz.

## Slide 23: G8C11 How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified?
Dot and dash.
On and off.
High and low.
Mark and space.

## Slide 24: G2E01 Which mode is normally used when sending RTTY signals via AFSK with an SSB transmitter?
USB
DSB
CW
LSB

## Slide 25: G2E14 What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned properly?
The mark and space frequencies may be reversed.
You may have selected the wrong baud rate.
You may be listening on the wrong sideband.
All of these choices are correct.

## Slide 26: G2E05 What is the standard sideband used to generate a JT65, JT9, or FT8 digital signal when using AFSK in any amateur band?
LSB.
USB.
DSB.
SSB.

## Slide 27: G7C10 What is an advantage of using I-Q modulation with software-defined radios (SDRs)??
The need for high resolution analog-to-digital converters is eliminated
All types of modulation can be created with appropriate processing
Minimum detectible signal level is reduced
Automatic conversion of the signal from digital to analog

## Slide 28: G2E08 In what segment of the 20-meter band are most PSK31 operations commonly found?
At the bottom of the slow-scan TV segment, near 14.230 MHz.
At the top of the SSB phone segment, near 14.325 MHz.
In the middle of the CW segment near 14.100 MHz.
Below the RTTY segment, near 14.070 MHz.

## Slide 29: G8C08 Which of the following statements is true about PSK31?
Upper case letters are sent with more power.
Upper case letters use longer Varicode bit sequences and thus slow down transmission.
Error correction is used to ensure accurate message reception.
Higher power is needed as compared to RTTY for similar error rates.

## Slide 30: G8C13 What is indicated on a waterfall display by one or more vertical lines on either side of a digital signal?
Long path propagation.
Backscatter propagation.
Insufficient modulation.
Overmodulation.

## Slide 31: G8C14 Which of the following describes a waterfall display?
Frequency is horizontal, signal strength is vertical line time is intensity.
Frequency is vertical, signal strength is intensity, time is horizontal.
Frequency is horizontal, signal strength is intensity, time is vertical.
Frequency is vertical, signal strength is horizontal, time is intensity.

## Slide 32: G8A12 What is QPSK modulation?
Modulation using quasi-parallel to serial conversion to reduce bandwidth
Modulation using quadra-pole sideband keying to generate spread spectrum signals
Modulation using Fast Fourier Transforms to generate frequencies at the first, second, third, and fourth harmonics of the carrier frequency to improve noise immunity
Modulation in which digital data is transmitted using 0-, 90-, 180- and 270-degrees phase shift to represent pairs of bits

## Slide 33: G8A06 Which of the following is characteristic of QPSK31?
It is sideband sensitive.
Its encoding provides error correction.
Its bandwidth is approximately the same as BPSK31.
All of these choices are correct.

## Slide 34: G8A01 How is direct binary FSK modulation generated?
By keying an FM transmitter with a sub-audible tone
By changing an oscillator’s frequency directly with a digital control signal
By using a transceiver’s computer data interface protocol to change frequencies
By reconfiguring the CW keying input to act as a tone generator

## Slide 35: G8C12 Which type of code is used for sending characters in a PSK31 signal?
Varicode
Viterbi
Volumetric
Binary

## Slide 36: G4A11 Why should the ALC system be inactive when transmitting AFSK data signals?
ALC will invert the modulation of the AFSK mode
The ALC action distorts the signal
When using digital modes, too much ALC activity can cause the transmitter to overheat
All these choices are correct

## Slide 37: G8B08 Why is it important to know the duty cycle of the mode you are using when transmitting?
To aid in tuning your transmitter
Some modes have high duty cycles that could exceed the transmitter’s average power rating
To allow time for the other station to break in during a transmission
To prevent overmodulation

## Slide 38: G8B10 What is the relationship between transmitted symbol rate and bandwidth?
Symbol rate and bandwidth are not related
Higher symbol rates require wider bandwidth
Lower symbol rates require wider bandwidth
Bandwidth is half the symbol rate

## Slide 39: G1C08 What is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz?
56 kilobaud.
19.6 kilobaud.
1200 baud.
300 baud.

## Slide 40: G1C10 What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10- meter band?
56 kilobaud.
19.6 kilobaud.
1200 baud.
300 baud.

## Slide 41: G8C03 What part of a packet radio frame contains the routing and handling information?
Directory.
Preamble.
Header.
Footer.

## Slide 42: G1E11 On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations?
On any band segment where digital operation is permitted.
Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands.
Only in the non-phone Extra Class segments of the bands.
Anywhere in the 6-meter or shorter wavelength bands, and in limited segments of some HF bands.

## Slide 43: G1E03 What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments?
The station initiating the contact must be under local or remote control.
The interrogating transmission must be made by another automatically controlled station.
No third-party traffic may be transmitted.
The control operator of the interrogating station must hold an Amateur Extra Class license.

## Slide 44: G1C07 What must be done before using a new digital protocol on the air?
Type-certify equipment to FCC standards
Obtain an experimental license from the FCC
Publicly document the technical characteristics of the protocol
Submit a rule-making proposal to the FCC describing the codes and methods of the technique

## Slide 45: G6B12 Which of these connector types is commonly used for low frequency or dc signal connections to a transceiver?
PL-259.
BNC.
RCA Phono.
Type N.

## Slide 46: G2E12 Which of the following describes Winlink?
An amateur radio wireless network to send and receive email on the internet
A form of Packet Radio
A wireless network capable of both VHF and HF band operation
All of the above

## Slide 47: G2E13 What is another name for a Winlink Remote Message Server?
Terminal Node Controller
Gateway
RJ-45
Printer/Server

## Slide 48: G2E02 What is VARA?
A low signal-to-noise digital mode used for EME (moonbounce)
A digital protocol used with Winlink
A radio direction finding system used on VHF and UHF
A DX spotting system using a network of software defined radios

## Slide 49: G2E10 Which of the following is a way to establish contact with a digital messaging system gateway station?
Send an email to the system control operator.
Send QRL in Morse code.
Respond when the station broadcasts its SSID.
Transmit a connect message on the station’s published frequency.

## Slide 50: G2E09 How do you join a contact between two stations using PACTOR protocol?
Send broadcast packets containing your call sign while in MONITOR mode.
Transmit a steady carrier until the PACTOR protocol times out and disconnects.
Joining an existing contact is not possible, PACTOR connections are limited to two stations.
Send a NAK response continuously so that the sending station must stand by.

## Slide 51: G2E03 What symptoms may result from other signals interfering with a PACTOR or VARA transmission?
Frequent retries or timeouts
Long pauses in message transmission
Failure to establish a connection between stations
All these choices are correct

## Slide 52: G8C06 What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR?
The checksum overflows.
The connection is dropped.
Packets will be routed incorrectly.
Encoding reverts to the default character set.

## Slide 53: G8C05 In an ARQ mode, what is meant by a NAK response to a transmitted packet?
Request retransmission of the packet
Packet was received without error
Receiving station connected and ready for transmissions
Entire file received correctly

## Slide 54: G8C10 How does forward error correction (FEC) allow the receiver to correct data errors?
By controlling transmitter output power for optimum signal strength.
By using the Varicode character set.
By transmitting redundant information with the data.
By using a parity bit with each character.

## Slide 55: G8C07 Which of the following narrow-band digital modes can receive signals with a very low signal-to-noise ratios?
MSK 144.
FT8.
AMTOR.
MFSK32.

## Slide 56: G8A09 What type of modulation is used by FT8 digital mode?
8-tone frequency shift keying.
Vestigial sideband.
Amplitude compressed AM.
Direct sequence spread spectrum.

## Slide 57: G2E07 Which of the following is a requirement when using the FT8?
A special hardware modem.
Computer time accurate to within approximately 1 second.
Receiver attenuator set to -12dB.
A vertically polarized antenna.

## Slide 58: G2C15 What does an FT8 signal report of +3 mean?
The signal is 3 times the noise level of an equivalent SSB signal
The signal is S3 (weak signals)
The signal-to-noise ratio is equivalent to +3dB in a 2.5 kHz bandwidth
The signal is 3 dB over S9

## Slide 59: G2E04 Which of the following is good practice when choosing a transmitting frequency to answer a station calling CQ using FT8?
Always call on the station’s frequency
Call on any frequency in the waterfall except the station’s frequency
Find a clear frequency during the same time slot as the calling station
Find a clear frequency during the alternate time slot to the calling station

## Slide 60: G2E15 Which of the following is a common location for FT8?
Anywhere in the voice portion of the band
Anywhere in the CW portion of the band
Approximately 14.074 MHz to 14.077 MHz
Approximately 14.110 MHz to 14.113 MHz

## Slide 61: G1E08 What is the maximum PEP output for spread spectrum transmissions?
100 milliwatts.
10 watts.
100 watts.
1500 watts.

## Slide 62: G1E07 In what part of the 2.4 GHz band may an amateur station communicate with non-licensed Wi-Fi stations?
Anywhere in the band
Channels 1 through 4
Channels 42 through 45
No part

## Slide 63: G8C01 On what band do amateurs share channels with the unlicensed Wi-Fi service?
432 MHz
902 MHz
2.4 GHz
10.7 GHz

## Slide 64: G8C09 Which is true of mesh network microwave nodes?
Having more nodes increases signal strengths
If one node fails, a packet may still reach its target station via an alternate node
Links between two nodes in a network may have different frequencies and bandwidths
More nodes reduce overall microwave out of band interference

## Slide 65: G2E11 What is the primary purpose of an Amateur Radio Emergency Data Network (AREDN) mesh network?
To provide FM repeater coverage in remote areas
To provide real time propagation data by monitoring amateur radio transmissions worldwide
To provide high-speed data services during an emergency or community event
To provide DX spotting reports to aid contesters and DXers

## Slide 66: G8A13 What is a link budget?
The financial costs associated with operating a radio link
The sum of antenna gains minus system losses
The sum of transmit power and antenna gains minus system losses as seen at the receiver
The difference between transmit power and receiver sensitivity

## Slide 67: G8A14 What is link margin?
The opposite of fade margin
The difference between received power level and minimum required signal level at the input to the receiver
Transmit power minus receiver sensitivity
Receiver sensitivity plus 3 dB

## Slide 68: G8C16 Which of the following provide digital voice modes?
WSPR, MFSK16, and EasyPAL
FT8, FT4, and FST4
Winlink, PACTOR II, and PACTOR III
DMR, D-STAR, and SystemFusion

## Slide 69: Thank You!