TH25AT

The Mars & Cap mod for the Kenwood TH-25AT is to remove resistors R18-21.  They 
are located on a panel under the display.  This one is a real pain to access but
 this mod gives transmit coverage from 140-163 Mhz.  The TM-721A mod gives trans
mit from 142-152 Mhz.