When your turn on your kitchen faucet, why doesn’t
ALL THE WATER IN THE ENTIRE
CITY WATER SYSTEM
Pour out through your sink in just a few seconds?
Water Pressure
Water Flow
Water Resistance
Discuss…..
VOLTAGE
CURRENT
RESISTANCE

---
VOLTMETER LAB
YELLOW = DANGER !!

---
For those not terrific with algebra…..

---
When you use electricity, why don’t they send you a bill for a million
Dollars every month?
POWER
ENERGY
Power = volts * amps (measured in WATTS)
Energy = Power * time (measured in kWHr @ $0.13 each locally)

---
For those not terrific with algebra…

---
Electrical current is measured in which of the following units?_clipboard0
Electrical current is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes
 T5A01 HRLM (3 - 1)

---
Electrical current is measured in which of the following units?
Electrical current is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes
(D) T5A01 HRLM (3 - 1)

---
Electrical power is measured in which of the following units?
Electrical power is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes
 T5A02 HRLM (3 - 7)

---
Electrical power is measured in which of the following units?
Electrical power is measured in which of the following units?
A. Volts
B. Watts
C. Ohms
D. Amperes
(B) T5A02 HRLM (3 - 7)

---
What is the name for the flow of electrons in an electric circuit?
A. Voltage
B. Resistance
C. Capacitance
D. Current
 T5A03 HRLM (3 - 1)

---
What is the name for the flow of electrons in an electric circuit?
A. Voltage
B. Resistance
C. Capacitance
D. Current
(D) T5A03 HRLM (3 - 1)

---
What is the name for a current that flows only in one direction?
A. Alternating current
B. Direct current
C. Normal current
D. Smooth current
 T5A04 HRLM (3 - 2)

---
What is the name for a current that flows only in one direction?
A. Alternating current
B. Direct current
C. Normal current
D. Smooth current
(B) T5A04 HRLM (3 - 2)

---
What is the electrical term for the electromotive force (EMF) that causes electron flow?
A. Voltage
B. Ampere-hours
C. Capacitance
D. Inductance
 T5A05 HRLM (3 - 1)

---
What is the electrical term for the electromotive force (EMF) that causes electron flow?
A. Voltage
B. Ampere-hours
C. Capacitance
D. Inductance
(A) T5A05 HRLM (3 - 1)

---
How much voltage does a mobile transceiver typically require?
How much voltage does a mobile transceiver typically require?
A. About 12 volts
B. About 30 volts
C. About 120 volts
D. About 240 volts
 T5A06 HRLM (5 - 16)

---
How much voltage does a mobile transceiver typically require?
How much voltage does a mobile transceiver typically require?
A. About 12 volts
B. About 30 volts
C. About 120 volts
D. About 240 volts
(A) T5A06 HRLM (5 - 16)

---
Which of the following is a good electrical conductor?
Which of the following is a good electrical conductor?
A. Glass
B. Wood
C. Copper
D. Rubber
 T5A07 HRLM (3 - 5)

---
Which of the following is a good electrical conductor?
Which of the following is a good electrical conductor?
A. Glass
B. Wood
C. Copper
D. Rubber
(C) T5A07 HRLM (3 - 5)

---
Which of the following is a good electrical insulator?
Which of the following is a good electrical insulator?
A. Copper
B. Glass
C. Aluminum
D. Mercury
 T5A08 HRLM (3 - 5)

---
Which of the following is a good electrical insulator?
Which of the following is a good electrical insulator?
A. Copper
B. Glass
C. Aluminum
D. Mercury
(B) T5A08 HRLM (3 - 5)

---
What is the name for a current that reverses direction on a regular basis?
A. Alternating current
B. Direct current
C. Circular current
D. Vertical current
 T5A09 HRLM (3 - 2)

---
What is the name for a current that reverses direction on a regular basis?
A. Alternating current
B. Direct current
C. Circular current
D. Vertical current
(A) T5A09 HRLM (3 - 2)

---
Which term describes the rate at which electrical energy is used?
A. Resistance
B. Current
C. Power
D. Voltage
 T5A10 HRLM (3 - 7)

---
Which term describes the rate at which electrical energy is used?
A. Resistance
B. Current
C. Power
D. Voltage
(C) T5A10 HRLM (3 - 7)

---
What is the unit of electromotive force?
What is the unit of electromotive force?
A. The volt
B. The watt
C. The ampere
D. The ohm
 T5A11 HRLM (3 - 2)

---
What is the unit of electromotive force?
What is the unit of electromotive force?
A. The volt
B. The watt
C. The ampere
D. The ohm
(A) T5A11 HRLM (3 - 2)

---
What describes the number of times per second that an alternating current makes a complete cycle?
A. Pulse rate
B. Speed
C. Wavelength
D. Frequency
 T5A12 HRLM (2 - 3)

---
What describes the number of times per second that an alternating current makes a complete cycle?
A. Pulse rate
B. Speed
C. Wavelength
D. Frequency
(D) T5A12 HRLM (2 - 3)

---
In which type of circuit is current the same through all components?
A. Series
B. Parallel
C. Resonant
D. Branch
 T5A13 HRLM (3 - 2)

---
In which type of circuit is current the same through all components?
A. Series
B. Parallel
C. Resonant
D. Branch
(A) T5A13 HRLM (3 - 2)

---
In which type of circuit is voltage the same across all components?
A. Series
B. Parallel
C. Resonant
D. Branch
 T5A14 HRLM (3 - 2)

---
In which type of circuit is voltage the same across all components?
A. Series
B. Parallel
C. Resonant
D. Branch
(B) T5A14 HRLM (3 - 2)

---
How many milliamperes is 1.5 amperes?_clipboard0
How many milliamperes is 1.5 amperes?
A. 15 milliamperes
B. 150 milliamperes
C. 1500 milliamperes
D. 15,000 milliamperes
 T5B01 HRLM (2 - 2)

---
How many milliamperes is 1.5 amperes?
How many milliamperes is 1.5 amperes?
A. 15 milliamperes
B. 150 milliamperes
C. 1500 milliamperes
D. 15,000 milliamperes
(C) T5B01 HRLM (2 – 2) 1 milliampere = 0.001 Amperes
1 microampere = 0. 000 001 amp
1 kiloamp = 1,000 amperes

---
What is another way to specify a radio signal frequency of 1,500,000 hertz?
A. 1500 kHz
B. 1500 MHz
C. 15 GHz
D. 150 kHz
 T5B02 HRLM (2 - 2)

---
What is another way to specify a radio signal frequency of 1,500,000 hertz?
A. 1500 kHz
B. 1500 MHz
C. 15 GHz
D. 150 kHz
(A) T5B02 HRLM (2 – 2)
1 kilohertz = 1000 Hertz.
1 500 000 Hz = 1 500 kHz = 1.5 MHz

---
How many volts are equal to one kilovolt?_clipboard1
How many volts are equal to one kilovolt?
A. One one-thousandth of a volt
B. One hundred volts
C. One thousand volts
D. One million volts
 T5B03 HRLM (2 - 2)

---
How many volts are equal to one kilovolt?
How many volts are equal to one kilovolt?
A. One one-thousandth of a volt
B. One hundred volts
C. One thousand volts
D. One million volts
(C) T5B03 HRLM (2 - 2)

---
How many volts are equal to one microvolt?_clipboard2
How many volts are equal to one microvolt?
A. One one-millionth of a volt
B. One million volts
C. One thousand kilovolts
D. One one-thousandth of a volt
 T5B04 HRLM (2 - 2)

---
How many volts are equal to one microvolt?
How many volts are equal to one microvolt?
A. One one-millionth of a volt
B. One million volts
C. One thousand kilovolts
D. One one-thousandth of a volt
(A) T5B04 HRLM (2 – 2)
1 microvolt = 0. 000 001 volts
1 000 000 microvolts = 1 volt

---
Which of the following is equal to 500 milliwatts?_clipboard3
Which of the following is equal to 500 milliwatts?
A. 0.02 watts
B. 0.5 watts
C. 5 watts
D. 50 watts
 T5B05 HRLM (2 - 2)

---
Which of the following is equal to 500 milliwatts?
Which of the following is equal to 500 milliwatts?
A. 0.02 watts
B. 0.5 watts
C. 5 watts
D. 50 watts
(B) T5B05 HRLM (2 - 2)

---
If an ammeter calibrated in amperes is used to measure a 3000-milliampere current, what reading would it show?
A. 0.003 amperes
B. 0.3 amperes
C. 3 amperes
D. 3,000,000 amperes
 T5B06 HRLM (2 - 2)

---
If an ammeter calibrated in amperes is used to measure a 3000-milliampere current, what reading would it show?
A. 0.003 amperes
B. 0.3 amperes
C. 3 amperes
D. 3,000,000 amperes
(C) T5B06 HRLM (2 - 2)

---
If a frequency display calibrated in megahertz shows a reading of 3.525 MHz, what would it show if it were calibrated in kilohertz?
A. 0.003525 kHz
B. 35.25 kHz
C. 3525 kHz
D. 3,525,000 kHz
 T5B07 HRLM (2 - 2)

---
If a frequency display calibrated in megahertz shows a reading of 3.525 MHz, what would it show if it were calibrated in kilohertz?
A. 0.003525 kHz
B. 35.25 kHz
C. 3525 kHz
D. 3,525,000 kHz
(C) T5B07 HRLM )
1 MHz = 1 000 000 Hz = 1 000 kHz

---
How many microfarads are equal to 1,000,000 picofarads?_clipboard4
How many microfarads are equal to 1,000,000 picofarads?
A. 0.001 microfarads
B. 1 microfarad
C. 1000 microfarads
D. 1,000,000,000 microfarads
 T5B08 HRLM (2 - 2)

---
How many microfarads are equal to 1,000,000 picofarads?
How many microfarads are equal to 1,000,000 picofarads?
A. 0.001 microfarads
B. 1 microfarad
C. 1000 microfarads
D. 1,000,000,000 microfarads
(B) T5B08 HRLM (2 – 2)
1 picofarad = 10-12 farad
 microfarads	nanofarads	picofarads
        1/1000 mfd 1/1000 nanofarad

---
What is the approximate amount of change, measured in decibels (dB), of a power increase from 5 watts to 10 watts?
A. 2 dB
B. 3 dB
C. 5 dB
D. 10 dB
 T5B09 HRLM (4 - 8)

---
What is the approximate amount of change, measured in decibels (dB), of a power increase from 5 watts to 10 watts?
A. 2 dB
B. 3 dB
C. 5 dB
D. 10 dB
(B) T5B09 HRLM (4 – 8)
Memorize 3 facts for POWER:: 3db = factor of TWO
        6DB = factor of FOUR
        10DB = factor of TEN

---
What is the approximate amount of change, measured in decibels (dB), of a power decrease from 12 watts to 3 watts?
A. -1 dB
B. -3 dB
C. -6 dB
D. -9 dB
 T5B10 HRLM (4 - 8)

---
What is the approximate amount of change, measured in decibels (dB), of a power decrease from 12 watts to 3 watts?
A. -1 dB
B. -3 dB
C. -6 dB
D. -9 dB
(C) T5B10 HRLM (4 - 8)

---
What is the amount of change, measured in decibels (dB), of a power increase from 20 watts to 200 watts?
A. 10 dB
B. 12 dB
C. 18 dB
D. 28 dB
 T5B11 HRLM (4 - 8)

---
What is the amount of change, measured in decibels (dB), of a power increase from 20 watts to 200 watts?
A. 10 dB
B. 12 dB
C. 18 dB
D. 28 dB
(A) T5B11 HRLM (4 - 8)

---
Which of the following frequencies is equal to 28,400 kHz?_clipboard5
Which of the following frequencies is equal to 28,400 kHz?
A. 28.400 MHz
B. 2.800 MHz
C. 284.00 MHz
D. 28.400 kHz
 T5B12 HRLM (2 - 2)

---
Which of the following frequencies is equal to 28,400 kHz?
Which of the following frequencies is equal to 28,400 kHz?
A. 28.400 MHz
B. 2.800 MHz
C. 284.00 MHz
D. 28.400 kHz
(A) T5B12 HRLM (2 - 2)

---
If a frequency display shows a reading of 2425 MHz, what frequency is that in GHz?
A. 0.002425 GHz
B. 24.25 GHz
C. 2.425 GHz
D. 2425 GHz
 T5B13 HRLM (2 - 2)

---
If a frequency display shows a reading of 2425 MHz, what frequency is that in GHz?
A. 0.002425 GHz
B. 24.25 GHz
C. 2.425 GHz
D. 2425 GHz
(C) T5B13 HRLM (2 - 2)

---
What is the ability to store energy in an electric field called?
A. Inductance
B. Resistance
C. Tolerance
D. Capacitance
 T5C01 HRLM (3 - 9)

---
What is the ability to store energy in an electric field called?
A. Inductance
B. Resistance
C. Tolerance
D. Capacitance
(D) T5C01 HRLM (3 – 9) You can make a capacitor with two sheets of aluminum foil and paper between.

---
What is the basic unit of capacitance?_clipboard0
What is the basic unit of capacitance?
A. The farad
B. The ohm
C. The volt
D. The henry
 T5C02 HRLM (3 - 9)

---
What is the basic unit of capacitance?
What is the basic unit of capacitance?
A. The farad
B. The ohm
C. The volt
D. The henry
(A) T5C02 HRLM (3 - 9)

---
What is the ability to store energy in a magnetic field called?_clipboard1
What is the ability to store energy in a magnetic field called?
A. Admittance
B. Capacitance
C. Resistance
D. Inductance
 T5C03 HRLM (3 - 9)

---
What is the ability to store energy in a magnetic field called?
What is the ability to store energy in a magnetic field called?
A. Admittance
B. Capacitance
C. Resistance
D. Inductance
(D) T5C03 HRLM (3 – 9) You can make an inductor by winding wire around a pencil….and even a straight wire has its own inductance!!

---
What is the basic unit of inductance?_clipboard2
What is the basic unit of inductance?
A. The coulomb
B. The farad
C. The henry
D. The ohm
 T5C04 HRLM (3 - 9)

---
What is the basic unit of inductance?
What is the basic unit of inductance?
A. The coulomb
B. The farad
C. The henry
D. The ohm
(C) T5C04 HRLM (3 - 9)

---
What is the unit of frequency?_clipboard3
What is the unit of frequency?
A. Hertz
B. Henry
C. Farad
D. Tesla
 T5C05 HRLM (2 - 3)

---
What is the unit of frequency?
What is the unit of frequency?
A. Hertz
B. Henry
C. Farad
D. Tesla
(A) T5C05 HRLM (2 - 3)

---
What does the abbreviation “RF” refer to? _clipboard4
What does the abbreviation “RF” refer to?
A. Radio frequency signals of all types
B. The resonant frequency of a tuned circuit
C. The real frequency transmitted as opposed to the apparent frequency
D. Reflective force in antenna transmission lines
 T5C06 HRLM (2 - 4)

---
What does the abbreviation “RF” refer to?
What does the abbreviation “RF” refer to?
A. Radio frequency signals of all types
B. The resonant frequency of a tuned circuit
C. The real frequency transmitted as opposed to the apparent frequency
D. Reflective force in antenna transmission lines
(A) T5C06 HRLM (2 - 4)

---
A radio wave is made up of what type of energy?_clipboard5
A radio wave is made up of what type of energy?
A. Pressure
B. Electromagnetic
C. Gravity
D. Thermal
 T5C07 HRLM (4 - 6)

---
A radio wave is made up of what type of energy?
A radio wave is made up of what type of energy?
A. Pressure
B. Electromagnetic
C. Gravity
D. Thermal
(B) T5C07 HRLM (4 - 6)

---
What is the formula used to calculate electrical power in a DC circuit?
A. Power (P) equals voltage (E) multiplied by current (I)
B. Power (P) equals voltage (E) divided by current (I)
C. Power (P) equals voltage (E) minus current (I)
D. Power (P) equals voltage (E) plus current (I)
 T5C08 HRLM (3 - 7)

---
What is the formula used to calculate electrical power in a DC circuit?
A. Power (P) equals voltage (E) multiplied by current (I)
B. Power (P) equals voltage (E) divided by current (I)
C. Power (P) equals voltage (E) minus current (I)
D. Power (P) equals voltage (E) plus current (I)
(A) T5C08 HRLM (3 - 7)

---
How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
A. 138 watts
B. 0.7 watts
C. 23.8 watts
D. 3.8 watts
 T5C09 HRLM (3 - 7)

---
How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
A. 138 watts
B. 0.7 watts
C. 23.8 watts
D. 3.8 watts
(A) T5C09 HRLM (3 - 7)

---
How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
A. 4.8 watts
B. 30 watts
C. 14.5 watts
D. 0.208 watts
 T5C10 HRLM (3 - 7)

---
How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
A. 4.8 watts
B. 30 watts
C. 14.5 watts
D. 0.208 watts
(B) T5C10 HRLM (3 - 7)

---
How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
A. 0.1 amperes
B. 10 amperes
C. 12 amperes
D. 132 amperes
 T5C11 HRLM (3 - 7)

---
How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
A. 0.1 amperes
B. 10 amperes
C. 12 amperes
D. 132 amperes
(B) T5C11 HRLM (3 - 7)

---
What is impedance? _clipboard6
What is impedance?
A. A measure of the opposition to AC current flow in a circuit
B. The inverse of resistance
C. The Q or Quality Factor of a component
D. The power handling capability of a component
 T5C12 HRLM (3 - 10)

---
What is impedance?
What is impedance?
A. A measure of the opposition to AC current flow in a circuit
B. The inverse of resistance
C. The Q or Quality Factor of a component
D. The power handling capability of a component
(A) T5C12 HRLM (3 - 10)

---
What is a unit of impedance? _clipboard7
What is a unit of impedance?
A. Volts
B. Amperes
C. Coulombs
D. Ohms
 T5C13 HRLM (3 - 10)

---
What is a unit of impedance?
What is a unit of impedance?
A. Volts
B. Amperes
C. Coulombs
D. Ohms
(D) T5C13 HRLM (3 – 10) (The answer is a little simpleminded--- impedance can have both “real” and “imaginary” parts --- 90 degrees out of phase for reactive component….the math is sorta “up there” )

---
What is the proper abbreviation for megahertz?_clipboard8
What is the proper abbreviation for megahertz?
A. mHz
B. mhZ
C. Mhz
D. MHz
 T5C14 HRLM (2 - 3)

---
What is the proper abbreviation for megahertz?
What is the proper abbreviation for megahertz?
A. mHz
B. mhZ
C. Mhz
D. MHz
(D) T5C14 HRLM (2 - 3)

---
What formula is used to calculate current in a circuit?_clipboard0
What formula is used to calculate current in a circuit?
A. Current (I) equals voltage (E) multiplied by resistance (R)
B. Current (I) equals voltage (E) divided by resistance (R)
C. Current (I) equals voltage (E) added to resistance (R)
D. Current (I) equals voltage (E) minus resistance (R)
 T5D01 HRLM (3 - 5)

---
What formula is used to calculate current in a circuit?
What formula is used to calculate current in a circuit?
A. Current (I) equals voltage (E) multiplied by resistance (R)
B. Current (I) equals voltage (E) divided by resistance (R)
C. Current (I) equals voltage (E) added to resistance (R)
D. Current (I) equals voltage (E) minus resistance (R)
(B) T5D01 HRLM (3 - 5)

---
What formula is used to calculate voltage in a circuit?_clipboard1
What formula is used to calculate voltage in a circuit?
A. Voltage (E) equals current (I) multiplied by resistance (R)
B. Voltage (E) equals current (I) divided by resistance (R)
C. Voltage (E) equals current (I) added to resistance (R)
D. Voltage (E) equals current (I) minus resistance (R)
 T5D02 HRLM (3 - 5)

---
What formula is used to calculate voltage in a circuit?
What formula is used to calculate voltage in a circuit?
A. Voltage (E) equals current (I) multiplied by resistance (R)
B. Voltage (E) equals current (I) divided by resistance (R)
C. Voltage (E) equals current (I) added to resistance (R)
D. Voltage (E) equals current (I) minus resistance (R)
(A) T5D02 HRLM (3 - 5)

---
What formula is used to calculate resistance in a circuit?_clipboard2
What formula is used to calculate resistance in a circuit?
A. Resistance (R) equals voltage (E) multiplied by current (I)
B. Resistance (R) equals voltage (E) divided by current (I)
C. Resistance (R) equals voltage (E) added to current (I)
D. Resistance (R) equals voltage (E) minus current (I)
 T5D03 HRLM (3 - 5)

---
What formula is used to calculate resistance in a circuit?
What formula is used to calculate resistance in a circuit?
A. Resistance (R) equals voltage (E) multiplied by current (I)
B. Resistance (R) equals voltage (E) divided by current (I)
C. Resistance (R) equals voltage (E) added to current (I)
D. Resistance (R) equals voltage (E) minus current (I)
(B) T5D03 HRLM (3 - 5)

---
RESISTOR LAB!!!!!!

---
What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
A. 3 ohms
B. 30 ohms
C. 93 ohms
D. 270 ohms
 T5D04 HRLM (3 - 6)

---
What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
A. 3 ohms
B. 30 ohms
C. 93 ohms
D. 270 ohms
(B) T5D04 HRLM (3 - 6)

---
What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
A. 18 ohms
B. 0.125 ohms
C. 8 ohms
D. 13.5 ohms
 T5D05 HRLM (3 - 6)

---
What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
A. 18 ohms
B. 0.125 ohms
C. 8 ohms
D. 13.5 ohms
(C) T5D05 HRLM (3 - 6)

---
What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
A. 3 ohms
B. 16 ohms
C. 48 ohms
D. 8 ohms
 T5D06 HRLM (3 - 6)

---
What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
A. 3 ohms
B. 16 ohms
C. 48 ohms
D. 8 ohms
(A) T5D06 HRLM (3 - 6)

---
What is the current in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
A. 9600 amperes
B. 200 amperes
C. 0.667 amperes
D. 1.5 amperes
 T5D07 HRLM (3 - 6)

---
What is the current in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
A. 9600 amperes
B. 200 amperes
C. 0.667 amperes
D. 1.5 amperes
(D) T5D07 HRLM (3 - 6)

---
What is the current through a 100-ohm resistor connected across 200 volts?
A. 20,000 amperes
B. 0.5 amperes
C. 2 amperes
D. 100 amperes
 T5D08 HRLM (3 - 6)

---
What is the current through a 100-ohm resistor connected across 200 volts?
A. 20,000 amperes
B. 0.5 amperes
C. 2 amperes
D. 100 amperes
(C) T5D08 HRLM (3 - 6)

---
What is the current through a 24-ohm resistor connected across 240 volts?
A. 24,000 amperes
B. 0.1 amperes
C. 10 amperes
D. 216 amperes
 T5D09 HRLM (3 - 6)

---
What is the current through a 24-ohm resistor connected across 240 volts?
A. 24,000 amperes
B. 0.1 amperes
C. 10 amperes
D. 216 amperes
(C) T5D09 HRLM (3 - 6)

---
What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
A. 1 volt
B. 0.25 volts
C. 2.5 volts
D. 1.5 volts
 T5D10 HRLM (3 - 6)

---
What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
A. 1 volt
B. 0.25 volts
C. 2.5 volts
D. 1.5 volts
(A) T5D10 HRLM (3 - 6)

---
What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
A. 1 volt
B. 10 volts
C. 11 volts
D. 9 volts
 T5D11 HRLM (3 - 7)

---
What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
A. 1 volt
B. 10 volts
C. 11 volts
D. 9 volts
(B) T5D11 HRLM (3 - 7)

---
What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
A. 8 volts
B. 0.2 volts
C. 12 volts
D. 20 volts
 T5D12 HRLM (3 - 7)

---
What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
A. 8 volts
B. 0.2 volts
C. 12 volts
D. 20 volts
(D) T5D12 HRLM (3 - 7)

---
What happens to current at the junction of two components in series?
A. It divides equally between them
B. It is unchanged
C. It divides based on the on the value of the components
D. The current in the second component is zero
 T5D13 HRLM (3 - 2)

---
What happens to current at the junction of two components in series?
A. It divides equally between them
B. It is unchanged
C. It divides based on the on the value of the components
D. The current in the second component is zero
(B) T5D13 HRLM (3 - 2)

---
What happens to current at the junction of two components in parallel?
A. It divides between them dependent on the value of the components
B. It is the same in both components
C. Its value doubles
D. Its value is halved
 T5D14 HRLM (3 - 2)

---
What happens to current at the junction of two components in parallel?
A. It divides between them dependent on the value of the components
B. It is the same in both components
C. Its value doubles
D. Its value is halved
(A) T5D14 HRLM (3 - 2)

---
What is the voltage across each of two components in series with a voltage source?
A. The same voltage as the source
B. Half the source voltage
C. It is determined by the type and value of the components
D. Twice the source voltage
 T5D15 HRLM (3 - 2)

---
What is the voltage across each of two components in series with a voltage source?
A. The same voltage as the source
B. Half the source voltage
C. It is determined by the type and value of the components
D. Twice the source voltage
(C) T5D15 HRLM (3 - 2)

---
What is the voltage across each of two components in parallel with a voltage source?
A. It is determined by the type and value of the components
B. Half the source voltage
C. Twice the source voltage
D. The same voltage as the source
 T5D16 HRLM (3 - 3)

---
What is the voltage across each of two components in parallel with a voltage source?
A. It is determined by the type and value of the components
B. Half the source voltage
C. Twice the source voltage
D. The same voltage as the source
(D) T5D16 HRLM (3 - 3)