Section T7

---
Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion
 T7A01 HRLM (5 - 9)

---
Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion
(B) T7A01 HRLM (5 – 9) Typical ham radio receivers can receive a signal LESS THAN A MICROVOLT STRONG; this is about 140 dB weaker than the transmitter output….

---
What is a transceiver?
What is a transceiver?
A. A type of antenna switch
B. A unit combining the functions of a transmitter and a receiver
C. A component in a repeater that filters out unwanted interference
D. A type of antenna matching network
 T7A02 HRLM (2 - 7)

---
What is a transceiver?
What is a transceiver?
A. A type of antenna switch
B. A unit combining the functions of a transmitter and a receiver
C. A component in a repeater that filters out unwanted interference
D. A type of antenna matching network
(B) T7A02 HRLM (2 - 7)

---
Which of the following is used to convert a radio signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier
 T7A03 HRLM (3 - 18)

---
Which of the following is used to convert a radio signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier
(B) T7A03 HRLM (3 – 18) Output will be SUM and DIFFERENCE FREQUENCIES --- and almost any non-linear device can be a mixer – diode, transistor, vacuum tube, even a rusty fence wire connection….

---
Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic distortion
 T7A04 HRLM (5 - 9)

---
Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio (seems to be a made-up term….)
B. Sensitivity
C. Selectivity
D. Harmonic distortion
(C) T7A04 HRLM (5 - 9)

---
What is the name of a circuit that generates a signal at a specific frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator
 T7A05 HRLM (3 - 17)

---
What is the name of a circuit that generates a signal at a specific frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator
(D) T7A05 HRLM (3 – 17) Anything that amplifies can become an oscillator if enough of the output gets backwards to the input in the proper phase relationship…..often amplifiers become unwanted oscillators…….

---
What device converts the RF input and output of a transceiver to another band?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter
 T7A06 HRLM (5 - 11)

---
What device converts the RF input and output of a transceiver to another band?
A. High-pass filter
B. Low-pass filter
C. Transverter
D. Phase converter
(C) T7A06 HRLM (5 - 11)

---
What is meant by “PTT”?
What is meant by “PTT”?
A. Pre-transmission tuning to reduce transmitter harmonic emission
B. Precise tone transmissions used to limit repeater access to only certain signals
C. A primary transformer tuner use to match antennas
D. The push-to-talk function that switches between receive and transmit
 T7A07 HRLM (5 - 7)

---
What is meant by “PTT”?
What is meant by “PTT”?
A. Pre-transmission tuning to reduce transmitter harmonic emission
B. Precise tone transmissions used to limit repeater access to only certain signals
C. A primary transformer tuner use to match antennas
D. The push-to-talk function that switches between receive and transmit
(D) T7A07 HRLM (5 - 7)

---
Which of the following describes combining speech with an RF carrier signal?
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering
 T7A08 HRLM (3 - 17)

---
Which of the following describes combining speech with an RF carrier signal?
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering
(C) T7A08 HRLM (3 - 17)
Reactance modulator will make phase-
Or frequency modulation;
Double Balanced mixer can make double
Sideband (then filter to get single sideband)
Just putting a carbon microphone in
Series with the output amplifier can
Make regular old AMPLITUDE
MODULATION --- and many original
Broadcast transmitters probably
Started that way!!

---
What is the function of the SSB/CW-FM switch on a VHF power amplifier?
A. Change the mode of the transmitted signal
B. Set the amplifier for proper operation in the selected mode
C. Change the frequency range of the amplifier to operate in the proper portion of the band
D. Reduce the received signal noise
 T7A09 HRLM (5 - 10)

---
What is the function of the SSB/CW-FM switch on a VHF power amplifier?
A. Change the mode of the transmitted signal
B. Set the amplifier for proper operation in the selected mode
C. Change the frequency range of the amplifier to operate in the proper portion of the band
D. Reduce the received signal noise
(B) T7A09 HRLM (5 - 10)
A non-linear class C amplifier, more efficient,
Can be used for CW or FM ---
But a LINEAR AMPLIFIER is rquired for
Single Side Band and often has lower
Efficiency, hence gets hotter….

---
What device increases the low-power output from a handheld transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All of these choices are correct
 T7A10 HRLM (5 - 10)

---
What device increases the low-power output from a handheld transceiver?
A. A voltage divider
B. An RF power amplifier
C. An impedance network
D. All of these choices are correct
(B) T7A10 HRLM (5 - 10)

---
Where is an RF preamplifier installed?
Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter's power amplifier
C. Between a transmitter and antenna tuner
D. At the receiver's audio output
 T7A11 HRLM (5 - 9)

---
Where is an RF preamplifier installed?_clipboard0
Where is an RF preamplifier installed?
A. Between the antenna and receiver
B. At the output of the transmitter's power amplifier
C. Between a transmitter and antenna tuner
D. At the receiver's audio output
(A) T7A11 HRLM (5 - 9)

---
What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone
 T7B01 HRLM (5 - 7)

---
What can you do if you are told your FM handheld or mobile transceiver is over-deviating?
A. Talk louder into the microphone
B. Let the transceiver cool off
C. Change to a higher power level
D. Talk farther away from the microphone
(D) T7B01 HRLM (5 - 7)

---
What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low
 T7B02 HRLM (9 - 8)

---
What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is unable to reject strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low
(A) T7B02 HRLM (9 - 8)
ANY DIODE ANYWHERE – and potentially the
Device can “receive” a radio signal – no matter
Whether it is a telephone, radio, phonograph…
Anything can potentially be overwhelmed
By a sufficiently strong signal.

---
Which of the following can cause radio frequency interference?_clipboard0
Which of the following can cause radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct
 T7B03 HRLM (9 - 8)

---
Which of the following can cause radio frequency interference?
Which of the following can cause radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct
(D) T7B03 HRLM (9 - 8)

---
Which of the following is a way to reduce or eliminate interference from an amateur transmitter to a nearby telephone?
A. Put a filter on the amateur transmitter
B. Reduce the microphone gain
C. Reduce the SWR on the transmitter transmission line
D. Put an RF filter on the telephone
 T7B04 HRLM (9 - 8)

---
Which of the following is a way to reduce or eliminate interference from an amateur transmitter to a nearby telephone?
A. Put a filter on the amateur transmitter
B. Reduce the microphone gain
C. Reduce the SWR on the transmitter transmission line
D. Put an RF filter on the telephone
(D) T7B04 HRLM (9 - 8)
DSL Internet installations usually included similar
Filters on the associated telephones also….
FILTER = capacitors/inductors

---
How can overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode
 T7B05 HRLM (9 - 9)

---
How can overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode
(A) T7B05 HRLM (9 - 9)

---
Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
D. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
 T7B06 HRLM (9 - 9)

---
Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
D. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
(A) T7B06 HRLM (9 - 9)

---
Which of the following can reduce overload to a VHF transceiver from a nearby FM broadcast station?
A. RF preamplifier
B. Double-shielded coaxial cable
C. Using headphones instead of the speaker
D. Band-reject filter
 T7B07 HRLM (9 - 9)

---
Which of the following can reduce overload to a VHF transceiver from a nearby FM broadcast station?
A. RF preamplifier
B. Double-shielded coaxial cable
C. Using headphones instead of the speaker
D. Band-reject filter
(D) T7B07 HRLM (9 - 9)

---
What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor about the rules that prohibit the use of devices that cause interference
C. Check your station and make sure it meets the standards of good amateur practice
D. All of these choices are correct
 T7B08 HRLM (9 - 10)

---
What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor about the rules that prohibit the use of devices that cause interference
C. Check your station and make sure it meets the standards of good amateur practice
D. All of these choices are correct
(D) T7B08 HRLM (9 - 10)

---
What is a Part 15 device?_clipboard1
What is a Part 15 device?
A. An unlicensed device that may emit low-powered radio signals on frequencies used by a licensed service
B. An amplifier that has been type-certified for amateur radio
C. A device for long-distance communications using special codes sanctioned by the International Amateur Radio Union
D. A type of test set used to determine whether a transmitter complies with FCC regulation 91.15
 T7B09 HRLM (9 - 10)

---
What is a Part 15 device?
What is a Part 15 device?
A. An unlicensed device that may emit low-powered radio signals on frequencies used by a licensed service
B. An amplifier that has been type-certified for amateur radio
C. A device for long-distance communications using special codes sanctioned by the International Amateur Radio Union
D. A type of test set used to determine whether a transmitter complies with FCC regulation 91.15
(A) T7B09 HRLM (9 - 10)

---
What might be a problem if you receive a report that your audio signal through the repeater is distorted or unintelligible?
A. Your transmitter is slightly off frequency
B. Your batteries are running low
C. You are in a bad location
D. All of these choices are correct
 T7B10 HRLM (6 - 5)

---
What might be a problem if you receive a report that your audio signal through the repeater is distorted or unintelligible?
A. Your transmitter is slightly off frequency
B. Your batteries are running low
C. You are in a bad location
D. All of these choices are correct
(D) T7B10 HRLM (6 - 5)

---
What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible voice transmissions
D. Frequent blowing of power supply fuses
 T7B11 HRLM (9 - 6)

---
What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible voice transmissions
D. Frequent blowing of power supply fuses
(C) T7B11 HRLM (9 - 6)

---
What should be the first step to resolve cable TV interference from your ham radio transmission?
A. Add a low-pass filter to the TV antenna input
B. Add a high-pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV coaxial connectors are installed properly
 T7B12 HRLM (9 - 9)

---
What should be the first step to resolve cable TV interference from your ham radio transmission?
A. Add a low-pass filter to the TV antenna input
B. Add a high-pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV coaxial connectors are installed properly
(D) T7B12 HRLM (9 - 9)
Loose connection would allow signal
In where it shouldnt be, and might also even
Function as a demodulator.

---
What is the primary purpose of a dummy load?_clipboard0
What is the primary purpose of a dummy load?
A. To prevent transmitting signals over the air when making tests
B. To prevent over-modulation of a transmitter
C. To improve the efficiency of an antenna
D. To improve the signal-to-noise ratio of a receiver
 T7C01 HRLM (5 - 7)

---
What is the primary purpose of a dummy load?
What is the primary purpose of a dummy load?
A. To prevent transmitting signals over the air when making tests
B. To prevent over-modulation of a transmitter
C. To improve the efficiency of an antenna
D. To improve the signal-to-noise ratio of a receiver
(A) T7C01 HRLM (5 - 7)

---
Which of the following instruments can be used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter
 T7C02 HRLM (4 - 19)

---
Which of the following instruments can be used to determine if an antenna is resonant at the desired operating frequency?
A. A VTVM
B. An antenna analyzer
C. A Q meter
D. A frequency counter
(B) T7C02 HRLM (4 - 19)
There are other ways also – like an SWR
Meter.

---
What, in general terms, is standing wave ratio (SWR)?_clipboard1
What, in general terms, is standing wave ratio (SWR)?
A. A measure of how well a load is matched to a transmission line
B. The ratio of high to low impedance in a feed line
C. The transmitter efficiency ratio
D. An indication of the quality of your station’s ground connection
 T7C03 HRLM (4 - 11)

---
What, in general terms, is standing wave ratio (SWR)?
What, in general terms, is standing wave ratio (SWR)?
A. A measure of how well a load is matched to a transmission line
B. The ratio of high to low impedance in a feed line
C. The transmitter efficiency ratio
D. An indication of the quality of your station’s ground connection
(A) T7C03 HRLM (4 - 11)

---
What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 2 to 1
B. 1 to 3
C. 1 to 1
D. 10 to 1
 T7C04 HRLM (4 - 11)

---
What reading on an SWR meter indicates a perfect impedance match between the antenna and the feed line?
A. 2 to 1
B. 1 to 3
C. 1 to 1
D. 10 to 1
(C) T7C04 HRLM (4 - 11)

---
Why do most solid-state amateur radio transmitters reduce output power as SWR increases?
A. To protect the output amplifier transistors
B. To comply with FCC rules on spectral purity
C. Because power supplies cannot supply enough current at high SWR
D. To improve the impedance match to the feed line
 T7C05 HRLM (4 - 11)

---
Why do most solid-state amateur radio transmitters reduce output power as SWR increases?
A. To protect the output amplifier transistors
B. To comply with FCC rules on spectral purity
C. Because power supplies cannot supply enough current at high SWR
D. To improve the impedance match to the feed line
(A) T7C05 HRLM (4 - 11)
High SWR can cause excessive VOLTAGE or
CURRENT in those transistors – and typically they
Can be destroyed by excessive voltage. Transmitting
Without an antenna connected to a handitalkie….
Can blow it in moments…

---
What does an SWR reading of 4:1 indicate?_clipboard2
What does an SWR reading of 4:1 indicate?
A. Loss of -4 dB
B. Good impedance match
C. Gain of +4 dB
D. Impedance mismatch
 T7C06 HRLM (4 - 11)

---
What does an SWR reading of 4:1 indicate?
What does an SWR reading of 4:1 indicate?
A. Loss of -4 dB
B. Good impedance match
C. Gain of +4 dB
D. Impedance mismatch
(D) T7C06 HRLM (4 - 11)

---
What happens to power lost in a feed line?_clipboard3
What happens to power lost in a feed line?
A. It increases the SWR
B. It comes back into your transmitter and could cause damage
C. It is converted into heat
D. It can cause distortion of your signal
 T7C07 HRLM (4 - 9)

---
What happens to power lost in a feed line?
What happens to power lost in a feed line?
A. It increases the SWR
B. It comes back into your transmitter and could cause damage
C. It is converted into heat
D. It can cause distortion of your signal
(C) T7C07 HRLM (4 - 9)
Things that increase the loss of power in COAX:
a) higher frequency
b) longer length
c) skinnier coax
d) BAD SWR!!!!

---
What instrument other than an SWR meter could you use to determine if a feed line and antenna are properly matched?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter
 T7C08 HRLM (4 - 19)

---
What instrument other than an SWR meter could you use to determine if a feed line and antenna are properly matched?
A. Voltmeter
B. Ohmmeter
C. Iambic pentameter
D. Directional wattmeter
(D) T7C08 HRLM (4 - 19)

---
Which of the following is the most common cause for failure of coaxial cables?
A. Moisture contamination
B. Gamma rays
C. The velocity factor exceeds 1.0
D. Overloading
 T7C09 HRLM (4 - 17)

---
Which of the following is the most common cause for failure of coaxial cables?
A. Moisture contamination
B. Gamma rays
C. The velocity factor exceeds 1.0
D. Overloading
(A) T7C09 HRLM (4 - 17)

---
Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable
 T7C10 HRLM (4 - 17)

---
Why should the outer jacket of coaxial cable be resistant to ultraviolet light?
A. Ultraviolet resistant jackets prevent harmonic radiation
B. Ultraviolet light can increase losses in the cable’s jacket
C. Ultraviolet and RF signals can mix, causing interference
D. Ultraviolet light can damage the jacket and allow water to enter the cable
(D) T7C10 HRLM (4 - 17)

---
What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent water absorption
D. It cannot be used at below freezing temperatures
 T7C11 HRLM (4 - 18)

---
What is a disadvantage of air core coaxial cable when compared to foam or solid dielectric types?
A. It has more loss per foot
B. It cannot be used for VHF or UHF antennas
C. It requires special techniques to prevent water absorption
D. It cannot be used at below freezing temperatures
(C) T7C11 HRLM (4 - 18)

---
What does a dummy load consist of?_clipboard4
What does a dummy load consist of?
A. A high-gain amplifier and a TR switch
B. A non-inductive resistor and a heat sink
C. A low-voltage power supply and a DC relay
D. A 50 ohm reactance used to terminate a transmission line
 T7C12 HRLM (5 - 7)

---
What does a dummy load consist of?
What does a dummy load consist of?
A. A high-gain amplifier and a TR switch
B. A non-inductive resistor and a heat sink
C. A low-voltage power supply and a DC relay
D. A 50 ohm reactance used to terminate a transmission line
(B) T7C12 HRLM (5 - 7)

---
Which instrument would you use to measure electric potential or electromotive force?
A. An ammeter
B. A voltmeter
C. A wavemeter
D. An ohmmeter
 T7D01 HRLM (3 - 2)

---
Which instrument would you use to measure electric potential or electromotive force?
A. An ammeter
B. A voltmeter
C. A wavemeter
D. An ohmmeter
(B) T7D01 HRLM (3 - 2)

---
What is the correct way to connect a voltmeter to a circuit?_clipboard0
What is the correct way to connect a voltmeter to a circuit?
A. In series with the circuit
B. In parallel with the circuit
C. In quadrature with the circuit
D. In phase with the circuit
 T7D02 HRLM (3 - 3)

---
What is the correct way to connect a voltmeter to a circuit?
What is the correct way to connect a voltmeter to a circuit?
A. In series with the circuit
B. In parallel with the circuit
C. In quadrature with the circuit
D. In phase with the circuit
(B) T7D02 HRLM (3 - 3)

---
How is a simple ammeter connected to a circuit?_clipboard1
How is a simple ammeter connected to a circuit?
A. In series with the circuit
B. In parallel with the circuit
C. In quadrature with the circuit
D. In phase with the circuit
 T7D03 HRLM (3 - 3)

---
How is a simple ammeter connected to a circuit?
How is a simple ammeter connected to a circuit?
A. In series with the circuit
B. In parallel with the circuit
C. In quadrature with the circuit
D. In phase with the circuit
(A) T7D03 HRLM (3 - 3)

---
Which instrument is used to measure electric current?_clipboard2
Which instrument is used to measure electric current?
A. An ohmmeter
B. A wavemeter
C. A voltmeter
D. An ammeter
 T7D04 HRLM (3 - 1)

---
Which instrument is used to measure electric current?
Which instrument is used to measure electric current?
A. An ohmmeter
B. A wavemeter
C. A voltmeter
D. An ammeter
(D) T7D04 HRLM (3 - 1)

---
What instrument is used to measure resistance?_clipboard3
What instrument is used to measure resistance?
A. An oscilloscope
B. A spectrum analyzer
C. A noise bridge
D. An ohmmeter
 T7D05 HRLM (3 - 5)

---
What instrument is used to measure resistance?
What instrument is used to measure resistance?
A. An oscilloscope
B. A spectrum analyzer
C. A noise bridge
D. An ohmmeter
(D) T7D05 HRLM (3 - 5)

---
Which of the following might damage a multimeter?_clipboard4
Which of the following might damage a multimeter?
A. Measuring a voltage too small for the chosen scale
B. Leaving the meter in the milliamps position overnight
C. Attempting to measure voltage when using the resistance setting
D. Not allowing it to warm up properly
 T7D06 HRLM (3 - 4)

---
Which of the following might damage a multimeter?
Which of the following might damage a multimeter?
A. Measuring a voltage too small for the chosen scale
B. Leaving the meter in the milliamps position overnight
C. Attempting to measure voltage when using the resistance setting
D. Not allowing it to warm up properly
(C) T7D06 HRLM (3 - 4)

---
Which of the following measurements are commonly made using a multimeter?
A. SWR and RF power
B. Signal strength and noise
C. Impedance and reactance
D. Voltage and resistance
 T7D07 HRLM (3 - 4)

---
Which of the following measurements are commonly made using a multimeter?
A. SWR and RF power – requires SWR meter/powermeter
B. Signal strength and noise – requires receiver
C. Impedance and reactance – requires ANTENNA ANALYZER
D. Voltage and resistance-- (can be done by multimeter)
(D) T7D07 HRLM (3 - 4)

---
Which of the following types of solder is best for radio and electronic use?
A. Acid-core solder
B. Silver solder
C. Rosin-core solder
D. Aluminum solder
 T7D08 HRLM (4 - 18)

---
Which of the following types of solder is best for radio and electronic use?
A. Acid-core solder
B. Silver solder
C. Rosin-core solder
D. Aluminum solder
(C) T7D08 HRLM (4 - 18)

---
What is the characteristic appearance of a cold solder joint?_clipboard5
What is the characteristic appearance of a cold solder joint?
A. Dark black spots
B. A bright or shiny surface
C. A grainy or dull surface
D. A greenish tint
 T7D09 HRLM (4 - 18)

---
What is the characteristic appearance of a cold solder joint?
What is the characteristic appearance of a cold solder joint?
A. Dark black spots
B. A bright or shiny surface
C. A grainy or dull surface
D. A greenish tint
(C) T7D09 HRLM (4 - 18)

---
What is probably happening when an ohmmeter, connected across an unpowered circuit, initially indicates a low resistance and then shows increasing resistance with time?
A. The ohmmeter is defective
B. The circuit contains a large capacitor
C. The circuit contains a large inductor
D. The circuit is a relaxation oscillator
 T7D10 HRLM (3 - 4)

---
What is probably happening when an ohmmeter, connected across an unpowered circuit, initially indicates a low resistance and then shows increasing resistance with time?
A. The ohmmeter is defective
B. The circuit contains a large capacitor
C. The circuit contains a large inductor
D. The circuit is a relaxation oscillator
(B) T7D10 HRLM (3 - 4)

---
Which of the following precautions should be taken when measuring circuit resistance with an ohmmeter?
A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
C. Ensure that the circuit is grounded
D. Ensure that the circuit is operating at the correct frequency
 T7D11 HRLM (3 - 4)

---
Which of the following precautions should be taken when measuring circuit resistance with an ohmmeter?
A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
C. Ensure that the circuit is grounded
D. Ensure that the circuit is operating at the correct frequency
(B) T7D11 HRLM (3 - 4)

---
Which of the following precautions should be taken when measuring high voltages with a voltmeter?
A. Ensure that the voltmeter has very low impedance
B. Ensure that the voltmeter and leads are rated for use at the voltages to be measured
C. Ensure that the circuit is grounded through the voltmeter
D. Ensure that the voltmeter is set to the correct frequency
 T7D12 HRLM (3 - 4)

---
Which of the following precautions should be taken when measuring high voltages with a voltmeter?
A. Ensure that the voltmeter has very low impedance
B. Ensure that the voltmeter and leads are rated for use at the voltages to be measured
C. Ensure that the circuit is grounded through the voltmeter
D. Ensure that the voltmeter is set to the correct frequency
(B) T7D12 HRLM (3 - 4)