|  | Eimac Power Grid Tube Reference Data |  |
| --- | --- | --- |

| Back to Power Grid Tube Catalog Index Additional Catalogs: Klystrode® IOT ¦ Remanufactured Tube |  |
| --- | --- |

# 3CX800A7

The 3CX800A7 is a compact high-mu power triode intended for use in zero bias class B amplifiers in audio or radio requency applications. It may also be useful as a pulse modulator or regulator. A single 3CX800A7 will deliver 750 watts PEP and 750 watts keydown CW output to 350 MHz. Linearity and power gain are excellent due to the beam forming geometry of the special grid and cathode design.

## Characteristics

| Plate Dissipation (Max.) 800 Watts Screen Dissipation (Max.) --- Watts Grid Dissipation (Max.) 4 Watts Frequency for Max. rating (CW) 350 MHz Amplification Factor 200 Filament/Cathode Oxide Coated Voltage Current 13.5 Volts 1.5 Amps Capacitance Grounded Grid Input Output Feedthrough 26.0 pf 6.1 pf .05 pf Capacitance --- Input Output Feedthrough --- pf --- pf --- pf Cooling Forced Air Base 11 Pin Air Socket SK-1900 Air Chimney SK-1906 Boiler --- Length 2.52 in; 64.01 mm Diameter 2.53 in; 64.26 mm Weight 11.5 oz; 326 gm |  |
| --- | --- |

|  | Maximum Ratings | Typical Operation |
| --- | --- | --- |
| Class of Operation | Type of Service | Plate Voltage (Volts) | Plate current (Amps) | Plate Voltage (Volts) | Screen Voltage (Volts) | Plate Current (Amps) | Drive Power (Watts) | Output Power (kiloWatts) |
| AB2 | Cathode Driven RF Linear Amplifier | 2,,250 | 0.6 | 2,200 | --- | 0.5 | 23 | 0.750 |
| --- | Pulse Modulator or Regulator | 3,500 | 8.0 | --- | --- | --- | --- | --- |

Characteristics and Operating values are based on performance tests. Figures may change without notice as the result of additional data or product refinement. CPI Eimac Division should be consulted before using this information for final equipment design.

Top of Page

Last page update 3/21/97 4:22:48 PM 
Eimac Web Pages © copyright 1996 CPI, Eimac Division