## Slide 1: CHAPTER 3
Electricity, Components and Circuits

## Slide 2: Background and concepts

## Slide 3: Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 4: Voltage, Current and Power
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Unites – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Power (P)
  Watts
  Units – Watts
  Unit Symbol W – 60W
P
I
E
P = I x E
Notes: Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 5: T5A11 What is the basic unit of electromotive force?
  A. The volt
  B. The watt
  C. The ampere
  D. The ohm

## Slide 6: T5A11 What is the basic unit of electromotive force?
A. The volt
  B. The watt
  C. The ampere
  D. The ohm

## Slide 7: T5A01 Electrical current is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
  D. Amperes

## Slide 8: T5A01 Electrical current is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
D. Amperes

## Slide 9: T5A03 What is the name for the flow of electrons in an electric circuit?
  A. Voltage
  B. Resistance
  C. Capacitance
  D. Current

## Slide 10: T5A03 What is the name for the flow of electrons in an electric circuit?
  A. Voltage
  B. Resistance
  C. Capacitance
D. Current

## Slide 11: T5A05 What is the electrical term for the electromotive force (EMF) that causes electron flow?
  A. Voltage
  B. Ampere-hours
  C. Capacitance
  D. Inductance

## Slide 12: T5A05 What is the electrical term for the electromotive force (EMF) that causes electron flow?
A. Voltage
  B. Ampere-hours
  C. Capacitance
  D. Inductance

## Slide 13: T5A10 Which term describes the rate at which electrical energy is used?
  A. Resistance
  B. Current
  C. Power
  D. Voltage

## Slide 14: T5A10 Which term describes the rate at which electrical energy is used?
  A. Resistance
  B. Current
C. Power
  D. Voltage

## Slide 15: T7D01 Which instrument would you use to measure electric potential or electromotive force?
  A. An ammeter
  B. A voltmeter
  C. A wavemeter
  D. An ohmmeter

## Slide 16: T7D01 Which instrument would you use to measure electric potential or electromotive force?
  A. An ammeter
B. A voltmeter
  C. A wavemeter
  D. An ohmmeter

## Slide 17: T7D02 What is the correct way to connect a voltmeter to a circuit?
  A. In series with the circuit
  B. In parallel with the circuit
  C. In quadrature with the circuit
  D. In phase with the circuit

## Slide 18: T7D02 What is the correct way to connect a voltmeter to a circuit?
  A. In series with the circuit
B. In parallel with the circuit
  C. In quadrature with the circuit
  D. In phase with the circuit

## Slide 19: T7D03 How is an ammeter usually connected to a circuit?
  A. In series with the circuit
  B. In parallel with the circuit
  C. In quadrature with the circuit
  D. In phase with the circuit

## Slide 20: T7D03 How is an ammeter usually connected to a circuit?
A. In series with the circuit
  B. In parallel with the circuit
  C. In quadrature with the circuit
  D. In phase with the circuit

## Slide 21: T5A07 Which of the following is a good electrical conductor?
  A. Glass
  B. Wood
  C. Copper
  D. Rubber

## Slide 22: T5A07 Which of the following is a good electrical conductor?
  A. Glass
  B. Wood
C. Copper
  D. Rubber

## Slide 23: T7D04 Which instrument is used to measure electric current?
  A. An ohmmeter
  B. A wavemeter
  C. A voltmeter
  D. An ammeter

## Slide 24: T7D04 Which instrument is used to measure electric current?
  A. An ohmmeter
  B. A wavemeter
  C. A voltmeter
D. An ammeter

## Slide 25: T5A08 Which of the following is a good electrical insulator?
  A. Copper
  B. Glass
  C. Aluminum
  D. Mercury

## Slide 26: T5A08 Which of the following is a good electrical insulator?
  A. Copper
B. Glass
  C. Aluminum
  D. Mercury

## Slide 27: T5D01 What formula is used to calculate current in a circuit?
  A. Current (I) equals voltage (E) multiplied by resistance (R)
  B. Current (I) equals voltage (E) divided by resistance (R)
  C. Current (I) equals voltage (E) added to resistance (R)
  D. Current (I) equals voltage (E) minus resistance (R)

## Slide 28: Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 29: T5D01 What formula is used to calculate current in a circuit?
  A. Current (I) equals voltage (E) multiplied by resistance (R)
B. Current (I) equals voltage (E) divided by resistance (R)
  C. Current (I) equals voltage (E) added to resistance (R)
  D. Current (I) equals voltage (E) minus resistance (R)

## Slide 30: T5D02 What formula is used to calculate voltage in a circuit?
  A. Voltage (E) equals current (I) multiplied by resistance (R)
  B. Voltage (E) equals current (I) divided by resistance (R)
  C. Voltage (E) equals current (I) added to resistance (R)
  D. Voltage (E) equals current (I) minus resistance (R)

## Slide 31: Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 32: T5D02 What formula is used to calculate voltage in a circuit?
A. Voltage (E) equals current (I) multiplied by resistance (R)
  B. Voltage (E) equals current (I) divided by resistance (R)
  C. Voltage (E) equals current (I) added to resistance (R)
  D. Voltage (E) equals current (I) minus resistance (R)

## Slide 33: T5D03 What formula is used to calculate resistance in a circuit?
  A. Resistance (R) equals voltage (E) multiplied by current (I)
  B. Resistance (R) equals voltage (E) divided by current (I)
  C. Resistance (R) equals voltage (E) added to current (I)
  D. Resistance (R) equals voltage (E) minus current (I)

## Slide 34: Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
To solve for a value, cover it with your finger and solve the remaining formula
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 35: T5D03 What formula is used to calculate resistance in a circuit?
  A. Resistance (R) equals voltage (E) multiplied by current (I)
B. Resistance (R) equals voltage (E) divided by current (I)
  C. Resistance (R) equals voltage (E) added to current (I)
  D. Resistance (R) equals voltage (E) minus current (I)

## Slide 36: T5D04 What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
  A. 3 ohms
  B. 30 ohms
  C. 93 ohms
  D. 270 ohms

## Slide 37: T5D04 What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
E
I
R
R = E / I
R = 90 V  3 A = 30Ω
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 38: T5D04 What is the resistance of a circuit in which a current of 3 amperes flows through a resistor connected to 90 volts?
  A. 3 ohms
B. 30 ohms
  C. 93 ohms
  D. 270 ohms

## Slide 39: T5D05 What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
  A. 18 ohms
  B. 0.125 ohms
  C. 8 ohms
  D. 13.5 ohms

## Slide 40: T5D05 What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
E
I
R
R = E / I
R = 12 V  1.5 A = 8 Ω
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 41: T5D05 What is the resistance in a circuit for which the applied voltage is 12 volts and the current flow is 1.5 amperes?
  A. 18 ohms
  B. 0.125 ohms
C. 8 ohms
  D. 13.5 ohms

## Slide 42: T5D06 What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
  A. 3 ohms
  B. 16 ohms
  C. 48 ohms
  D. 8 Ohms

## Slide 43: T5D06 What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
E
I
R
R = E / I
R = 12 V  4 A = 3 Ω
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 44: T5D06 What is the resistance of a circuit that draws 4 amperes from a 12-volt source?
A. 3 ohms
  B. 16 ohms
  C. 48 ohms
  D. 8 Ohms

## Slide 45: T5D07 What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
  D. 1.5 amperes

## Slide 46: T5D07 What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
E
I
R
I = E / R
I = 120V  80Ω = 1.5A
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 47: T5D07 What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
D. 1.5 amperes

## Slide 48: T5D08 What is the current flowing through a 100-ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
  C. 2 amperes
  D. 100 amperes

## Slide 49: T5D08 What is the current flowing through a 100-ohm resistor connected across 200 volts?
E
I
R
I = E / R
I = 200V  100Ω = 2 A
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 50: T5D08 What is the current flowing through a 100-ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
C. 2 amperes
  D. 100 amperes

## Slide 51: T5D09 What is the current flowing through a 24-ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
  C. 10 amperes
  D. 216 amperes

## Slide 52: T5D09 What is the current flowing through a 24-ohm resistor connected across 240 volts?
E
I
R
I = E / R
I = 240V  24Ω = 10 A
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 53: T5D09 What is the current flowing through a 24-ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
C. 10 amperes
  D. 216 amperes

## Slide 54: T5D10 What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
  A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts

## Slide 55: T5D10 What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
E
I
R
E = I * R
E = 0.5A x 2Ω = 1V
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 56: T5D10 What is the voltage across a 2-ohm resistor if a current of 0.5 amperes flows through it?
A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts

## Slide 57: T5D11 What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
  A. 1 volt
  B. 10 volts
  C. 11 volts
  D. 9 volts

## Slide 58: T5D11 What is the voltage across a 10-ohm resistor if a current of 1 amperes flows through it?
E
I
R
E = I * R
E = 1 A x 10Ω = 10V
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 59: T5D11 What is the voltage across a 10-ohm resistor if a current of 1 ampere flows through it?
  A. 1 volt
B. 10 volts
  C. 11 volts
  D. 9 volts

## Slide 60: T5D12 What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
  A. 8 volts
  B. 0.2 volts
  C. 12 volts
  D. 20 volts

## Slide 61: T5D12 What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
E
I
R
E = I * R
E = 2 A x 10Ω = 20V
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 62: T5D12 What is the voltage across a 10-ohm resistor if a current of 2 amperes flows through it?
  A. 8 volts
  B. 0.2 volts
  C. 12 volts
  D. 20 volts

## Slide 63: T7D05 What instrument is used to measure resistance?
  A. An oscilloscope
  B. A spectrum analyzer
  C. A noise bridge
  D. An ohmmeter

## Slide 64: T7D05 What instrument is used to measure resistance?
  A. An oscilloscope
  B. A spectrum analyzer
  C. A noise bridge
D. An ohmmeter

## Slide 65: T7D11 Which of the following precautions should be taken when measuring circuit resistance with an ohmmeter?
  A. Ensure that the applied voltages are correct
  B. Ensure that the circuit is not powered
  C. Ensure that the circuit is grounded
  D. Ensure that the circuit is operating at the correct frequency

## Slide 66: T7D11 Which of the following precautions should be taken when measuring circuit resistance with an ohmmeter?
  A. Ensure that the applied voltages are correct
B. Ensure that the circuit is not powered
  C. Ensure that the circuit is grounded
  D. Ensure that the circuit is operating at the correct frequency

## Slide 67: T7D12 Which of the following precautions should be taken when measuring high voltages with a voltmeter?
A. Ensure that the voltmeter has very low impedance
B. Ensure that the voltmeter and leads are rated for use at the voltages to be measured
C. Ensure that the circuit is grounded through the voltmeter
D. Ensure that the voltmeter is set to the correct frequency

## Slide 68: T7D12 Which of the following precautions should be taken when measuring high voltages with a voltmeter?
A. Ensure that the voltmeter has very low impedance
B. Ensure that the voltmeter and leads are rated for use at the voltages to be measured
C. Ensure that the circuit is grounded through the voltmeter
D. Ensure that the voltmeter is set to the correct frequency

## Slide 69: T7D07 Which of the following measurements are commonly made using a multimeter?
  A. SWR and RF power
  B. Signal strength and noise
  C. Impedance and reactance
  D. Voltage and resistance

## Slide 70: T7D07 Which of the following measurements are commonly made using a multimeter?
  A. SWR and RF power
  B. Signal strength and noise
  C. Impedance and reactance
D. Voltage and resistance

## Slide 71: T7D06 Which of the following might damage a multimeter?
  A. Measuring a voltage too small for the chosen scale
  B. Leaving the meter in the milliamps position overnight
  C. Attempting to measure voltage when using the resistance setting
  D. Not allowing it to warm up properly

## Slide 72: T7D06 Which of the following might damage a multimeter?
  A. Measuring a voltage too small for the chosen scale
  B. Leaving the meter in the milliamps position overnight
C. Attempting to measure voltage when using the resistance setting
  D. Not allowing it to warm up properly

## Slide 73: T7D10 What is probably happening when an ohmmeter, connected across an unpowered circuit, initially indicates a low resistance and then shows increasing resistance with time?
A. The ohmmeter is defective
B. The circuit contains a large capacitor
C. The circuit contains a large inductor
D. The circuit is a relaxation oscillator

## Slide 74: T7D10 What is probably happening when an ohmmeter, connected across an unpowered circuit, initially indicates a low resistance and then shows increasing resistance with time?
A. The ohmmeter is defective
B. The circuit contains a large capacitor
C. The circuit contains a large inductor
D. The circuit is a relaxation oscillator

## Slide 75: T5A02 Electrical power is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
  D. Amperes

## Slide 76: T5A02 Electrical power is measured in which of the following units?
  A. Volts
B. Watts
  C. Ohms
  D. Amperes

## Slide 77: Direct Current Alternating Current
DC
Current flows in one direction only
  Examples:
    Battery Operated Devices
    Cars
AC
Current flows in both directions, voltage and current very with time
  Example: House Wiring

## Slide 78: T5A04 What is the name for a current that flows only in one direction?
  A. Alternating current
  B. Direct current
  C. Normal current
  D. Smooth current

## Slide 79: T5A04 What is the name for a current that flows only in one direction?
  A. Alternating current
B. Direct current
  C. Normal current
  D. Smooth current

## Slide 80: T5A09 What is the name for a current that reverses direction on a regular basis?
  A. Alternating current
  B. Direct current
  C. Circular current
  D. Vertical current

## Slide 81: T5A09 What is the name for a current that reverses direction on a regular basis?
A. Alternating current
  B. Direct current
  C. Circular current
  D. Vertical current

## Slide 82: Voltage, Current and Power
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Unites – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Power (P)
  Watts
  Units – Watts
  Unit Symbol W – 60W
P
I
E
P = I x E
Notes: Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician. I is used as the abbreviation because it referred to the Intensity of the current.
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 83: T5C08 What is the formula used to calculate electrical power in a DC circuit?
  A. Power (P) equals voltage (E) multiplied by current (I)
  B. Power (P) equals voltage (E) divided by current (I)
  C. Power (P) equals voltage (E) minus current (I)
  D. Power (P) equals voltage (E) plus current (I)

## Slide 84: T5C08 What is the formula used to calculate electrical power in a DC circuit?
A. Power (P) equals voltage (E) multiplied by current (I)
  B. Power (P) equals voltage (E) divided by current (I)
  C. Power (P) equals voltage (E) minus current (I)
  D. Power (P) equals voltage (E) plus current (I)

## Slide 85: T5C09 How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
  A. 138 watts
  B. 0.7 watts
  C. 23.8 watts
  D. 3.8 watts

## Slide 86: T5C09 How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
P
I
E
P = I x E
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 87: T5C09 How much power is being used in a circuit when the applied voltage is 13.8 volts DC and the current is 10 amperes?
A. 138 watts
  B. 0.7 watts
  C. 23.8 watts
  D. 3.8 watts

## Slide 88: T5C10 How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
  A. 4.8 watts
  B. 30 watts
  C. 14.5 watts
  D. 0.208 watts

## Slide 89: T5C10 How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
P
I
E
P = I * E
P = 2.5 A x 12 V = 30 W
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 90: T5C10 How much power is being used in a circuit when the applied voltage is 12 volts DC and the current is 2.5 amperes?
  A. 4.8 watts
B. 30 watts
  C. 14.5 watts
  D. 0.208 watts

## Slide 91: T5C11 How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
  A. 0.1 amperes
  B. 10 amperes
  C. 12 amperes
  D. 132 amperes

## Slide 92: T5C11 How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
P
I
E
I = P / E
I = 120 W  12 VDC = 10A
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 93: T5C11 How many amperes are flowing in a circuit when the applied voltage is 12 volts DC and the load is 120 watts?
  A. 0.1 amperes
B. 10 amperes
  C. 12 amperes
  D. 132 amperes

## Slide 94: T5C01 What is the ability to store energy in an electric field called?
  A. Inductance
  B. Resistance
  C. Tolerance
  D. Capacitance

## Slide 95: T5C01 What is the ability to store energy in an electric field called?
  A. Inductance
  B. Resistance
  C. Tolerance
D. Capacitance

## Slide 96: T5C02 What is the basic unit of capacitance?
  A. The farad
  B. The ohm
  C. The volt
  D. The henry

## Slide 97: T5C02 What is the basic unit of capacitance?
A. The farad
  B. The ohm
  C. The volt
  D. The henry

## Slide 98: T5C03 What is the ability to store energy in a magnetic field called?
  A. Admittance
  B. Capacitance
  C. Resistance
  D. Inductance

## Slide 99: T5C03 What is the ability to store energy in a magnetic field called?
  A. Admittance
  B. Capacitance
  C. Resistance
D. Inductance

## Slide 100: T5C04 What is the basic unit of inductance?
  A. The coulomb
  B. The farad
  C. The henry
  D. The ohm

## Slide 101: T5C04 What is the basic unit of inductance?
  A. The coulomb
  B. The farad
C. The henry
  D. The ohm

## Slide 102: T6A01 What electrical component is used to oppose the flow of current in a DC circuit?
  A. Inductor
  B. Resistor
  C. Voltmeter
  D. Transformer

## Slide 103: T6A01 What electrical component is used to oppose the flow of current in a DC circuit?
  A. Inductor
B. Resistor
  C. Voltmeter
  D. Transformer

## Slide 104: T6A02 What type of component is often used as an adjustable volume control?
  A. Fixed resistor
  B. Power resistor
  C. Potentiometer
  D. Transformer

## Slide 105: T6A02 What type of component is often used as an adjustable volume control?
  A. Fixed resistor
  B. Power resistor
C. Potentiometer
  D. Transformer

## Slide 106: T6A03 What electrical parameter is controlled by a potentiometer?
  A. Inductance
  B. Resistance
  C. Capacitance
  D. Field strength

## Slide 107: T6A03 What electrical parameter is controlled by a potentiometer?
  A. Inductance
B. Resistance
  C. Capacitance
  D. Field strength

## Slide 108: T6A04 What electrical component stores energy in an electric field?
  A. Resistor
  B. Capacitor
  C. Inductor
  D. Diode

## Slide 109: T6A04 What electrical component stores energy in an electric field?
  A. Resistor
B. Capacitor
  C. Inductor
  D. Diode

## Slide 110: T6A05 What type of electrical component consists of two or more conductive surfaces separated by an insulator?
  A. Resistor
  B. Potentiometer
  C. Oscillator
  D. Capacitor

## Slide 111: T6A05 What type of electrical component consists of two or more conductive surfaces separated by an insulator?
  A. Resistor
  B. Potentiometer
  C. Oscillator
D. Capacitor

## Slide 112: T6A06 What type of electrical component stores energy in a magnetic field?
  A. Resistor
  B. Capacitor
  C. Inductor
  D. Diode

## Slide 113: T6A06 What type of electrical component stores energy in a magnetic field?
  A. Resistor
  B. Capacitor
C. Inductor
  D. Diode

## Slide 114: T6A07 What electrical component is usually composed of a coil of wire?
  A. Switch
  B. Capacitor
  C. Diode
  D. Inductor

## Slide 115: T6A07 What electrical component is usually composed of a coil of wire?
  A. Switch
  B. Capacitor
  C. Diode
D. Inductor

## Slide 116: T6D06 What component is commonly used to change 120V AC house current to a lower AC voltage for other uses?
  A. Variable capacitor
  B. Transformer
  C. Transistor
  D. Diode

## Slide 117: T6D06 What component is commonly used to change 120V AC house current to a lower AC voltage for other uses?
  A. Variable capacitor
B. Transformer
  C. Transistor
  D. Diode

## Slide 118: T5C12 What is meant by the term impedance?
A. It is a measure of the opposition to AC current flow in a circuit
B. It is the inverse of resistance
C. It is a measure of the Q or Quality Factor of a component
D. It is a measure of the power handling capability of a component

## Slide 119: T5C12 What is meant by the term impedance?
A. It is a measure of the opposition to AC current flow in a circuit
B. It is the inverse of resistance
C. It is a measure of the Q or Quality Factor of a component
D. It is a measure of the power handling capability of a component

## Slide 120: T6D08 Which of the following is used together with an inductor to make a tuned circuit?
  A. Resistor
  B. Zener diode
  C. Potentiometer
  D. Capacitor

## Slide 121: T6D08 Which of the following is used together with an inductor to make a tuned circuit?
  A. Resistor
  B. Zener diode
  C. Potentiometer
D. Capacitor

## Slide 122: T5C13 What are the units of impedance?
A. Volts
B. Ampères
C. Coulombs
D. Ohms

## Slide 123: T5C13 What are the units of impedance?
A. Volts
B. Ampères
C. Coulombs
D. Ohms

## Slide 124: T6D09 What is the name of a device that combines several semiconductors and other components into one package?
  A. Transducer
  B. Multi-pole relay
  C. Integrated circuit
  D. Transformer

## Slide 125: T6D09 What is the name of a device that combines several semiconductors and other components into one package?
  A. Transducer
  B. Multi-pole relay
C. Integrated circuit
  D. Transformer

## Slide 126: T6B01 What class of electronic components is capable of using a voltage or current signal to control current flow?
  A. Capacitors
  B. Inductors
  C. Resistors
  D. Transistors

## Slide 127: T6B01 What class of electronic components is capable of using a voltage or current signal to control current flow?
  A. Capacitors
  B. Inductors
  C. Resistors
D. Transistors

## Slide 128: T6B02 What electronic component allows current to flow in only one direction?
  A. Resistor
  B. Fuse
  C. Diode
  D. Driven Element

## Slide 129: T6B02 What electronic component allows current to flow in only one direction?
  A. Resistor
  B. Fuse
C. Diode
  D. Driven Element

## Slide 130: T6B03 Which of these components can be used as an electronic switch or amplifier?
  A. Oscillator
  B. Potentiometer
  C. Transistor
  D. Voltmeter

## Slide 131: T6B03 Which of these components can be used as an electronic switch or amplifier?
  A. Oscillator
  B. Potentiometer
C. Transistor
  D. Voltmeter

## Slide 132: T6B04 Which of the following components can be made of three layers of semiconductor material?
A. Alternator
B. Transistor
C. Triode
D. Pentagrid converter

## Slide 133: T6B04 Which of the following components can be made of three layers of semiconductor material?
A. Alternator
B. Transistor
C. Triode
D. Pentagrid converter

## Slide 134: T6B05 Which of the following electronic components can amplify signals?
  A. Transistor
  B. Variable resistor
  C. Electrolytic capacitor
  D. Multi-cell battery

## Slide 135: T6B05 Which of the following electronic components can amplify signals?
A. Transistor
  B. Variable resistor
  C. Electrolytic capacitor
  D. Multi-cell battery

## Slide 136: T6B06 How is the cathode lead of a semiconductor diode usually identified?
A. With the word cathode
B. With a stripe
C. With the letter C
D. All of these choices are correct

## Slide 137: T6B06 How is the cathode lead of a semiconductor diode usually identified?
A. With the word cathode
B. With a stripe
C. With the letter C
D. All of these choices are correct

## Slide 138: T6B07 What does the abbreviation LED stand for?
A. Low Emission Diode
B. Light Emitting Diode
C. Liquid Emission Detector
D. Long Echo Delay

## Slide 139: T6B07 What does the abbreviation LED stand for?
A. Low Emission Diode
B. Light Emitting Diode
C. Liquid Emission Detector
D. Long Echo Delay

## Slide 140: T6B08 What does the abbreviation FET stand for?
A. Field Effect Transistor
B. Fast Electron Transistor
C. Free Electron Transition
D. Field Emission Thickness

## Slide 141: T6B08 What does the abbreviation FET stand for?
A. Field Effect Transistor
B. Fast Electron Transistor
C. Free Electron Transition
D. Field Emission Thickness

## Slide 142: T6B09 What are the names of the two electrodes of a diode?
  A. Plus and minus
  B. Source and drain
  C. Anode and cathode
  D. Gate and base

## Slide 143: T6B09 What are the names of the two electrodes of a diode?
  A. Plus and minus
  B. Source and drain
C. Anode and cathode
  D. Gate and base

## Slide 144: T6B10 What are the three electrodes of a PNP or NPN transistor?
A. Emitter, base, and collector
B. Source, gate, and drain
C. Cathode, grid, and plate
D. Cathode, drift cavity, and collector

## Slide 145: T6B10 What are the three electrodes of a PNP or NPN transistor?
A. Emitter, base, and collector
B. Source, gate, and drain
C. Cathode, grid, and plate
D. Cathode, drift cavity, and collector

## Slide 146: T6B11 What at are the three electrodes of a field effect transistor?
A. Emitter, base, and collector
B. Source, gate, and drain
C. Cathode, grid, and plate
D. Cathode, gate, and anode

## Slide 147: T6B11 What at are the three electrodes of a field effect transistor?
A. Emitter, base, and collector
B. Source, gate, and drain
C. Cathode, grid, and plate
D. Cathode, gate, and anode

## Slide 148: T6B12 What is the term that describes a transistor's ability to amplify a signal?
  A. Gain
  B. Forward resistance
  C. Forward voltage drop
  D. On resistance

## Slide 149: T6B12 What is the term that describes a transistor's ability to amplify a signal?
A. Gain
  B. Forward resistance
  C. Forward voltage drop
  D. On resistance

## Slide 150: T6D01 Which of the following devices or circuits changes an alternating current into a varying direct current signal?
  A. Transformer
  B. Rectifier
  C. Amplifier
  D. Reflector

## Slide 151: T6D01 Which of the following devices or circuits changes an alternating current into a varying direct current signal?
  A. Transformer
B. Rectifier
  C. Amplifier
  D. Reflector

## Slide 152: T6D07 Which of the following is commonly used as a visual indicator?
A. LED
B. FET
C. Zener diode
D. Bipolar transistor

## Slide 153: T6D07 Which of the following is commonly used as a visual indicator?
A. LED
B. FET
C. Zener diode
D. Bipolar transistor

## Slide 154: T6D10 What is the function of component 2 in Figure T1?
  A. Give off light when current flows through it
  B. Supply electrical energy
  C. Control the flow of current
  D. Convert electrical energy into radio waves

## Slide 156: T6D10 What is the function of component 2 in Figure T1?
  A. Give off light when current flows through it
  B. Supply electrical energy
C. Control the flow of current
  D. Convert electrical energy into radio waves

## Slide 157: T6D11 What is a simple resonant or tuned circuit?
A. An inductor and a capacitor connected in series or parallel to form a filter
B. A type of voltage regulator
C. A resistor circuit used for reducing standing wave ratio
D. A circuit designed to provide high fidelity audio

## Slide 158: T6D11 What is a simple resonant or tuned circuit?
A. An inductor and a capacitor connected in series or parallel to form a filter
B. A type of voltage regulator
C. A resistor circuit used for reducing standing wave ratio
D. A circuit designed to provide high fidelity audio

## Slide 159: T6A08 What electrical component is used to connect or disconnect electrical circuits?
A. Magnetron
B. Switch
C. Thermistor
D. All of these choices are correct

## Slide 160: T6A08 What electrical component is used to connect or disconnect electrical circuits?
A. Magnetron
B. Switch
C. Thermistor
D. All of these choices are correct

## Slide 161: T6A09 What electrical component is used to protect other circuit components from current overloads?
A. Fuse
B. Capacitor
C. Inductor
D. All of these choices are correct

## Slide 162: T6A09 What electrical component is used to protect other circuit components from current overloads?
A. Fuse
B. Capacitor
C. Inductor
D. All of these choices are correct

## Slide 163: T6D02 What best describes a relay?
A. A switch controlled by an electromagnet
B. A current controlled amplifier
C. An optical sensor
D. A pass transistor

## Slide 164: T6D02 What best describes a relay?
A. A switch controlled by an electromagnet
  B. A current controlled amplifier
  C. An optical sensor
  D. A pass transistor

## Slide 165: T6D03 What type of switch is represented by component 3 in figure T2?
A. Single-pole single-throw
B. Single-pole double-throw
C. Double-pole single-throw
D. Double-pole double-throw

## Slide 167: T6D03 What type of switch is represented by component 3 in figure T2?
A. Single-pole single-throw
B. Single-pole double-throw
C. Double-pole single-throw
D. Double-pole double-throw

## Slide 168: T6D04 Which of the following can be used to display signal strength on a numeric scale?
  A. Potentiometer
  B. Transistor
  C. Meter
  D. Relay

## Slide 169: T6D04 Which of the following can be used to display signal strength on a numeric scale?
  A. Potentiometer
  B. Transistor
C. Meter
  D. Relay

## Slide 170: T0A04 What is the purpose of a fuse in an electrical circuit?
  A. To prevent power supply ripple from damaging a circuit
  B. To interrupt power in case of overload
  C. To limit current to prevent shocks
  D. All of these choices are correct

## Slide 171: T0A04 What is the purpose of a fuse in an electrical circuit?
  A. To prevent power supply ripple from damaging a circuit
B. To interrupt power in case of overload
  C. To limit current to prevent shocks
  D. All of these choices are correct

## Slide 172: T0A05 Why is it unwise to install a 20-ampere fuse in the place of a 5-ampere fuse?
  A. The larger fuse would be likely to blow because it is rated for higher current
  B. The power supply ripple would greatly increase
  C. Excessive current could cause a fire
  D. All of these choices are correct

## Slide 173: T0A05 Why is it unwise to install a 20-ampere fuse in the place of a 5-ampere fuse?
  A. The larger fuse would be likely to blow because it is rated for higher current
  B. The power supply ripple would greatly increase
C. Excessive current could cause a fire
  D. All of these choices are correct

## Slide 174: T6C01 What is the name for standardized representations of components in an electrical wiring diagram?
  A. Electrical depictions
  B. Grey sketch
  C. Schematic symbols
  D. Component callouts

## Slide 175: T6C01 What is the name for standardized representations of components in an electrical wiring diagram?
  A. Electrical depictions
  B. Grey sketch
C. Schematic symbols
  D. Component callouts

## Slide 176: T6C02 What is component 1 in figure T1?
  A. Resistor
  B. Transistor
  C. Battery
  D. Connector

## Slide 178: T6C02 What is component 1 in figure T1?
A. Resistor
  B. Transistor
  C. Battery
  D. Connector

## Slide 179: T6C03 What is component 2 in figure T1?
  A. Resistor
  B. Transistor
  C. Indicator lamp
  D. Connector

## Slide 181: T6C03 What is component 2 in figure T1?
  A. Resistor
B. Transistor
  C. Indicator lamp
  D. Connector

## Slide 182: T6C04 What is component 3 in figure T1?
  A. Resistor
  B. Transistor
  C. Lamp
  D. Ground symbol

## Slide 184: T6C04 What is component 3 in figure T1?
  A. Resistor
  B. Transistor
C. Lamp
  D. Ground symbol

## Slide 185: T6C05 What is component 4 in figure T1?
  A. Resistor
  B. Transistor
  C. Battery
  D. Ground symbol

## Slide 187: T6C05 What is component 4 in figure T1?
  A. Resistor
  B. Transistor
C. Battery
  D. Ground symbol

## Slide 188: T6C06 What is component 6 in figure T2?
  A. Resistor
  B. Capacitor
  C. Regulator IC
  D. Transistor

## Slide 190: T6C06 What is component 6 in figure T2?
  A. Resistor
B. Capacitor
  C. Regulator IC
  D. Transistor

## Slide 191: T6C07 What is component 8 in figure T2?
  A. Resistor
  B. Inductor
  C. Regulator IC
  D. Light emitting diode

## Slide 193: T6C07 What is component 8 in figure T2?
  A. Resistor
  B. Inductor
  C. Regulator IC
D. Light emitting diode

## Slide 194: T6C08 What is component 9 in figure T2?
  A. Variable capacitor
  B. Variable inductor
  C. Variable resistor
  D. Variable transformer

## Slide 196: T6C08 What is component 9 in figure T2?
  A. Variable capacitor
  B. Variable inductor
C. Variable resistor
  D. Variable transformer

## Slide 197: T6C09 What is component 4 in figure T2?
  A. Variable inductor
  B. Double-pole switch
  C. Potentiometer
  D. Transformer

## Slide 199: T6C09 What is component 4 in figure T2?
  A. Variable inductor
  B. Double-pole switch
  C. Potentiometer
D. Transformer

## Slide 200: T6C10 What is component 3 in figure T3?
  A. Connector
  B. Meter
  C. Variable capacitor
  D. Variable inductor

## Slide 202: T6C10 What is component 3 in figure T3?
  A. Connector
  B. Meter
  C. Variable capacitor
D. Variable inductor

## Slide 203: T6C11 What is component 4 in figure T3?
  A. Antenna
  B. Transmitter
  C. Dummy load
  D. Ground

## Slide 205: T6C11 What is component 4 in figure T3?
A. Antenna
  B. Transmitter
  C. Dummy load
  D. Ground

## Slide 206: T6C12 What do the symbols on an electrical circuit schematic diagram represent?
  A. Electrical components
  B. Logic states
  C. Digital codes
  D. Traffic nodes

## Slide 207: T6C12 What do the symbols on an electrical circuit schematic diagram represent?
A. Electrical components
  B. Logic states
  C. Digital codes
  D. Traffic nodes

## Slide 208: T6C13 Which of the following is accurately represented in electrical circuit schematic diagrams?
  A. Wire lengths
  B. Physical appearance of components
  C. The way components are interconnected
  D. All of these choices are correct

## Slide 209: T6C13 Which of the following is accurately represented in electrical circuit schematic diagrams?
  A. Wire lengths
  B. Physical appearance of components
C. The way components are interconnected
  D. All of these choices are correct

## Slide 210: T7A03 Which of the following is used to convert a radio signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier

## Slide 211: T7A03 Which of the following is used to convert a radio signal from one frequency to another?
A. Phase splitter
B. Mixer
C. Inverter
D. Amplifier

## Slide 212: T7A05 What is the name of a circuit that generates a signal of a desired frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator

## Slide 213: T7A05 What is the name of a circuit that generates a signal of a desired frequency?
A. Reactance modulator
B. Product detector
C. Low-pass filter
D. Oscillator

## Slide 214: T7A08 Which of the following describes combining speech with an RF carrier signal?-
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering

## Slide 215: T7A08 Which of the following describes combining speech with an RF carrier signal?-
A. Impedance matching
B. Oscillation
C. Modulation
D. Low-pass filtering

## Slide 216: T7A01 Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion

## Slide 217: T7A01 Which term describes the ability of a receiver to detect the presence of a signal?
A. Linearity
B. Sensitivity
C. Selectivity
D. Total Harmonic Distortion

## Slide 218: T7A04 Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic Distortion

## Slide 219: T7A04 Which term describes the ability of a receiver to discriminate between multiple signals?
A. Discrimination ratio
B. Sensitivity
C. Selectivity
D. Harmonic Distortion

## Slide 220: T7A06 What device takes the output of a low-powered 28 MHz SSB exciter and produces a 222 MHz output signal?
  A. High-pass filter
  B. Low-pass filter
  C. Transverter
  D. Phase converter

## Slide 221: T7A06 What device takes the output of a low-powered 28 MHz SSB exciter and produces a 222 MHz output signal?
  A. High-pass filter
  B. Low-pass filter
C. Transverter
  D. Phase converter

## Slide 222: T7A13 Which of the following circuits demodulates FM signals?
  A. Limiter
  B. Discriminator
  C. Product detector
  D. Phase inverter

## Slide 223: T7A13 Which of the following circuits demodulates FM signals?
  A. Limiter
B. Discriminator
  C. Product detector
  D. Phase inverter