## Slide 1: Technician License Course Chapter 5
Lesson Plan Module 12 –
Power Sources and RF Interference (RFI)

## Slide 2
Power Supplies
Most modern radio equipment runs from 12 volts dc.
  Actual preferred voltage is 13.8 volts.
Household ac power is 120 volts ac.
Power supplies convert 120 volts ac to regulated, filtered dc.
  If you use a lab-type 12 volt power supply, be sure it is adjustable to 13.8 volts.
Notes: Note “power supply” generally refers to converting ac to dc of any voltage, not just 120 VAC to 12 VDC.
Review the reason for “12 V” radios actually requiring 13.8 V – see module 11.

## Slide 3
Types of Power Supplies
Linear:
  Use iron transformers
  Heavy (physically)
  Do not emit RF, generally immune to strong RF
Switching:
  Electronics instead of transformers
  Lightweight and small
  Can emit RF if not properly filtered
    Check product reviews
Notes: Examples of the different kinds of supplies would be helpful to illustrate the differences.
Note that small switching supplies for consumer appliances (under-cabinet lighting, battery charging, etc) are often prolific generators of noise that interferes with communication. Replacing the supply with a linear type will eliminate the noise.

## Slide 4
Power Supply Ratings Voltage and Current
Continuous duty – how much current can be supplied continuously.
Intermittent duty – how much current can be supplied for short surges, such as on voice peaks.
Regulation – how well the power supply maintains a constant output voltage.

## Slide 5
Mobile Power Wiring Safety
Car batteries hold lots of energy – shorting a battery could cause a fire.
Special requirements for safe car wiring:
  Fuse both positive and negative leads.
  Connect radio’s negative lead to negative terminal or engine block ground strap.
  Use grommets or protective sleeves to protect wires.
  Don’t assume all metal in the car is grounded; modern cars are as much plastic as metal.
Notes: The concept of fusing both the negative and positive leads of the equipment in a car installation might take some explanation. The vehicle manufacturer may have specific recommendations in a service bulletin – check with the dealer or an audio/radio installation shop.

## Slide 6
Batteries
Create current through a chemical reaction
  Individual cells connected in series or parallel
  Cell chemistry determines voltage per cell
Battery types
  Disposable (primary batteries)
  Rechargeable (secondary batteries)
  Storage
Energy capabilities rated in Ampere-hours
  Amps X time (at a constant voltage)
Notes: Examples of the different kinds of batteries will help illustrate this point. Discuss how the different kinds of batteries are used.

## Slide 7
Battery Charging
Some batteries can be recharged, some cannot.
Use the proper charger for the battery being charged.
Batteries will lose capacity with each cycle.
Best if batteries are maintained fully charged.
  Over-charging will cause heating and could damage the battery.
Lead-acid batteries release explosive hydrogen during charging or rapid discharge so adequate ventilation is required.
Notes: Make sure the students understand that hazards from hydrogen buildup are real and ventilation is a must – no kidding!

## Slide 8
Battery Charging
Automobiles can be a good emergency power source by recharging batteries
A 12-volt lead-acid station battery can be recharged by connecting it to an automobile’s electrical system
  Monitor battery temperature
  Make sure battery is well-ventilated

## Slide 9
Handheld Transceivers
Battery packs – packages of several individual rechargeable batteries connected together.
  NiCd (nickel-cadmium)
  NiMH (nickel-metal hydride)
  Li-ion (lithium-ion)
For emergencies, have a battery pack that can use disposable batteries (AA size).
Notes: Show several types of battery packs, compare weight and other parameters such as self-discharge, total battery capacity, etc. Note that if commercial power is unavailable, conventional pack chargers won’t work. Need AA-cell packs or chargers that can run from a vehicle’s battery system.

## Slide 10
Radio Frequency Interference (RFI)
Signals that interfere with radio reception.
Interference can be FROM your station or TO your station.
Solving the problem might take a little detective work!

## Slide 11
Types of RFI
Direct detection – offending signals get into the electronic circuits to cause interference.
Overload – strong signal that overwhelms the ability of the receiver to reject it.
RF Current – can be picked up by cables of consumer equipment.
Transmitted harmonics – must be filtered out at the transmitter.
Notes: Discuss briefly with the students these basic types of RFI, and how they might be able to distinguish between them. At the same time, discuss some techniques they might use to mitigate the effects of the interference.
Direct detection usually affects consumer electronic devices (telephones and audio equipment). Poor shielding allows signal to be received within the equipment. Very difficult to eliminate.
Common-mode RF current detection caused by consumer equipment cables picking up RF. Generally not the fault of the amateur. Can be mitigated by proper installation, filters, ferrite bead chokes, etc. ARRL Handbook RFI chapter has examples of using filters and chokes.
Overload – usually seen in fringe reception areas of TV signals. Not as much a problem now days with digital, satellite, and cable TV. Usually the problem can be mitigated by reducing transmitter power or filtering to reject transmitted signal at the receiver.
Harmonics – not common, sometimes due to misadjusted transmitter or bad connection in antenna system

## Slide 12
Filters
Filters attenuate (reduce) signals
High-pass – reduce low-frequency signals
Low-pass – reduce high-frequency signals
Band-pass – only pass a range of signals
Notch – reduces a narrow range of signals
Selecting correct filter requires understanding the source of the interference
Notes: Cover basics of each type of filter, show examples of receiving filters and a transmitting low-pass filter for HF.

## Slide 13
Ferrite Chokes
Creates impedance (opposition to ac) on cables and wires.
Can be used to block RF current that causes interference to entertainment equipment, microphones, monitors, amplifiers, etc.
Wind cable through ferrite core to create blocking impedance.
Notes: Show examples of ferrite cores and snap-on cores. Emphasize that the proper type (mix) of ferrite must be used.

## Slide 14
Cable TV Interference
Usually the result of broken shielding somewhere in the cable.
  Loose connections
  Broken connections
  Corroded connections
Usually solved by proper cable maintenance by cable supplier.
Notes: Note that ham signals can interfere with cable channels or vice versa.

## Slide 15
Noise Sources
Electrical arcs (motors, thermostats, electric fences, neon signs)
Power lines
Motor vehicle ignitions or alternators
Switching power supplies
Computers, networks and TV sets
Notes: Discuss with the students other sources of interfering noise and give them techniques on how to seek out the source of the noise. In many cases of the fixed noise, simply turning off the potentially offending appliance will help identify the source. Power line noise mitigation is the responsibility of the power company. Motor vehicle ignition noise is generally short lived unless it is coming from the hams vehicle. Grounding and filtering in many of these cases will mitigate the noise.
Show students the ARRL website pages on interference.

## Slide 16
RFI Guidelines
Operate your equipment properly.
Eliminate interference in your own home.
Use good station building practices to eliminate unwanted signals.
  Shielded wire and cables
  Shielded equipment
  Good connections and filters

## Slide 17
Dealing with RFI
Take interference complaints seriously.
Make sure that you’re really not the cause (demonstrate that you don’t interfere within your own home).
Offer to help eliminate the RFI, even if you are not at fault.
Consult ARRL RFI Resources for help and assistance.

## Slide 18
Part 15 Rules
Applies only to unlicensed devices
Unlicensed devices may not interfere with licensed services, such as amateur radio
Unlicensed devices must accept any interference they receive from licensed services
RFI from and to unlicensed devices is the responsibility of the users of such devices

## Slide 19
What the Rules Say
Bottom line – If your station is operating properly, you are protected against interference complaints
BUT – Be a good neighbor because they are probably not familiar with Part 15 rules and regulations
Notes: Discuss with the students that though the law is probably on their side, their neighbors will not understand that and they will hold the ham responsible for the interference. It takes diplomacy to deal with RFI complaints.

## Slide 20
Electrical Safety Grounding and Circuit Protection (in the Home)
Make sure your home is “up to code.”
Most ham equipment does not require special wiring or circuits.
  Use 3-wire power cords.
  Use circuit breakers, circuit breaker outlets, or Ground Fault Interrupter (GFI) circuit breakers.
  Use proper fuse or circuit breaker size.
  Don’t overload single outlets.
Notes: It would be a good idea to show the students a properly wired 3-prong plug using proper color code wiring.

## Slide 21
RF “Grounding”
Not the same as ac safety grounding
“Bonding” is more accurate
Keep all equipment at the same RF voltage
  Current will not flow between pieces of equipment which can cause RF feedback
  Minimizes RF “hot spots” (RF burns)
  Use solid strap or wire for best RF connection
Notes: Note that using coax braid is not recommended for RF connections/grounding because once removed from the jacket it begins to lose contact between the braid wires and they also start to oxidize. Use strap or solid wire.

## Slide 22
Practice Questions

## Slide 23: What is one way to recharge a 12-volt lead-acid station battery if the commercial power is out?
A. Cool the battery in ice for several hours
B. Add acid to the battery
C. Connect the battery in parallel with a vehicle's battery and run the engine
D. All of these choices are correct
  T2C02 HRLM (5-18)

## Slide 24: What is one way to recharge a 12-volt lead-acid station battery if the commercial power is out?
A. Cool the battery in ice for several hours
B. Add acid to the battery
C. Connect the battery in parallel with a vehicle's battery and run the engine
D. All of these choices are correct
  T2C02 HRLM (5-18)

## Slide 25: Which is a good reason to use a regulated power supply for communications equipment?
A. It prevents voltage fluctuations from reaching sensitive circuits
B. A regulated power supply has FCC approval
C. A fuse or circuit breaker regulates the power
D. Power consumption is independent of load
  T4A03 HRLM (5-15)

## Slide 26: Which is a good reason to use a regulated power supply for communications equipment?
A. It prevents voltage fluctuations from reaching sensitive circuits
B. A regulated power supply has FCC approval
C. A fuse or circuit breaker regulates the power
D. Power consumption is independent of load
  T4A03 HRLM (5-15)

## Slide 27: Where must a filter be installed to reduce harmonic emissions from your station?
A. Between the transmitter and the antenna
B. Between the receiver and the transmitter
C. At the station power supply
D. At the microphone
  T4A04 HRLM (5-21)

## Slide 28: Where must a filter be installed to reduce harmonic emissions from your station?
A. Between the transmitter and the antenna
B. Between the receiver and the transmitter
C. At the station power supply
D. At the microphone
  T4A04 HRLM (5-21)

## Slide 29: Which type of conductor is best to use for RF grounding?
A. Round stranded wire
B. Round copper-clad steel wire
C. Twisted-pair cable
D. Flat strap
  T4A08 HRLM (5-25)

## Slide 30: Which type of conductor is best to use for RF grounding?
A. Round stranded wire
B. Round copper-clad steel wire
C. Twisted-pair cable
D. Flat strap
  T4A08 HRLM (5-25)

## Slide 31: Which of the following could you use to cure distorted audio caused by RF current flowing on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke
  T4A09 HRLM (5-20)

## Slide 32: Which of the following could you use to cure distorted audio caused by RF current flowing on the shield of a microphone cable?
A. Band-pass filter
B. Low-pass filter
C. Preamplifier
D. Ferrite choke
  T4A09 HRLM (5-20)

## Slide 33: What is the source of a high-pitched whine that varies with engine speed in a mobile transceiver’s receive audio?
A. The ignition system
B. The alternator
C. The electric fuel pump
D. Anti-lock braking system controllers
  T4A10 HRLM (5-16)

## Slide 34: What is the source of a high-pitched whine that varies with engine speed in a mobile transceiver’s receive audio?
A. The ignition system
B. The alternator
C. The electric fuel pump
D. Anti-lock braking system controllers
  T4A10 HRLM (5-16)

## Slide 35: Where should the negative return connection of a mobile transceiver's power cable be connected?
A. At the battery or engine block ground strap
B. At the antenna mount
C. To any metal part of the vehicle
D. Through the transceiver’s mounting bracket
  T4A11 HRLM (5-15)

## Slide 36: Where should the negative return connection of a mobile transceiver's power cable be connected?
A. At the battery or engine block ground strap
B. At the antenna mount
C. To any metal part of the vehicle
D. Through the transceiver’s mounting bracket
  T4A11 HRLM (5-15)

## Slide 37: What could be happening if another operator reports a variable high-pitched whine on the audio from your mobile transmitter?
A. Your microphone is picking up noise from an open window
B. You have the volume on your receiver set too high
C. You need to adjust your squelch control
D. Noise on the vehicle’s electrical system is being transmitted along with your speech audio
  T4A12 HRLM (5-16)

## Slide 38: What could be happening if another operator reports a variable high-pitched whine on the audio from your mobile transmitter?
A. Your microphone is picking up noise from an open window
B. You have the volume on your receiver set too high
C. You need to adjust your squelch control
D. Noise on the vehicle’s electrical system is being transmitted along with your speech audio
  T4A12 HRLM (5-16)

## Slide 39: How much voltage does a mobile transceiver usually require?
A. About 12 volts
B. About 30 volts
C. About 120 volts
D. About 240 volts
  T5A06 HRLM (5-15)

## Slide 40: How much voltage does a mobile transceiver usually require?
A. About 12 volts
B. About 30 volts
C. About 120 volts
D. About 240 volts
  T5A06 HRLM (5-15)

## Slide 41: Which of the following battery types is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid gel-cell
D. All of these choices are correct
  T6A10 HRLM (5-17)

## Slide 42: Which of the following battery types is rechargeable?
A. Nickel-metal hydride
B. Lithium-ion
C. Lead-acid gel-cell
D. All of these choices are correct
  T6A10 HRLM (5-17)

## Slide 43: Which of the following battery types is not rechargeable?
A. Nickel-cadmium
B. Carbon-zinc
C. Lead-acid
D. Lithium-ion
  T6A11 HRLM (5-17)

## Slide 44: Which of the following battery types is not rechargeable?
A. Nickel-cadmium
B. Carbon-zinc
C. Lead-acid
D. Lithium-ion
  T6A11 HRLM (5-17)

## Slide 45: What type of circuit controls the amount of voltage from a power supply?
A. Regulator
B. Oscillator
C. Filter
D. Phase inverter
  T6D05 HRLM (5-15)

## Slide 46: What type of circuit controls the amount of voltage from a power supply?
A. Regulator
B. Oscillator
C. Filter
D. Phase inverter
  T6D05 HRLM (5-15)

## Slide 47: Which is of the following is a common reason to use shielded wire?
A. To decrease the resistance of DC power connections
B. To increase the current carrying capability of the wire
C. To prevent coupling of unwanted signals to or from the wire
D. To couple the wire to other signals
  T6D12 HRLM (5-22)

## Slide 48: Which is of the following is a common reason to use shielded wire?
A. To decrease the resistance of DC power connections
B. To increase the current carrying capability of the wire
C. To prevent coupling of unwanted signals to or from the wire
D. To couple the wire to other signals
  T6D12 HRLM (5-22)

## Slide 49: What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is susceptible to strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low
  T7B02 HRLM (5-21)

## Slide 50: What would cause a broadcast AM or FM radio to receive an amateur radio transmission unintentionally?
A. The receiver is susceptible to strong signals outside the AM or FM band
B. The microphone gain of the transmitter is turned up too high
C. The audio amplifier of the transmitter is overloaded
D. The deviation of an FM transmitter is set too low
  T7B02 HRLM (5-21)

## Slide 51: Which of the following may be a cause of radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct
  T7B03 HRLM (5-19)

## Slide 52: Which of the following may be a cause of radio frequency interference?
A. Fundamental overload
B. Harmonics
C. Spurious emissions
D. All of these choices are correct
  T7B03 HRLM (5-19)

## Slide 53: Which of the following is a way to reduce or eliminate interference by an amateur transmitter to a nearby telephone?
A. Put a filter on the amateur transmitter
B. Reduce the microphone gain
C. Reduce the SWR on the transmitter transmission line
D. Put a RF filter on the telephone
  T7B04 HRLM (5-21)

## Slide 54: Which of the following is a way to reduce or eliminate interference by an amateur transmitter to a nearby telephone?
A. Put a filter on the amateur transmitter
B. Reduce the microphone gain
C. Reduce the SWR on the transmitter transmission line
D. Put a RF filter on the telephone
  T7B04 HRLM (5-21)

## Slide 55: How can overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode
  T7B05 HRLM (5-21)

## Slide 56: How can overload of a non-amateur radio or TV receiver by an amateur signal be reduced or eliminated?
A. Block the amateur signal with a filter at the antenna input of the affected receiver
B. Block the interfering signal with a filter on the amateur transmitter
C. Switch the transmitter from FM to SSB
D. Switch the transmitter to a narrow-band mode
  T7B05 HRLM (5-21)

## Slide 57: Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
D. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
  T7B06 HRLM (5-22)

## Slide 58: Which of the following actions should you take if a neighbor tells you that your station’s transmissions are interfering with their radio or TV reception?
A. Make sure that your station is functioning properly and that it does not cause interference to your own radio or television when it is tuned to the same channel
B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
D. Install a harmonic doubler on the output of your transmitter and tune it until the interference is eliminated
  T7B06 HRLM (5-22)

## Slide 59: Which of the following may be useful in correcting a radio frequency interference problem?
A. Snap-on ferrite chokes
B. Low-pass and high-pass filters
C. Band-reject and band-pass filters
D. All of these choices are correct
  T7B07 HRLM (5-19)

## Slide 60: Which of the following may be useful in correcting a radio frequency interference problem?
A. Snap-on ferrite chokes
B. Low-pass and high-pass filters
C. Band-reject and band-pass filters
D. All of these choices are correct
  T7B07 HRLM (5-19)

## Slide 61: What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor about the rules that prohibit the use of devices which cause interference
C. Check your station and make sure it meets the standards of good amateur practice
D. All of these choices are correct
  T7B08 HRLM (5-23)

## Slide 62: What should you do if something in a neighbor’s home is causing harmful interference to your amateur station?
A. Work with your neighbor to identify the offending device
B. Politely inform your neighbor about the rules that prohibit the use of devices which cause interference
C. Check your station and make sure it meets the standards of good amateur practice
D. All of these choices are correct
  T7B08 HRLM (5-23)

## Slide 63: What is a Part 15 device?
An unlicensed device that may emit low powered radio signals on frequencies used by a licensed service
A type of amateur radio that can legally be used in the citizen’s band
A device for long distance communications using special codes sanctioned by the International Amateur Radio Union
A type of test set used to determine whether a transmitter is in compliance with FCC regulation 91.15
  T7B09 HRLM (5-23)

## Slide 64: What is a Part 15 device?
An unlicensed device that may emit low powered radio signals on frequencies used by a licensed service
A type of amateur radio that can legally be used in the citizen’s band
A device for long distance communications using special codes sanctioned by the International Amateur Radio Union
A type of test set used to determine whether a transmitter is in compliance with FCC regulation 91.15
  T7B09 HRLM (5-23)

## Slide 65: What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible transmissions
D. Frequent blowing of power supply fuses
  T7B11 HRLM (5-24)

## Slide 66: What is a symptom of RF feedback in a transmitter or transceiver?
A. Excessive SWR at the antenna connection
B. The transmitter will not stay on the desired frequency
C. Reports of garbled, distorted, or unintelligible transmissions
D. Frequent blowing of power supply fuses
  T7B11 HRLM (5-24)

## Slide 67: What might be the first step to resolve cable TV interference from your ham radio transmission?
A. Add a low pass filter to the TV antenna input
B. Add a high pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV coaxial connectors are installed properly
  T7B12 HRLM (5-21)

## Slide 68: What might be the first step to resolve cable TV interference from your ham radio transmission?
A. Add a low pass filter to the TV antenna input
B. Add a high pass filter to the TV antenna input
C. Add a preamplifier to the TV antenna input
D. Be sure all TV coaxial connectors are installed properly
  T7B12 HRLM (5-21)

## Slide 69: What kind of hazard is presented by a conventional 12-volt storage battery?
A. It emits ozone which can be harmful to the atmosphere
B. Shock hazard due to high voltage
C. Explosive gas can collect if not properly vented
D. All of these choices are correct
  T0A09 HRLM (5-18)

## Slide 70: What kind of hazard is presented by a conventional 12-volt storage battery?
A. It emits ozone which can be harmful to the atmosphere
B. Shock hazard due to high voltage
C. Explosive gas can collect if not properly vented
D. All of these choices are correct
  T0A09 HRLM (5-18)

## Slide 71: What can happen if a lead-acid storage battery is charged or discharged too quickly?
A. The battery could overheat and give off flammable gas or explode
B. The voltage can become reversed
C. The memory effect will reduce the capacity of the battery
D. All of these choices are correct
  T0A10 HRLM (5-18)

## Slide 72: What can happen if a lead-acid storage battery is charged or discharged too quickly?
A. The battery could overheat and give off flammable gas or explode
B. The voltage can become reversed
C. The memory effect will reduce the capacity of the battery
D. All of these choices are correct
  T0A10 HRLM (5-18)