## Slide 1: Technician Licensing Class
Safety First!
Section 20
Valid July 1, 2014
Through
June 30, 2018
Notes: 1

## Slide 2: Safety First!
  Electrical shock can be a problem at your station.
      2. Connect all AC powered station equipment to a common safety ground
  1. Use three-wire cords and plugs for all AC powered equipment.

## Slide 3: Safety First!
3. Use a circuit protected by a ground-fault interrupter.
T0A06 All three are good ways to guard against electrical shock at your station
  Use three-wire cords and plugs for all AC powered equipment
  Connect all AC powered station equipment to a common safety ground
  Use a circuit protected by a ground-fault interrupter

## Slide 4: Safety First!
  T0A03 The green wire in a three-wire electrical AC plug is safety ground.
Hot (Live)
Neutral
Ground
AC Line Connections

## Slide 5: Safety First!
  T0A11 A fuse or circuit breaker in series with the AC "hot" conductor is safety equipment that should always be included in home-built equipment that is powered from 120V AC power circuits.
  T0A04 The purpose of a fuse in an electrical circuit is to interrupt power in case of overload.
Place the fuses as close to the battery as possible
Fuses
Slow-Blow fuse
Automobile fuse

## Slide 6: Safety First!
  T0A05 It is unwise to install a 20-ampere fuse in the place of a 5-ampere fuse because excessive current could cause a fire.
  T0A11 The kind of hazard that might exist in a power supply when it is turned off and disconnected is that you might receive an electric shock from stored charge in large capacitors.
Filter Capacitors
Charges stored from capacitors can HURT !

## Slide 7: Safety First!
  T7D12 When measuring high voltages with a voltmeter ensure that the voltmeter and leads are rated for use at the voltages to be measured.
  T0A02 Current flowing through the body cause a health hazard:
      By heating tissue;
      It disrupts the electrical functions of cells;
      It causes involuntary muscle contractions.
  T2C02 One way to recharge a 12-volt lead-acid station battery, if the commercial power is out, is to connect the battery in parallel with a car's battery and run the engine.

## Slide 8: Safety First!
  T0A10 If a lead-acid storage battery is charged or discharged too quickly it could overheat and give off flammable gas or explode
  T0A01 Shorting the terminals of a 12-volt storage battery can cause burns, fire, or an explosion.
  T0A09 A hazard is presented by a conventional 12-volt storage battery with its explosive gas that can collect if not properly vented.
  T0B09 You should avoid attaching an antenna to a utility pole as the antenna could contact high-voltage power wires.
        And it may be illegal to do

## Slide 9: Safety First!
  T0B04 Looking for and staying clear of any overhead electrical wires is an important safety precaution to observe when putting up an antenna tower.
    Overhead electrical wires carry more than 120 VAC
    Use common sense and think safety first
    Have help, don’t work alone
    Always look UP first
  T0B06 The minimum safe distance to allow from a power line when installing an antenna is to ensure that no part of the antenna can come closer than 10 feet to the power wires if antenna falls unexpectedly.
    This is a ‘minimum’ distance
    Keep away from all wires

## Slide 10: Safety First!
  T0B02 Putting on a climbing harness and safety glasses is a good precaution to observe before climbing an antenna tower.
Climbing Harness
Safety Glasses
And
Hard Hat

## Slide 11: Safety First!
  T0B03 It is never safe to climb a tower without a helper or observer.
  Never work on a tower without a helper
  T0B07 An important safety rule to remember when using a crank-up tower is that this type of tower must never be climbed unless it is in the fully retracted position.
      Think weight overload and never climb a cranked up tower
  T0B11 Grounding requirements for an amateur radio tower or antenna are established by local electrical codes
      Check local codes before putting up an antenna
  T0B08 Proper grounding method for a tower is to have separate eight-foot long ground rods for each tower leg, bonded to the tower and each other.

## Slide 12: Safety First!
  T4A08 A Flat strap conductor is best to use for RF grounding.
      Offers best surface area
        Bleed off static and minimize ground currents
        Straps usually are 3 inches wide
        Folding okay to snake down to a healthy ground rod
Copper Ground Strap provides good surface area ground

## Slide 13: Safety First!
  T0B12 A good practice when installing ground wires on a tower for lightning protection is to ensure that connections are short and direct.
  T0B10 Sharp bends must be avoided in grounding conductors used for lightning protection,.
  T0A07 Precautions should be taken when installing devices for lightning protection in a coaxial cable feedline by grounding all of the protectors to a common plate which is in turn connected to an external ground.
      Good for nearby lightning strikes
      Direct hits, forget it, kiss everything goodbye for good
  T0B01 Members of a tower work team should wear a hard hat and safety glasses at all times when any work is being done on the tower.
      On ground or up the tower; Wear hard hat and safety glasses

## Slide 14: Safety First!
  T0B05 The purpose of a gin pole is to lift tower sections or antennas.
Gin Pole

## Slide 15: Safety First!
  T0C04 Factors affecting the RF exposure of people near an amateur station antenna:
      Frequency and power level of the RF field
      Distance from the antenna to a person
      Radiation pattern of the antenna
Controlled
Uncontrolled

## Slide 16: Safety First!
  T0C05 Exposure limits vary with frequency because the human body absorbs more RF energy at some frequencies than at others.
Never stand in front of a microwave feedhorn antenna. On transmit, it radiates a concentrated beam of RF energy.
  T0C02 Of the following frequencies - 3.5 MHz, 50 MHz, 440 MHz, and 1296 MHz - a 50 MHz frequency has the lowest Maximum Permissible Exposure limit.
  T0C03 The maximum power level that an amateur radio station may use at VHF frequencies before an RF exposure evaluation is required is 50 watts PEP at the antenna.

## Slide 17: Safety First!
17
  T0C01 VHF and UHF radio signals are non-ionizing radiation.
        Quite different from X-ray, gamma ray, and ultra violet radiation
  T0C06 Acceptable methods to determine that your station complies with FCC RF exposure regulations:
        By calculation based on FCC OET Bulletin 65
        By calculation based on computer modeling
        By measurement of field strength using calibrated equipment
The safest place to mount the mobile antenna for minimum RF exposure is on the metal roof as shown.
  T0C08 An action amateur operators might take to prevent exposure to RF radiation in excess of FCC-supplied limits is to relocate antennas.

## Slide 18: Safety First!
  T0C09 To make sure your station stays in compliance with RF safety regulations, re-evaluate the station whenever an item of equipment is changed.
  T0C11 When referring to RF exposure, "duty cycle" is the percentage of time the transceiver is transmitting.
  T0C10 Duty cycle is one of the factors used to determine safe RF radiation exposure levels because it affects the average exposure of people to radiation.

## Slide 19: Safety First!
  T0C12 RF radiation differs from ionizing radition (radioactivity) because RF radiation does not have sufficient energy to cause genetic damage.
  T0C13 If the averaging time for exposure is 6 minutes, 2 times the power density is permitted if the signal is present for 3 minutes and absent for 3 minutes rather than being present for the entire 6 minutes. This is based on exposure limits for a given frequency from the FCC OET Bulletin 65 or computer modeling tools. Duty cycle is used as the time the signal is present.

## Slide 20: Safety First!
  T0C07 If a person accidentally touched your antenna while you were transmitting they might receive a painful RF burn.
Be sure to place your antennas where no one can touch them. All antennas, not just the mobile ones.

## Slide 21
Take Aways
Notes: 21

## Slide 22
Take Aways
All three are good ways to guard against electrical shock at your station
  Use three-wire cords and plugs for all AC powered equipment
  Connect all AC powered station equipment to a common safety ground
  Use a circuit protected by a ground-fault interrupter
Current flowing through the body can cause a health hazard all of the following:
  By heating tissue
  It disrupts the electrical functions of cells
  It causes involuntary muscle contractions
Safety ground is connected to the green wire in a three-wire electrical AC plug.
The purpose of a fuse in an electrical circuit is to interrupt power in case of overload.

## Slide 23
Take Aways
It is unwise to install a 20-ampere fuse in the place of a 5‑ampere fuse because excessive current could cause a fire.
ALL of these are a good way to guard against electrical shock at your station:
  Use three-wire cords and plugs for all AC powered equipment
  Connect all AC powered station equipment to a common safety ground
  Use a circuit protected by a ground-fault interrupter
Precautions that should be taken when installing devices for lightning protection in a coaxial cable feedline include grounding all of the protectors to a common plate which is in turn connected to an external ground.

## Slide 24
Take Aways
One way to recharge a 12-volt lead-acid station battery, if the commercial power is out, is to connect the battery in parallel with a car's battery and run the engine.
If a conventional 12-volt storage battery is not properly vented, explosive gas can collect and present a hazard.
If a lead-acid storage battery is charged or discharged too quickly, the battery could overheat and give off flammable gas or explode.
  Shorting the terminals of a 12-volt storage battery can cause burns, fire, or an explosion.
A good practice when installing ground wires on a tower for lightning protection is to ensure that connections are short and direct.

## Slide 25
Take Aways
A fuse or circuit breaker in series with the AC "hot" conductor should always be included in home-built equipment that is powered from 120V AC power circuits
The kind of hazard that might exist in a power supply when it is turned off and disconnected is that you might receive an electric shock from stored charge in large capacitors
Members of a tower work team should wear a hard hat and safety glasses at all times when any work is being done on the tower.
A good precaution to observe before climbing an antenna tower is put on a climbing harness and safety glasses.

## Slide 26
Take Aways
It is never safe to climb a tower without a helper or observer.
An important safety precaution to observe when putting up an antenna tower is look for and stay clear of any overhead electrical wires.
The purpose of a gin pole is to lift tower sections or antennas.
The minimum safe distance from a power line to allow when installing an antenna is so that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires. (Look Up)
An important safety rule to remember when using a crank-up tower is this type of tower must never be climbed unless it is in the fully retracted position.

## Slide 27
Take Aways
A Flat strap type of conductor is best to use for RF grounding.
A separate eight-foot long ground rods for each tower leg, bonded to the tower and each other, is considered to be a proper grounding method for a tower.
You should avoid attaching an antenna to a utility pole because the antenna could contact high-voltage power wires.
Avoid sharp bends when routing ground conductors used for lightning protection.
  When measuring high voltages with a voltmeter ensure that the voltmeter and leads are rated for use at the voltages to be measured.

## Slide 28
Take Aways
Local electrical codes establish grounding requirements for an amateur radio tower or antenna
VHF and UHF radio signals are non-ionizing radiation.
50 MHz has the lowest Maximum Permissible Exposure limit.
ALL of these factors affect the RF exposure of people near an amateur station antenna:
  Frequency and power level of the RF field
  Distance from the antenna to a person
  Radiation pattern of the antenna
Notes: Local electrical codes establish grounding requirements for an amateur radio tower or antenna
VHF and UHF radio signals are non-ionizing radiation.
50 MHz has the lowest Maximum Permissible Exposure limit.
ALL of these factors affect the RF exposure of people near an amateur station antenna:
  Frequency and power level of the RF field
  Distance from the antenna to a person
  Radiation pattern of the antenna
The maximum power level that an amateur radio station may use at VHF frequencies before an RF exposure evaluation is required is 50 watts PEP at the antenna.

## Slide 29
Take Aways
The maximum power level that an amateur radio station may use at VHF frequencies before an RF exposure evaluation is required is 50 watts PEP at the antenna.
Exposure limits vary with frequency because the human body absorbs more RF energy at some frequencies than at others.
ALL of these are acceptable methods to determine that your station complies with FCC RF exposure regulations:
  By calculation based on FCC OET Bulletin 65
  By calculation based on computer modeling
  By measurement of field strength using calibrated equipment

## Slide 30
Take Aways
If a person accidentally touched your antenna while you were transmitting they might receive a painful RF burn.
An action amateur operators might take to prevent exposure to RF radiation in excess of FCC-supplied limits includes relocating the antenna.
You can make sure your station stays in compliance with RF safety regulations by re-evaluating the station whenever an item of equipment is changed.
Duty cycle is one of the factors used to determine safe RF radiation exposure levels because it affects the average exposure of people to radiation.

## Slide 31
Take Aways
When referring to RF exposure, duty cycle is the percentage of time that a transceiver is transmitting
RF radiation differs from ionizing radition (radioactivity) because RF radiation does not have sufficient energy to cause genetic damage.
If the averaging time for exposure is 6 minutes, 2 times the power density is permitted if the signal is present for 3 minutes and absent for 3 minutes rather than being present for the entire 6 minutes. This is based on exposure limits for a given frequency. Duty cycle is used as the time the signal is present.

## Slide 32: Element 2 Technician Class Question Pool
Valid July 1, 2014
Through
June 30, 2018
Safety First!
Element 2 Technician Class Question Pool

## Slide 33: T0A06 What is a good way to guard against electrical shock at your station?
  Use three-wire cords and plugs for all AC powered equipment
  Connect all AC powered station equipment to a common safety ground
  Use a circuit protected by a ground-fault interrupter
  All of these choices are correct

## Slide 34: T0A03 What is connected to the green wire in a three- wire electrical AC plug?
  Neutral
  Hot
  Safety ground
  The white wire

## Slide 35: T0A08 What safety equipment should always be included in home-built equipment that is powered from 120V AC power circuits?
  A fuse or circuit breaker in series with the AC hot conductor
  An AC voltmeter across the incoming power source
  An inductor in series with the AC power source
  A capacitor across the AC power source

## Slide 36: T0A04 What is the purpose of a fuse in an electrical circuit?
  To prevent power supply ripple from damaging a circuit
  To interrupt power in case of overload
  To limit current to prevent shocks
  All of these choices are correct

## Slide 37: T0A05 Why is it unwise to install a 20-ampere fusein the place of a 5-ampere fuse?
  The larger fuse would be likely to blow because it is rated for higher current
  The power supply ripple would greatly increase
  Excessive current could cause a fire
  All of these choices are correct

## Slide 38: T0A11 What kind of hazard might exist in a power supply when it is turned off and disconnected?
  Static electricity could damage the grounding system
  Circulating currents inside the transformer might cause damage
  The fuse might blow if you remove the cover
  You might receive an electric shock from stored charge in large capacitors

## Slide 39: T7D12 Which of the following precautions should be taken when measuring high voltage with a voltmeter?
  Ensure that the voltmeter has very low impedance
  Ensure that the voltmeter and leads are rated for use at the voltage to be measured
  Ensure that the circuit is grounded through the voltmeter
  Ensure that the voltmeter is set to the correct frequency

## Slide 40: T0A02 How does current flowing through the body cause a health hazard?
  By heating tissue
  It disrupts the electrical functions of cells
  It causes involuntary muscle contractions
  All of these choices are correct

## Slide 41: T2C02 What is one way to recharge a 12-volt lead-acid Station battery if the commercial power is out?
  Cool the battery in ice for several hours
  Add acid to the battery
  Connect the battery in parallel with a vehicle’s battery and run the engine
  All of these choices are correct

## Slide 42: T0A10 What can happen if a lead-acid storage battery is charged or discharged too quickly?
  The battery could overheat and give off flammable gas or explode
  The voltage can become reversed
  The memory effect will reduce the capacity of the battery
  All of these choices are correct

## Slide 43: T0A01 Which of the following is a safety hazard of a 12 voltage storage battery?
  Touching both terminals with the hands can cause electrical shock
  Shorting the terminals can cause burns, fire, or an explosion
  RF emissions from the battery
  All of these choices are correct

## Slide 44: T0A09 What kind of hazard is presented by a conventional 12-volt storage battery?
  It emits ozone which can be harmful to the atmosphere
  Shock hazard due to high voltage
  Explosive gas can collect if not properly vented
  All of these choices are correct

## Slide 45: T0B04 Which of the following is an important safety precaution to observe when putting up an antenna tower?
  Wear a ground strap connected to your wrist at all times
  Insulate the base of the tower to avoid lightning strikes
  Look for and stay clear of any overhead electrical wires
  All of these choices are correct

## Slide 46: T0B06 What is the minimum safe distance from a power line to allow when installing an antenna?
  Half the width of your property
  The height of the power line above ground
  1/2 wavelength at the operating frequency
  So that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires

## Slide 47: T0B09 Why should you avoid attaching an antenna to a utility pole?
  The antenna will not work properly because of induced voltages
  The utility company will charge you an extra monthly fee
  The antenna could contact high-voltage power wires
  All of these choices are correct

## Slide 48: T0B02 What is a good precaution to observe before climbing an antenna tower?
  Make sure that you wear a grounded wrist strap
  Remove all tower grounding connections
  Put on a climbing harness and safety glasses
  All of the these choices are correct

## Slide 49: T0B03 Under what circumstances is it safe to climb a tower without a helper or observer?
  When no electrical work is being performed
  When no mechanical work is being performed
  When the work being done is not more than 20 feet above the ground
  Never

## Slide 50: T0B01 When should members of a tower work team wear a hard hat and safety glasses?
  At all times except when climbing the tower
  At all times except when belted firmly to the tower
  At all times when any work is being done on the tower
  Only when the tower exceeds 30 feet in height

## Slide 51: T0B05 What is the purpose of a gin pole?
  To temporarily replace guy wires
  To be used in place of a safety harness
  To lift tower sections or antennas
  To provide a temporary ground

## Slide 52: T0B07 Which of the following is an important safety rule to remember when using a crank-up tower?
  This type of tower must never be painted
  This type of tower must never be grounded
  This type of tower must never be climbed unless it is in the fully retracted position
  All of these choices are correct

## Slide 53: T0B11 Which of the following establishes grounding requirements for an amateur radio tower or antenna?
  FCC Part 97 Rules
  Local electrical codes
  FAA tower lighting regulations
  Underwriters Laboratories' recommended practices

## Slide 54: T0B08 What is considered to be a proper grounding method for a tower?
  A single four-foot ground rod, driven into the ground no more than 12 inches from the base
  A ferrite-core RF choke connected between the tower and ground
  Separate eight-foot long ground rods for each tower leg, bonded to the tower and each other
  A connection between the tower base and a cold water pipe

## Slide 55: T4A08 Which type of conductor is best to use for RF grounding?
  Round stranded wire
  Round copper-clad steel wire
  Twisted-pair cable
  Flat strap

## Slide 56: T0B12 Which of the following is good practice when installing ground wires on a tower for lightning protection?
  Put a loop in the ground connection to prevent water damage to the ground system
  Make sure that all bends in the ground wires are clean, right angle bends
  Ensure that connections are short and direct
  All of these choices are correct

## Slide 57: T0B10 Which of the following is true concerning grounding conductors used for lightning protection?
  Only non-insulated wire must be used
  Wires must be carefully routed with precise right-angle bends
  Sharp bends must be avoided
  Common grounds must be avoided

## Slide 58: T0A07 Which of these precautions should be taken when installing devices for lightning protection in a coaxial cable feedline?
  Include a parallel bypass switch for each protector so that it can be switched out of the circuit when running high power
  Include a series switch in the ground line of each protector to prevent RF overload from inadvertently damaging the protector
  Keep the ground wires from each protector separate and connected to station ground
  Ground all of the protectors to a common plate which is in turn connected to an external ground

## Slide 59: T0C04 What factors affect the RF exposure of people near an amateur station antenna?
  Frequency and power level of the RF field
  Distance from the antenna to a person
  Radiation pattern of the antenna
  All of these choices are correct

## Slide 60: T0C05 Why do exposure limits vary with frequency?
  Lower frequency RF fields have more energy than higher frequency fields
  Lower frequency RF fields do not penetrate the human body
  Higher frequency RF fields are transient in nature
  The human body absorbs more RF energy at some frequencies than at others

## Slide 61: T0C02 Which of the following frequencies has the lowest Maximum Permissible Exposure limit?
  3.5 MHz
  50 MHz
  440 MHz
  1296 MHz

## Slide 62: T0C03 What is the maximum power level that an amateur radio station may use at VHF frequencies before an RF exposure evaluation is required?
  1500 watts PEP transmitter output
  1 watt forward power
  50 watts PEP at the antenna
  50 watts PEP reflected power

## Slide 63: T0C01 What type of radiation are VHF and UHF radio signals?
  Gamma radiation
  Ionizing radiation
  Alpha radiation
  Non-ionizing radiation

## Slide 64: T0C06 Which of the following is an acceptable method to determine that your station complies with FCC RF exposure regulations?
  By calculations based FCC OET Bulletin 65
  By calculation based on computer modeling
  By measurement of field strength using calibrated equipment
  All of these choices are correct

## Slide 65: T0C08 Which of the following actions might amateur operators take to prevent exposure to RF radiation in excess of FCC-supplied limits?
  Relocate antennas
  Relocate the transmitter
  Increase the duty cycle
  All of these choices are correct

## Slide 66: T0C09 How can you make sure your station stays in compliance with RF safety regulations?
  By informing the FCC of any changes made in your station
  By re-evaluating the station whenever an item of equipment is changed
  By making sure your antennas have low SWR
  All of these choices are correct

## Slide 67: T0C11 What is the definition of duty cycle during the averaging time for RF exposure?
  The difference between lowest power output and highest output power of a transmitter
  The difference between the PEP and average power output power of a transmitter
  The percentage of time that a transmitter transmits
  The percentage of time that a transmitter is not transmitting

## Slide 68: T0C12 How does RF radiation differ from ionizing radiation (radioactivity)?
  RF radiation does not have sufficient energy to cause genetic damage
  RF radiation can only be detected with an RF dosimeter
  RF radiation is limited in range to a few feet
  RF radiation is perfectly safe

## Slide 69: T0C13 If the averaging time for exposure is 6 minutes, how much power density is permitted if the signal is present for 3 minutes and absent for 3 minutes rather than being present for the entire 6 minutes?
  3 times as much
  1/2 as much
  2 times as much
  There is no adjustment allowed for shorter exposure times

## Slide 70: T0C10 Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
  It affects the average exposure of people to radiation
  It affects the peak exposure of people to radiation
  It takes into account the antenna feedline loss
  It takes into account the thermal effects of the final amplifier

## Slide 71: T0C07 What could happen if a person accidentally touched your antenna while you were transmitting?
  Touching the antenna could cause television interference
  They might receive a painful RF burn
  They might develop radiation poisoning
  All of these choices are correct