LIVING CHRISTMAS TREE LIGHTING, 2005

CABLES TO AND BEHIND TREE, BY DIMMER NUMBER                         |    Current

Dim-(Ch)-Cable Color-Cable # - Tape Color    Assign               Notes          Strings | 1999 - Now

1        9      Green          040 BLK-YLW-BLK    MIXED row 1 & 2 (Top of Tree)  (1 ea)     2.9  3.0

2      10      Orange          01 BLK-BRN            Mixed row 3                                (2)     2.2     2.2

3      11      Orange        011 BLK-BRN-BRN    Mixed row 4                                (2)     2.5     2.6

4      12      Orange          03 BLK-OR              Mixed row 5                                (3)     2.3     3.8

5      13      Orange        014 BLK-BRN-YLW    Mixed row 6                                (4)     5.4     5.2

6      14      Black           021 BLK-RED-BRN    Mixed row 7                                (4)     6.3     4.9

7      15      Black           116 BRN-BRN-BLU    Mixed row 8       (Split)                (5)      6.3    6.4    (split)

8      16      Orange          04 BLK-YLW            Mixed row 9       (Split)                (8)      9.3   10.6   (split)

9      34      Orange        031 BLK-OR-BRN      BLUE row 1 & 2 (Top of Tree)     (1 ea)  1.8    2.0

10     35      Orange          06 BLK-BLUE           Blue row 3                                  (2)      1.8     2.6

11     36      Green          046 BLK-YLW-BLUE  Blue row 4                                  (4)      3.1    4.1

12     37      Green          048 BLK-YLW-GRAY Blue row 5                                   (3)      3.0    3.4

13     38      Orange          08 BLK-GRAY          Blue row 6                                  (4)      3.1     4.0

14     39      Black           103 BRN-BLK-OR      Blue row 7                                   (5)      2.9    5.3

15     40      Black           115 BRN-BRN-GRN   Blue row 8         (Split)                 (6)      4.4    6.0   (split)

16     41      Black                  BLUE                  Blue row 9        (Split)                 (12)    10.2   13.3   (split)

17     18      Green          041 BLK-YLW-BRN    RED row 1 & 2  (Top of Tree)       (1 ea)  2.5   2.6

18     19      Orange         028 BLK-RED-GRAY Red row 3                                    (2)      2.1    2.3

19     20      Orange        012 BLK-BRN-RED    Red row 4                                     (2)      2.8    2.1

20     21      Orange          02 BLK-RED            Red row 5                                     (3)     2.9     4.0

21     22      Orange        013 BLK-BRN-OR      Red row 6                                     (4)      3.9    5.6

22     23      Black           102 BRN-BLK-RED    Red row 7                                     (4)      3.9    5.1

23     24      Black           109 BRN-BLK-WH     Red row 8                                     (5)      3.8     6.6   (split)

24     25      Black                   RED                  Red row 9                                     (8)       6.6     9.6   (split)

25     43      Orange        030 BLK-OR-BLK       GREEN row 1 & 2 (Top of Tree)  (1 ea)    2.8    2.8

26     44      Orange         05 BLK-GREEN        Green row 3                                  (2)      2.1    2.2

27     45      Orange       010 BLK-BRN-BLK      Green row 4                                  (2)      2.7    2.9

28     46      Green        044 BLK-YLW-YLW     Green row 5                                  (3)      2.6    3.8

29     47      Orange       015 BLK-BRN-GRN     Green row 6                                  (4)      3.6    5,2

30     48      Black          119 BRN-BRN-WH     Green row 7                                  (4)      3.9     5.4

31     49      Black          106 BRN-BLK-BLUE   Green row 8                                  (5)       5.1    6.1   (split)

32     50      Black                 GREEN               Green row 9                                  (9)       7.6    9.0   (split)

33     26      Green         043 BLK-YLW-OR      GARLAND     (Needs twenty 15’ strands)  4.3    4.8

34     28      Orange       032 BLK-OR-RED       STROBE LIGHTS & Ballast               Ca. 1.6    1.7

35     27      Orange         09 BLK-WHITE         TUBE LIGHTS                                         2.6    2.4

36     32      Orange       029 BLK-RED-GRN     CROSS                                                   1.7     1.8

37     30      Green         042 BLK-YLW-RED     STAR  - LIGHT AND MOTOR                 3.0     2,6

38               Green        045  BLK-YLW-GN      DRAMA -   Fire Pots     (cable colors reversed)

39              Orange       021  BLK-RED-BRN     DRAMA -  Stage Left Lightning

40              Orange       026  BLK-RED-BLU     DRAMA -   Stage Right Lightning

41              Orange       022  BLK-RED-RED    DRAMA -   Stage Right Top Scrim

42              Orange       025  BLK-RED-WH      DRAMA -   Stage Left Top Scrim

43              Yellow        102  BRN-BRN-BRN    DRAMA -   Cross scrim

44              Yellow        112  BRN-BRN-RED    DRAMA -   Small Star

45              Orange       020  BLK-RED-BLK     DRAMA -   Stage Left Lightning

46 	     Orange       023  BLK-RED-OR       DRAMA -   Tomb Light & Motor

47              Orange       024  BLK-RED-YLW    DRAMA -   Stable lights

48              Orange       033  BLK-OR-OR         DRAMA -   Open

Hot Pocket  Yellow      022   BRN-BRN-OR    Extra Work line - “Hot Pocket” -  (Night light, misc)

Mirror Ball Orange            BRN-RED-OR      Work lights - (Plugged into WALL outlet - wall breaker 29)

1999 TOTAL          165 A

(All levels, 1 thru 8, completely rebuilt [off of tree], 11/99)

CURRENT THRU PRIMARY WIRES:

RED - 54 A.  BLUE - 42 A.  BLACK - 41 A.  WHITE (Neut) - 31 A.  Green (Ground) - 0.    Total, 168 A (12/99)

NOTE - all information on these papers cover ONLY the TREE PROPER.  Hookup and programming information for the Drama lights, overhead lights, etc, must be obtained from Ron Dowell.

COLOR CODE

0 - Black           5 - Green                                                        Color codes read from the end

1 - Brown         6 - Blue                                                           in toward the center of each

2 - Red             7 - Violet (not available)                                 cable from each end.

3 - Orange        8 - Gray

4 - Yellow         9 - White

___________________

|                                     |

| O     O               O       |               SOCKET, LOOKING INTO IT.

|__________________  |

|        |                 |

N      G              H

e        n              o

u       d               t

.   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .   .

APPROX. NR NEEDED                *  (Star)

1 string of each color-->                _1_      [4’]                                             [Levels 1 & 2

1  string of each color-->              _|_2_|__    [5.5’]                                        hooked together]

2 strings of each -->                _|____3____|__  [11.5]

2 strings of each -->          _|_______4_______|__  (4 blue strings) [16’ ?]      [Garland now has plugs at one END]

3 strings of each --->    _|__________5__________|__     [22’]                       [Its plugs go to the Stage Left side]

4 strings of each -> _|_____________6_____________|__ [26’]                      [as do the plugs for the colored lights].

4  strings-->      _|________________7________________|__ (5 blue strings)  [32’]

5 strings ea.-_|___________________8___________________|__  (6 blue strings)  [36’]  Row split into 2 parts.

|         Garland in 2 sections for this level now.               |

|                                          9                                          |

|                         2 GROUPS of 4 STRINGS                  |

|                      OF EACH COLOR  (= 8 each)              |

| EXCEPT BLUE, WHICH GETS 3 GROUPS OF  4  |

|_________(total,  approx. 36 strings on bottom)_______|

Approximately 30 strings of each color are needed, except blue with 38.   25 bulbs per string.  Ca. 3200 C7 bulbs needed!  (Individual strings rated at 7 amps [use 7 A fuses]; light-duty extension cords rated at 13 amps).

“Levels”, as seen from the front.  (They do NOT correspond with the level number painted on the steps).

------------------------------------------------------------------------------------------------------------------------------------------

FRS CHANNELS AND FREQUENCIES	|	DIP SWITCH SETTINGS, R S Units    		     |  SCANNER

1     462.5625		(61)		|	CHANNEL	SET TO ON                 |  CH   Freq

2     462.5875				|	   1		1, 2, 3, 4                        |   91    462.5625 (1)

3     462.6125				|	   2		1                                    |   92    467.7125 (14)

4     462.6375				|	   3		2                                    |   93    464.900

5     462.6625		(65)		|	   4		1, 2                                |   94    469.900

6     462.6875				|	   5		3                                    |   95    146.430

7     462.7125				|	   6		1, 3                                |   96    154.430

8     467.5625				|	   7		2, 3                                |   97    155.160

9     467.5875				|	   8		1, 2, 3                            |   98    467.5875 (8)

10    467.6125		(70)		|	   9		4             (1999, in use)  |  99    154.280

11    467.6375		(91)		|	 10		1, 4         (1999, in use)  | 100    ----

12    467.6625				|	 11		2, 4                                 |

13    467.6875				|	 12		1, 2, 4		           ICOM   IC-T8A

14    467.7125		(94)		|	 13		3, 4		          50   469.900 SVBC 2

|	 14		1, 3, 4	                            51  161.760  Link #2

Last revision - 2004/11/24	light01.doc					 	          52  161.735 Link #1

53  467.7125 FRS

54  467.6375 FRS

55 462.5635 FRS