## Slide 1: Coax Connector 3 Piece Connector Assembly Gerry Crenshaw WD4BIS www.qsl.net/wd4bis

## Slide 2: Three Piece Coax Connectors
Advancements in materials and tooling now make the 3 piece connector the preferred connector for many types of coax.
Regardless of the connector type, they all work the same.
Results are consistent and repeatable time after time.
NASA has a requirement of “crimped wherever possible” due to launch “G” forces and out gassing.

## Slide 3: The Connector
Regardless of the connector type, the assembly typically consists of three parts
The Center Pin
The Crimping Ferrule
Connector Body

## Slide 4: Connector Types
Connectors types available include:
BNC
TNC
Type N
SMA
UHF/PL259
Mini UHF
FME
Vendor proprietary (Such as Erricson, Hirose)

## Slide 5: Coax Types
The connectors are cable specific. This has to do with the dimensions of the cable, center conductor and dialectic.
They are available for coax types:
RG6
RG8X
RG58A (solid center) RG58AU (stranded center)
RG59
RG174
Type 734A/735
LMR

## Slide 6: Tooling
You will need
Crimper
Coax Strip tool or…..
Knife and ruler
Scissors to trim stray strands

## Slide 7: Tooling, Coax Strip tool
A coax strip tool listed as 2 Level, makes 2 cuts.
A coax strip tool listed as 3 Level, makes 3 cuts.
The tools are usually specified for per coax type.
  RG58, RG59, RG8, RG213, etc.
The depth of the cuts may have to be adjusted by the included hex wrench, or a fine screwdriver.
The more expensive tools have various “V” groves for different coax types and depths and replaceable blades.

## Slide 8: Cable Preparation
Slide the crimping ferrule on coax

## Slide 9: Cable Preparation
Make three cuts to expose the individual elements.

## Slide 10: Assembly
Trim center conductor and slide on center pin.
Crimp

## Slide 11: Assembly
Insert pin into Connector Body. Push
Listen or feel for the click that says its seated.

## Slide 12: Assembly
Slide Crimping ferrule down coax until it bumps the body.
Crimp

## Slide 13: Workshop
Time permitting, we will connectorize some coax.